## Slide 1
AUTOMOBILE ENGLISH
汽车专业英语
Shanxi Institute of Mechanical & Electrical Engineering
山西机电职业技术学院
Lesson 8 Clutches
离合器
Unit 3 Power train

## Slide 2
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
clutch | apply
spin | locate
disconnect | rub
engage | press
slippage | clutch pedal
flywheel | slide
clutch disc | release
pressure plate | rotate
clutch cover | mechanism
release bearing | 
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 3
Decide whether the following statements are true or false.
( ) 1. Clutches are needed in a car because the engine spins all the time, and so
does the wheels.
( ) 2. The clutch allows us to smoothly engage a spinning engine to a non-
spinning transmission by controlling the slippage between them.
( ) 3. When the driver presses the clutch pedal, the clutch disc slides forward.
( ) 4. When the driver releases the clutch pedal, the clutch disc slides forward.
( ) 5. Automatic transmission cars don’t have clutches.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
1
F
T
F
T
F
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 4
Fill in the blanks with the missing words.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Components of a clutch | Generally speaking, there are 1____________ important components in a clutch, including the 2_____________, the clutch disc, the 3______________ plate, the 4____________ cover , and the 5_____________ bearing.
Clutch cover | The clutch cover is 6_________ into the flywheel on the 7_______________ side of the clutch.
2
five
fly wheel
pressure
clutch
release
bolted
engine
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 5
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Clutch disc | The clutch disc is 8____________ between the 9_____________ and the pressure plate. Both sides of the clutch disc have 10__________________ material which the 11______________ plate and the 12_______________ can rub against when fully engaged. It is why the clutch disc is also called the 13______________ disc.
Clutch | In a few words, the clutch is a 14___________________ to connect or 15_____________ the flow of 16_________ to the transmission with the 17_____________ on.
located
flywheel
friction
pressure
fly wheel
friction
mechanism
disconnect
power
engine
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 6
Cars need a clutch because the engine spins all the time, but the car’s wheels do not. In order for a car to stop without killing the engine, the wheels need to be disconnected from the engine somehow. The clutch allows a driver to smoothly engage a spinning engine to a non-spinning transmission by controlling the slippage between them.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
There are five important components in a clutch, including the flywheel, the clutch disc, the pressure plate, the clutch cover, and the release bearing.
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 7
The clutch cover is bolted into the flywheel on the engine side of the clutch. The pressure plate applies pressure on the clutch disc. The clutch disc is located between the flywheel and the pressure plate. Both sides of the clutch disc have friction material which the pressure plate and the flywheel can rub against when fully engaged. It is for this reason that the clutch disc is also called the friction disc.
When the driver presses the clutch pedal, the clutch disc slides back. This is the disengaged condition in which the clutch disc doesn’t touch the flywheel. At that time, the engine is still running but no power is transferred to the wheels.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 8
When the driver releases the clutch pedal, the clutch disc slides forward. This is the engaged condition in which the clutch disc has touched the flywheel. At that time, both of them rotate at the same speed, the power is sent to the wheels.
In short, the clutch is a mechanism to connect or disconnect the flow of power to the transmission without turning the engine off. It operates through friction which comes from contact between a friction disc and a flywheel. That is the reason why the clutch is called a friction mechanism.
Automatic transmission cars also have clutches, although differeent from those in manual transmission cars.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 9
汽车需要离合器，因为发动机一直在旋转，但汽车的车轮不会。为了让汽车在不熄火的情况下停下来，车轮需要以某种方式与发动机断开。通过控制它们之间的滑移，离合器可以让旋转的发动机平稳地接合到不旋转的变速器上。
离合器有五个重要部件，包括飞轮、离合器盘、压盘、离合器盖和分离轴承。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 10
离合器盖用螺栓固定在离合器靠近发动机一侧的飞轮上。压盘对离合器盘施加压力。离合器盘位于飞轮和压盘之间。离合器盘的两侧有摩擦材料，压盘和飞轮在同离合器盘完全啮合时可以产生摩擦。也正是由于这个原因，离合器盘被称为摩擦盘。
当驾驶员踩下离合器踏板时，离合器盘向后滑动。这是脱离状态，离合器盘不接触飞轮。这时发动机仍在运转，但没有动力传递到车轮上。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 11
当驾驶员松开离合器踏板时，离合器盘向前滑动。这是离合器盘接触飞轮的啮合状态。这时，两者以相同的速度旋转，动力被传送到车轮上。
简而言之，离合器是一种在不关闭发动机的情况下，连接或断开变速器的动力流的机制。它通过摩擦盘和飞轮之间产生摩擦来运行。这就是为什么离合器被称为摩擦机构的原因。
自动变速器汽车也有离合器，虽然与手动变速器汽车的离合器不同。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 12
1 _________________
2 _________________
3 _________________
4 _________________
5 _________________
Name the parts of the clutch.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
3
release bearing
clutch cover
pressure plate
flywheel
clutch disc
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 13
Complete the sentences by using the words in Task 3. Change the form when necessary.
1. The _______________ is on the engine side of the clutch.
2. The _______________ fits between the flywheel and the pressure plate.
3. The clutch disc slides forward when the clutch pedal is ______________ by the
driver.
4. The _________________ exerts pressure on the pressure plate.
5. The ___________________ is permanently lubricated and requires no cleaning or
lubrication.
6. When your foot is off the pedal, the _________________ will be pushed against
the clutch disc, which in turn presses against the flywheel.
7. The ______________ is bolted into the flywheel.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
4
flywheel
clutch disc
released
diaphragm spring
bearing
pressure plate
clutch disc
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 14
Complete the following table and introduce to each other how the car clutch works. The following diagram can be useful.
5
How the car clutch works
clutch pedal | pressure plate | clutch disc | clutch disc & flywheel | engine & transmission (gearbox)
 | applies no pressure |  | no touch | 
released |  | slides forward |  | engaged
pressed
slides
back
disengaged
applies pressure
touch
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 15
1. I often hear some noise when pressing the clutch.
2. Is it serious?
3. May I help you?
4. Thank you.
5. Oh, yes.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Choose a suitable expression for each blank to complete the following dialogue.
Situation: A is a mechanic in a 4S store, B is a customer.
6
A: Good morning, Miss Green. __________________
B: Yes. __________________________________________
A: Is the noise piercing?
B: ________________________
A: I see. I think your car has a bad or worn clutch.
B: ___________________________
A: No, it is a common clutch problem.
B: Oh, it’s so good. ________________
May I help you?
I often hear some noise when pressing the clutch.
Oh, yes.
Is it serious?
Thank you.
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 16
Complete the word search.
7
c | o | m | p | o | n | e | n | t
l | i | k | e | n | i | n | e | i
u | s | e | d | l | k | g | x | m
t | a | p | a | y | e | a | t | e
c | u | t | l | a | r | g | e | e
h | s | l | i | p | e | e | l | t
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 17
Thank you!