## Slide 1
AUTOMOBILE ENGLISH
汽车专业英语
Shanxi Institute of Mechanical & Electrical Engineering
山西机电职业技术学院
Lesson 10 Automatic transmission
自动变速器
Unit 3 Power train

## Slide 2
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
motion | planetary gear | loosen
accelerator | gear ratio | combination
brake | sun gear | individual
in harmony | planet gear | hydraulic system
torque converter | carrier | hydraulic regulating valve
coupling | internal/ring gear | shift valve
power train | brake band | servo
impeller | actuate | plunger
turbine | tighten | element
stator | stationary | channel
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 3
Decide whether the following statements are true or false.
( ) 1. For automatic transmission cars, the driver can control the car only through the
accelerator.
( ) 2. The torque converter is similar to the clutch in a manual transmission.
( ) 3. The impeller of the torque converter is connected to the engine’s crankshaft.
( ) 4. An automatic transmission uses a planetary gear to change the gear ratios.
( ) 5. The hydraulic pressure coming from the pump is used to operate the shift
valves.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
1
T
F
T
F
F
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 4
Fill in the blanks with the missing words.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Automatic transmission | An automatic transmission is used to change the gears 1____________. There is no 2___________ pedal in AT cars. The driver controls the car through the 3______________ and the brake.
Torque converter | The torque converter is the coupling between the engine and the 4___________ which transmits power to the drive wheels. It has three parts: the 5____________ , the turbine and the 6__________ ( or guide wheel ).
2
automatically
clutch
accelerator
power train
impeller
stator
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 5
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Gear system | The planetary gear system has three parts --- the 7______ gear, the planet gears and the 8___________, and the internal gear or the 9____________.
Brake bands and clutches | The brake bands and the clutches actuate the 10______________ of gears in the planetary gear set. They 11_______________ to hold a particular gear stationary or 12______________ to enable that gear to spin.
Hydraulic system | The hydraulic system consists of four parts, they are the pump, the hydraulic regulating 13________, the shift valves and the 14___________.
sun
changing
carrier
ring gear
tighten
loosen
valves
servos
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 6
An automatic transmission can automatically change the gears while the car is in motion. In cars with automatic transmission, there is no clutch pedal. The driver controls the car through the accelerator and the brake. But getting that to happen involves many components that must work in harmony. Here are the key elements:
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 7
1. Torque converter
The torque converter is the coupling between the engine and the power train. It transmits power to the drive wheels, as the clutch in a manual transmission does. There are three parts in it. They are the impeller connected to the engine’s crankshaft, the turbine connected to the output shaft, and the stator ( or guide wheel ) between the two.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 8
2. Gear system
An automatic transmission uses a set of planetary gears to change the gear ratios. The planetary gear system has three parts --- the sun gear, the planet gears and the carrier, and the internal gear (also called ring gear).
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 9
3. Brake bands and clutches
The brake bands and the clutches actuate the changing of gears in the planetary gear set. They tighten to hold a particular gear stationary or loosen to enable that gear to spin. And it is the combination of stationary and spinning gears in the gear set that produces each individual gear ratio.
4. Hydraulic system
The hydraulic system consists of the pump, various hydraulic regulating valves, the shift valves and the servos ( the plungers and the cylinders used to operate shifting elements such as the brake bands and the clutches ). The hydraulic pressure coming from the pump is used to operate the servos. The fluid is channeled to the various servos through the shift valves.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 10
自动变速器能在汽车行驶时自动换挡。在自动变速器的汽车中，没有离合踏板。驾驶员通过油门和刹车来控制汽车。但要实现这一目标，需要许多部件协同工作。以下是关键部分:
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 11
1.变矩器
变矩器是发动机和传动系统之间的耦合。它将动力传递给驱动轮，就像手动变速器中的离合器一样。它由三个部分组成：与发动机曲轴相连的泵轮，与输出轴相连的涡轮，以及两者之间的定子(或导轮)。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 12
2.齿轮系统
自动变速器使用一组行星齿轮来改变齿轮传动比。行星齿轮系统有三个部分——太阳齿轮，行星齿轮和载体，内部齿轮或环形齿轮。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 13
3.制动带和离合器
制动带和离合器驱动行星齿轮组的齿轮变换。制动带和离合器收紧以固定某个特定的齿轮，松开以使该齿轮旋转。每个齿轮比都是由齿轮组中固定齿轮和旋转齿轮的不同组合产生的。
4.液压系统
液压系统由油泵、各种液压调节阀、换档阀和伺服器(用于操作制动带和离合器等换档元件的柱塞和油缸)组成。用于操作伺服系统的液压来自于油泵。这种液压油通过换档阀输送到各个伺服系统。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 14
1.P _________________
2.R _________________
3.N _________________
4.D _________________
5.S _________________
6.L _________________
Write out the transmission settings these automatic gear shift letters stand for.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
3
the park setting
the reverse setting
the neutral setting
the drive setting
the sport setting
the low drive setting
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 15
Find the transmission settings which fit the descriptions in Task 3.
Which setting ...
1. ensures that the car cannot move in a stationary state?
2. is used when the driver backs the car?
3. is usually used for short stops?
4. is used when the car is ready to go?
The park setting ensures that the car cannot move in a stationary state.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
4
The reverse setting is used when the driver backs the car.
The neutral setting is usually used for short stops.
The drive setting is used when the car is ready to go.
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 16
5. is suitable for high speed or overtaking other cars on the road?
6. is used for climbing hills or trying to navigate poor road conditions such as being
stuck in snow or mud?
The sport setting is suitable for high speed or overtaking other cars on the road.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
The low drive setting is used for climbing hills or trying to navigate poor road conditions such as being stuck in snow or mud.
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 17
1. ______________ 2. ___________________ 3. ___________
4. ______________ 5. _______ 6. _______ 7. ______ 8. _______
9. ______________________ 10. _________ 11. ______ 12. _________
13. ___________________ 14. ___________
Fill in the following blanks and introduce the key components of the automatic transmission.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
5
torque converter
brake bands & clutches
gear system
hydraulic system
impeller
stator
turbine
pump
hydraulic regulating valves
shift valves
servos
sun gear
planet gears and carrier
internal gear
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 18
Choose a suitable expression for each blank to complete the following conversation.
6
Situation: B is Linda, who wants to buy a car. A is Linda’s friend Tom, who is giving Linda some advice on buying a car.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
1. I like automatic transmission cars, too.
2. Congratulations on getting your driving license.
3. Thank you very much for your advice.
4. What car do you want?
5. Could you give me some advice?
A: Hi, Linda. ____________
B: Thanks, Tom. I’m considering buying a car.
A: Really? ______. A manual one or an automatic one?
B: I'm not sure. _________
A: Well, I think an AT car is safe, although the manual one is fuel-efficient.
B: Yes, you are right. ________
A: Besides, the automatic transmission car is easier to control.
B: Yes, I can’t agree with you any more. ______
A: My pleasure.
2
4
5
1
3
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 19
A: Hi, Linda. ___________________________________________
B: Thanks, Tom. I’m considering buying a car.
A: Really? ____________________________, a manual one or an automatic one?
B: I'm not sure. _____________________________
A: Well, I think an AT car is safe, although the manual one is fuel-efficient.
B: Yes, you are right. __________________________________ .
A: Besides, the automatic transmission car is easier to control.
B: Yes, I can’t agree with you any more. _______________________________
A: My pleasure.
Congratulations on getting your driving license.
Which car do you want?
Could you give me some advice?
I like automatic transmission cars, too.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Thank you very much for your advice.
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 20
Complete the word search.
7
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
s | d | f | r | e | w | q | l | y
e | l | e | m | e | n | t | o | u
r | b | r | a | k | e | k | o | p
v | x | c | g | i | j | l | s | s
o | v | c | a | r | r | i | e | r
c | h | a | n | n | e | l | n | x
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 21
Thank you!