## Slide 1
AUTOMOBILE ENGLISH
汽车专业英语
Shanxi Institute of Mechanical & Electrical Engineering
山西机电职业技术学院
Lesson 9 Manual transmission
手动变速器
Unit 3 Power train

## Slide 2
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
device | output shaft
install | determine
gear | torque
gear shift lever | gearbox
selection | eventually
driveability | pinion gear
avoid | attach
damage | permanently
switch | parallel
input shaft | fasten
counter shaft | 
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 3
Decide whether the following statements are true or false.
( ) 1. A transmission is just a power changing device.
( ) 2. Modern car transmissions have two types.
( ) 3. The driver can stay in a lower gear to avoid damaging the engine when he must
move more quickly.
( ) 4. The counter shaft is driven by the input shaft through a pinion gear.
( ) 5. The output shaft carries the power on to the wheels.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
1
T
F
F
T
T
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 4
Fill in the blanks with the missing words.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Transmission | A transmission is installed at some point between the 1____________ and the 2__________________ of the car. Modern car transmissions come in two types: 3______________ and 4________________.
Manual transmission | In a manual transmission, the driver must 5________________ selects gears by operating a gear shift lever and a 6_______________ when changing gears. The major parts of a manual transmission are an 7______________, a 8_______________ and an output shaft.
2
engine
driving wheels
manual
automatic
manually
clutch
input shaft
counter shaft
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 5
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Input shaft | The input shaft is connected to the 9___________ via a clutch so that it can be 10__________ or disengaged through the mechanism of the clutch.
Counter shaft | The counter shaft transfers 11______________ to the output shaft through the 12________ which are attached to it permanently and 13_________ along with it.
Output shaft | The output shaft is driven by the counter shaft through a set of 14_____________ gears parallel to those on the 15______________.
flyweel
engaged
power
gears
spin
transmission
counter shaft
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 6
A transmission is a speed and power changing device installed at some point between the engine and the driving wheels of the car. Modern car transmissions come in two types: manual and automatic.
In a manual transmission, the driver must manually selects gears by operating a gear shift(selector) lever and a clutch when changing gears. Proper gear selection improves the driveability but it also requires the driver to accept some training. When driving slowly, the driver can stay in a lower gear and avoid damaging the engine. When he must move more quickly, the driver can switch gears to a higher level.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 7
The major parts of a manual transmission are an input shaft, a counter shaft, and an output shaft. Shafts have gears on them which determine what torque and speed are transferred to the wheels.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 8
1. Input shaft
The car’s engine crankshaft turns and creates power. This mechanical energy must first go through the transmission gearbox before it eventually reaches the wheels. The first component to receive this energy is the input shaft. This shaft is connected to the flywheel via a clutch so that it can be engaged or disengaged through the mechanism of the clutch.
2. Counter shaft
The counter shaft is driven by the input shaft through a pinion gear. And it transfers power to the output shaft through the gears which are attached to it permanently and spin along with it.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 9
3. Output shaft
The final component that carries the power out of the transmission gearbox and on to the wheels is the output shaft. It is driven by the counter shaft through a set of transmission gears parallel to those on the counter shaft. The output shaft gears are not permanently attached to it. These gears are actually shifted manually by the driver. Only the selected gear is fastened and rotates the output shaft along with it, while the others spin freely until another one is selected.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 10
变速器是一种安装在发动机和汽车驱动轮之间的速度和功率转换装置。现代汽车的变速器有两种：手动和自动。
在手动变速器中，驾驶员在换挡时必须通过操作变速杆和离合器来手动选择档位。适当的档位选择可以提高驾驶性能，但也需要驾驶员接受一些训练。车速慢时，司机可以保持较低的档位，避免损坏发动机。当必须加速时，司机可以切换到更高的档位。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 11
手动变速器的主要部件是输入轴、副轴和输出轴。轴上有齿轮，这些齿轮决定传递给车轮的扭矩和速度。
1.输入轴
汽车的发动机曲轴转动并产生动力。这种机械能必须首先通过变速箱，然后才最终到达车轮。接收这种能量的第一个部件是输入轴。这个轴通过离合器与飞轮相连，这样飞轮就可以通过离合器的机构啮合或分离。
2.副轴
副轴由输入轴通过一个小齿轮驱动。它通过固定在副轴上并随着副轴旋转的齿轮将动力传递给输出轴。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 12
3.输出轴
将动力从变速箱输送到车轮上的最后一个部件是输出轴。它由副轴通过一组与副轴平行的传动齿轮驱动。输出轴齿轮不是永久地附在轴上。这些齿轮实际上是由司机手动转换的。只有选中的齿轮被紧固，输出轴随之旋转，其他齿轮自由旋转，直到选中另一个齿轮。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 13
1 _________________
2 _________________
3 _________________
4 _________________
5 _________________
6 _________________
7 _________________
8 _________________
Name the parts of the the manual transmission.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
3
synchronizer
shift fork
shift rail
gear shift lever
input shaft
counter shaft
gears
output shaft
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 14
Find the parts which fit the descriptions in Task 3.
Which part ...
1. transfers power to the output shaft?
2. is connected to the flywheel via a clutch?
3. is operated by the driver?
4. is driven by the counter shaft?
The counter shaft transfers power to the output shaft.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
4
The input shaft is connected to the flywheel via a clutch.
The gear shift lever is operated by the driver.
The output shaft is driven by the counter shaft.
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 15
5. determines what torque and speed are transferred to the wheels?
6. matches the speed of the desired gear to the speed of the spinning output shaft?
7. moves the synchronizer’s sleeve to lock the spinning gear to the shaft?
Gears determines what torque and speed are transferred to the wheels.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
The synchronizer matches the speed of the desired gear to the speed of the spinning output shaft.
The shift fork moves the synchromizer’s sleeve to lock the spinning gear to the shaft.
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 16
Fill in the following blanks and introduce what the manual transmission is and its working principle.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
5
utomatic
nput
utput
ear
onstant
ynchronizer
everse
ssembly
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 17
Choose a suitable expression for each blank to complete the following conversation.
6
Situation: A is a salesperson in a 4S store, B is a customer.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
1. Would you like MT or AT?
2. What can I do for you?
3. Can we have a test drive after that?
4. she’s afraid that the MT car is difficult to control.
5. Could you show me where it is?
A: Welcome to Summer 4S Store. ______________
B: I’d like to look at a hatchback. _____________
A: Certainly. This way, please. __________
B: In fact, I prefer to buy a MT car. But my wife has
just got her driving license, and ________
A: I see. Let me introduce both of them to you so that
you can make your choice.
B: Oh, it’s great. ________
A: Yes, of course.
2
5
1
4
3
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 18
A: Welcome to Summer 4S Store. ________________________
B: I’d like to look at a hatchback. _____________________________
A: Certainly. This way, please. ___________________________
B: In fact, I prefer to buy a MT car. But my wife has just got her driving license,
and _____________________________________________
A: I see. Let me introduce both of them to you so that you can make your choice.
B: Oh, it’s great. _______________________________
A: Yes, of course.
What can I do for you?
Could you show me where it is?
Would you like MT or AT?
she’s afraid that the MT car is difficult to control.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Can we have a test drive after that?
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 19
Complete the word search.
7
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
a | b | a | t | t | a | c | h | t
f | z | d | s | r | w | n | i | o
d | g | e | a | r | f | s | w | r
e | l | v | t | l | m | h | r | q
s | w | i | t | c | h | a | e | u
t | e | c | r | p | q | f | s | e
w | c | e | f | a | s | t | e | n
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 20
Thank you!