## Slide 1
AUTOMOBILE ENGLISH
汽车专业英语
Shanxi Institute of Mechanical & Electrical Engineering
山西机电职业技术学院
Lesson 12 Brakes
制动器
Unit 4 Steering & braking systems

## Slide 2
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
disastrous | rear
operate | backing plate
brake pedal | wheel cylinder
master cylinder | brake shoe
brake line | adjuster
rod | brake caliper
brake fluid | brake pad
compress | brake rotor
build up | service brake
disc type | parking brake
drum type | slip
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 3
Choose the correct answer for each question below.
1.Which is not a part of a hydraulic brake system?
A. the brake lines B. the clutch pedal
C. the brake pedal D. the master cylinder
2. What is the function of the parking brake system?
A. to reduce the speed of the car
B. to stop the running car
C. to control the speed of the car
D. to prevent the car slipping away from its parking place
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
1
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 4
Fill in the blanks with the missing words.
Brakes | It’s very 1_______________ for cars to have brakes. Usually, there are brakes on all of the 2______ wheels. These brakes are 3____________ by a 4________________ system.
Drum brake | A drum brake is usually composed of the 5___________ plate, the wheel 6_____________, the brake 7________, the brake drums and the brake 8_______________.
Disc brake | A disc brake has 9_________ main parts, including the brake 10____________, the 11_________ pad, and the brake 12__________.
2
important
four
operated
hydraulic
backing
cylinder
adjuster
shoes
three
caliper
brake
rotor
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 5
Service brake | The service brake is used to 13_____ down or 14__________ the car which is 15_________ at a high 16__________.
Parking brake | The parking brake is also called the 17__________ brake, which is used to ensure that the car doesn’t 18___________ away even on a slope.
slow
running
stop
speed
hand
slip
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 6
Brakes are very important to a car. If they don’t work properly, the result can be disastrous.
Cars have brakes on all of the four wheels. These brakes are operated by a hydraulic system. A hydraulic braking system mainly consists of the brake pedal, the master cylinder, the brake lines and the brakes.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
The brake pedal is connected to the master cylinder via a metal rod. The master cylinder is a sealed chamber full of brake fluid. The brake lines connect the master cylinder to the brakes.
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 7
When the driver presses the brake pedal, the metal rod attached to it acts on a piston in the master cylinder. This piston compresses the brake fluid in the master cylinder, which builds up pressure within the brake system. That pressure is transmitted through the brake lines and provides the force needed to work the car’s brakes.
The brakes are either a disc type or drum type. Many cars have four-wheel disc brakes, although some have discs for the front wheels and drums for the rear.
1. Drum brake
A drum brake is usually composed of the backing plate, the wheel cylinder, the brake shoes, the brake drum and the brake adjuster. When the driver applies the brake, the control device forces the brake shoes against the rotating brake drums. Friction between the shoes and the drums slows or stops the wheels so that the car is braked.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 8
2. Disc brake
The main parts of a disc brake include the brake caliper, the brake pad, and the brake rotor. When the driver applies the brake, the control device forces the brake pads against the rotating rotor. Friction between the pads and the rotor slows or stops the wheels.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 9
The car brakes can also be divided into the service brake and the parking brake. The service brake is used to slow down or stop the car that’s running at a high speed. The parking brake, which is also called the hand brake, can prevent the car slipping away from its parking place.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 10
制动器对汽车来说很重要。如果它们不能正常工作，结果可能是灾难性的。
汽车的四个轮子上都有制动器，由液压系统控制。液压制动系统主要由制动踏板、主缸、制动管路和制动器组成。刹车踏板通过金属连杆与主缸相连。主缸是一个密封的腔室，充满制动液。制动管路将主缸与制动器连接起来。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 11
当驾驶员踩下刹车踏板时，附在刹车踏板上的金属连杆作用于主缸中的活塞。这个活塞压缩主缸中的制动液，从而增加制动系统中的压力。这种压力通过刹车管路传递，并提供汽车刹车所需的力。
制动器有盘式和鼓式两种。许多汽车都有四轮盘式制动器，不过有些汽车的前轮是盘式制动器，后轮是鼓式制动器。
1. 鼓式制动器
鼓式制动器通常由制动底板、制动轮缸、制动蹄、制动鼓和制动调节器组成。当驾驶员刹车时，控制装置使刹车蹄紧贴旋转的刹车鼓。刹车蹄和刹车鼓之间的摩擦使车轮减速或停止，从而使汽车刹车。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 12
2. 盘式制动器
盘式制动器的主要部件包括制动钳、刹车片和刹车盘。当驾驶员刹车时，控制装置使刹车片紧贴旋转的刹车盘。刹车片和刹车盘之间的摩擦使轮子减速或停止。
汽车制动器也可分为行车制动和驻车制动。行车制动用于减慢或停止高速行驶的汽车。驻车制动可以防止汽车从其停放的地方滑出，也叫手刹。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 13
汽车制动器也可分为行车制动器和驻车制动器。行车制动器用于减慢或停止高速行驶的汽车。驻车制动器可以防止汽车从其停放的地方滑出，也叫手刹。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 14
1 _________________
2 _________________
3 _________________
4 _________________
5 _________________
6 _________________
7 _________________
8 _________________
9 _________________
10 _________________
drum
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
3
Name the following brake system and its parts.
brake pedal
master cylinder
brake line
brake fluid
wheel cylinder
pistons
brake drum
brake shoes
backing plate
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 15
Which part ...
1. stores the brake fluid?
2. is located inside the wheel cylinder?
3. is controlled directly by the driver?
4. is surfaced with frictional linings?
5. builds up pressure within the brake system?
Find the parts which fit the descriptions in Task 3.
The master cylinder stores the brake fluid.
The piston is located inside the wheel cylinder.
The brake pedal is controlled directly by the driver.
The brake shoes is surfaced with frictional linings.
The piston builds up pressure within the brake system.
4
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 16
6. rotates with the wheel together?
7. is a pipe through which the brake fluid passes?
The brake drum rotates with the wheel together.
The brake line is a pipe through which the brake fluid passes.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 17
1 _________________
2 _________________
3 _________________
4 _________________
5 _________________
6 _________________
7 _________________
8 _________________
Fill in the following blanks and describe how the hydraulic disc brake system works.
5
Parking
Drum
caliper
rotor
backing
shoes
brake
cylinder
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 18
A: Good morning, Miss Green. May I help you?
B: Yes._______________________________________________
And it stops when I apply the brakes.
A: Is the noise piercing?
B: Oh, yes.
A: I see. _____________________________________________
I’ll replace them with new ones.
B: Is it serious?
A: No, ____________________________________
B: Oh, it’s so good. Thank you.
A: _________________________
Choose a suitable expression for each blank to complete the following conversation.
6
I always hear some noise when driving the car.
Situation: A is a mechanic in a 4S store, B is a customer.
1. It’s very likely that your brake pads are worn out.
2. I always hear some noise when driving the car.
3. You are welcome.
4. it is the most common braking problem.
It’s very likely that your brake pads are worn out.
it is the most common braking problem.
You are welcome.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 19
Complete the word search.
7
h | y | d | r | a | u | l | i | c
i | i | p | b | t | r | o | a | y
g | c | d | r | u | m | r | k | l
h | m | u | a | p | a | r | k | i
e | m | a | k | d | i | s | c | n
o | s | p | e | e | d | p | i | y
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 20
Thank you!