## Slide 1
AUTOMOBILE ENGLISH
汽车专业英语
Shanxi Institute of Mechanical & Electrical Engineering
山西机电职业技术学院
Lesson 4 Electronic fuel injection system
电控燃油喷射系统
Unit 2 Engines

## Slide 2
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
electronic | manifold | calculate
injection | delivery | optimum
sensor | tank | volume
detect | pump | monitor
be divided into | filter | oxygen
subsystem | injector | mixture
induction | regulator | mount
consist of | spray | temperature
air cleaner | deliver | coolant
assembly | pulse | additional
throttle | manifold | incoming
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 3
Choose the correct answer for each question below.
1. The EFI system is composed of ____________ basic subsystems.
A. one B. two
C. three D. four
2. What is the basic function of the ECU?
A. To control the pulse length of the injector.
B.To control the pulse width of the injector.
C. To control the fuel injection volume.
D. To detect the engine condition.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
1
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 4
Fill in the blanks with the missing words.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Air induction system | There are three parts in the air induction system, including an 1____________ assembly, a throttle body, and an 2__________ manifold. The 3______________ contains the throttle valve.
Fuel delivery system | The fuel delivery system provides the fuel mixing with the 4_______. The fuel is taken from the fuel 5________ by the fuel 6________. Then it is 7__________ under pressure by an injector. Any fuel which is not used is returned to the tank through the 8________________.
2
air cleaner
intake
throttle body
air
tank
pump
sprayed
fuel return line
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 5
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Electronic control system | The electronic control system is composed of the 9_________ and many sensors. The ECU receives 10________ from the sensors, 11___________ the optimum fuel injection volume, and causes the 12____________ to inject the fuel. The number and types of sensors 13___________ with the system. For example, the oxygen sensor, usually mounted in the 14__________ manifold, 15___________ the amount of 16__________ in the engine’s exhaust gases.
ECU
signals
calculates
injectors
vary
exhaust
monitors
oxygen
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 6
The electronic fuel injection system uses a number of sensors to detect the engine condition and the running condition of a car. The electronic fuel injection system can be divided into three subsystems:
(1) Air induction system. The air induction system consists of an air cleaner assembly, a throttle body, and an intake manifold. The throttle body contains the throttle valve, which is opened and closed by the driver to control the amount of air entering the intake manifold.
(2) Fuel delivery system. The fuel delivery system provides the fuel which mixes with the air. The main parts of the system are the fuel tank, fuel pump, fuel filter, fuel supply line, fuel injector, fuel pressure regulator, and fuel return line.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 7
The fuel is taken from the fuel tank by the fuel pump and sprayed under pressure by an injector. The fuel pressure in the fuel line must be regulated to maintain stable by the pressure regulator. Any fuel which is not delivered to the intake manifold is returned to the tank through the fuel return line.
(3) Electronic control system. The electronic control system consists of the Electronic Control Unit (ECU) and various sensors.
The basic function of the ECU is to control the pulse width of the injector. It receives signals from the sensors whenever the engine is running. Then it calculates the optimum fuel injection volume and causes the injectors to inject the fuel.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 8
The sensors monitor various engine functions and feed this information to the ECU. The number and types of sensors vary with the system.
The oxygen sensor monitors the amount of oxygen in the engine’s exhaust gases. The ECU uses signals from the oxygen sensor to control the air-fuel mixture. The oxygen sensor is generally mounted in the exhaust manifold.
Every injection system has a temperature sensor to measure the temperature of the engine coolant. Many injection systems have an additional sensor to measure the temperature of the incoming air.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 9
电控燃油喷射系统使用多个传感器来检测发动机状况和汽车的运行状况。电控燃油喷射系统可分为三个子系统:
（1）空气供给系统。空气供给系统由空气滤清器总成、节气门体和进气歧管组成。节气门体包含节流阀，通过驾驶员的操作，节流阀会打开和关闭，从而控制进入进气歧管的空气量。
（2）燃油供给系统。燃油供给系统负责提供混合了空气的燃料。该系统的主要部件有燃油箱、燃油泵、燃油滤清器、燃油输送管、喷油器、燃油压力调节器、燃油回油管等。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 10
燃油由燃油泵从油箱中取出，并在压力下由喷油器喷射。燃油管路中的燃油压力必须由压力调节器调节以保持稳定。任何没有送到进气歧管的燃油都通过回油管回到油箱。
（3）电子控制系统。电子控制系统由电子控制单元(ECU)和各种传感器组成。
电控单元的基本功能是控制喷油器的脉冲宽度。每当发动机运转时，它就会接收传感器发出的信号。然后计算出最佳喷油量，使喷油器进行喷油。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 11
传感器监测发动机的各种功能，并将这些信息反馈给ECU。传感器的数量和类型随系统而异。
氧气传感器监测引擎废气中的氧气量。ECU使用来自氧气传感器的信号来控制空气燃料混合物。氧气传感器一般安装在排气歧管中。
每个喷射系统都有一个温度传感器来测量发动机冷却液的温度。许多喷射系统都有一个额外的传感器来测量吸入空气的温度。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 12
1 _________________
2 _________________
3 _________________
4 _________________
5 _________________
6 _________________
7 _________________
Name the parts of the fuel delivery system.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
3
fuel pressure regulator
fuel return line
fuel pump
fuel injector
fuel filter
fuel supply line
fuel tank
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 13
Find the parts which fit the descriptions in Task 3.
Which car ...
1. stores the fuel supplied into the engine?
2. is a computer controlled valve which can open and close many times each second?
3. is controlled electrically to draw the fuel from the tank and supply it to the fuel
injector?
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
4
The fuel tank stores the fuel supplied into the engine.
The fuel injector is a computer controlled valve which can open and close many
times each second.
The fuel pump is controlled electrically to draw the fuel from the tank and supply it to the fuel injector.
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 14
4. is responsible for screening out dirt and rust particles from the fuel?
5. keeps the fuel pressure stable?
6. is a pipe through which the fuel enters the engine?
7. is a pipe through which the fuel goes back to the tank?
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
The fuel pressure regulator keeps the fuel pressure stable.
The fuel supply line is a pipe through which the fuel enters the engine.
The fuel return line is a pipe through which the fuel goes back to the tank.
The fuel filter is responsible for screening out dirt and rust particles from the fuel.
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 15
FillFill in the following blanks and describe how these components work.
5
fuel supply
line
air cleaner
assembly
intake
manifold
fuel tank
fuel filter
air induction system
fuel injector
fuel pressure regulator
fuel return
line
electronic control system
ECU
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 16
A: Good morning, Miss Green. What’s the matter with
your car?
B: Good morning. _____________________
A: I see. We’ll check it for you.
A: _________________________________________
B: So ...?
A: Don’t worry.________________________________
_______
B: Oh, it’s so good. Thank you.
A: ________________
Choose a suitable expression for each blank to complete the following conversation.
6
Situation: A is a mechanic in a 4S store, B is a customer.
1.We are going to replace them with new ones.
2. My car doesn’t start up.
3. It’s my pleasure.
4.There is something wrong with the fuel injectors.
My car doesn’t start up.
There is something wrong with the fuel injectors.
It’s my pleasure.
We are going to replace them with new
ones.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 17
Complete the word search.
7
s | u | b | s | y | s | t | e | m
p | u | m | p | o | w | i | r | a
r | h | y | o | x | y | g | e | n
a | p | e | s | u | f | n | j | i
y | c | l | e | a | n | e | r | f
i | a | q | n | i | k | t | f | o
p | u | l | s | e | d | a | u | l
b | m | w | o | y | l | n | s | d
e | v | x | r | h | z | k | c | b
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 18
Thank you!