## Slide 1
AUTOMOBILE ENGLISH
汽车专业英语
Shanxi Institute of Mechanical & Electrical Engineering
山西机电职业技术学院
Lesson 7 Emission control system
排放控制系统
Unit 2 Engines

## Slide 2
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
catalytic converter | capacity
positive | require
ventilation | sufficient
evaporative | ignite
hydrocarbon | vapor
carbon monoxide | corrosive
oxide | emit
nitrogen | trap
convert | mechanical
pollutant | component
carbon dioxide | carbon canister
inert | 
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 3
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
1
Choose the correct answer for each question below.
1. Which system is used to control harmful emissions?
A. lubrication system B. cooling system
C. emission control system D. fuel injection system
2. Which is not one type of the emission control system?
A. ECU B. EGR
C. TWC D. EVAP
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 4
Fill in the blanks with the missing words.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
TWC system | This system could 1____________ hydrocarbons (HC), carbon monoxide (CO), and nitrogen oxides (NOx). It can 2___________ harmful gases and pollutants into carbon dioxide (CO2) and 3__________ (H2O). It is mounted on the 4__________ pipe.
EGR system | This system can send some exhaust gases back into the 5___________. These exhaust gases are 6__________ gases because they are already 7__________. So they decrease the combustion 8____________ of the cylinders.
2
control
convert
water
exhaust
cylinders
inert
burnt
capacity
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 5
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
AIR system | 9______________ fuel will increase hydrocarbon emissions. Inside the exhaust manifold there is sufficient 10________ to support combustion. If we introduce some 11___________, the unburned fuel will ignite. This combustion wonuce any 12___________, but it will reduce excessive hydrocarbon emissions.
PCV system | The purpose of this system is to direct the corrosive gases and 13__________ into the air-fuel intake system to be 14____________.
Unburned
heat
oxygen
power
vapors
burned
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 6
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
EVAP system | This system can trap the emissions from the fuel 15_______ and circulate them into the combustion chamber. Its key component is the carbon 16_________ that stores the hydrocarbons.
tank
canister
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 7
Emission control system is used to keep the harmful emissions as low as possible. We can generally classify the emission control system into five types: three-way catalytic converter (TWC) system, exhaust gas recirculation (EGR) system, air injection (AIR) system, positive crankcase ventilation (PCV) system and evaporative emission control (EVAP) system.
Three-way catalytic converter (TWC) system
The three-way catalytic converter system is used in all modern cars because it could not only control hydrocarbons (HC) and carbon monoxide (CO), but also control nitrogen oxides (NOx). It can convert harmful gases and pollutants into carbon dioxide (CO2) and water (H2O). It is mounted on the exhaust pipe.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 8
Exhaust gas recirculation (EGR) system
Exhaust Gas Recirculation system is used to send some exhaust gases back into the cylinders to reduce combustion temperature. The exhaust gases are inert gases because they are already burnt. Hence, they decrease the combustion capacity of the cylinders and that decreases the heat produced and less heat means lower emission.
Air injection (AIR) system
Since no engine is 100% efficient, there will always be some unburned fuel which increases hydrocarbon emissions. Combustion requires fuel, oxygen and heat. Inside the exhaust manifold there is sufficient heat to support combustion. If we introduce some oxygen, the unburned fuel will ignite. This combustion will not produce any power, but it will reduce excessive hydrocarbon emissions.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 9
Positive crankcase ventilation (PCV) system
The process of combustion forms gases and vapors. Many of them are quite corrosive, so they have to be removed. The purpose of the positive crankcase ventilation system is to direct these gases and vapors into the air-fuel intake system to be burned during combustion.
Evaporative emission control (EVAP) system
Gasoline evaporates quite easily. These evaporative emissions will cause pollution if they are emitted into the atmosphere. The evaporative emission control system can trap these emissions from the fuel tank and circulate them into the combustion chamber. Its key mechanical component is the carbon canister that stores the hydrocarbons.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 10
排放控制系统用于尽可能降低有害气体的排放。我们一般可以将排放控制系统分为五类:三元催化转化器(TWC)系统、废气再循环(EGR)系统、空气喷射(air)系统、曲轴箱正通风(PCV)系统和蒸发排放控制(EVAP)系统。
三元催化转换器(TWC)系统
三元催化转换器系统被用于所有现代汽车，因为它不仅可以控制碳氢化合物(HC)和一氧化碳(CO)，还可以控制氮氧化物(NOx)。它可以将有害气体和污染物转化为二氧化碳和水。它安装在排气管上。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 11
废气再循环系统
废气再循环系统用于将部分废气送回气缸以降低燃烧温度。废气是惰性气体，因为它们已经燃烧过了。因此，它们降低了气缸的燃烧能力，从而减少了产生的热量，减少热量意味着降低排放。
空气喷射系统
由于没有发动机是100%高效的，总会有一些未燃烧的燃油增加碳氢化合物的排放。燃烧需要燃油、氧气和热量。排气歧管内部有足够的热量来支持燃烧。如果我们引入一些氧气，未燃烧的燃油就能燃烧。这种燃烧不做任何功，但会减少过量的碳氢化合物排放。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 12
曲轴箱强制通风(PCV)系统
燃烧过程形成气体和蒸汽。其中很多都有很强的腐蚀性，所以必须去除。曲轴箱强制通风系统的目的是引导这些气体和蒸汽进入空气/燃油进气系统，并被燃烧掉。
蒸发排放控制(EVAP)系统
汽油很容易蒸发。这些蒸发排放物如果排放到大气中就会造成污染。蒸发排放控制系统可以将这些来自燃油箱的排放物聚集起来，并使其循环进入燃烧室。它的关键机械部件是储存碳氢化合物的活性碳罐。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 13
Write down what these abbreviations mean.
1. TWC ______________________________________________
2. EGR ______________________________________________
3. AIR ______________________________________________
4. PCV ______________________________________________
5. EVAP ______________________________________________
6. CO ______________________________________________
7. HC ______________________________________________
8. NOx ______________________________________________
9. CO2 ______________________________________________
10. H2O ______________________________________________
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
3
three-way catalytic converter
exhaust gas recirculation
air injection
positive crankcase ventilation
evaporative emission control
carbon monoxide
hydrocarbon
nitrogen oxide
carbon dioxide
water
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 14
Find the abbreviatioins which fit the descriptions in Task 3.
Which abbreviation ...
1. can take in some oxygen so as to ignite the unburned fuel?
2. sends some exhaust gases back into the cylinders?
3. is the clearest emission?
4. is mounted on the exhaust pipe?
5. can trap the evaporative emissions from the fuel tank？
6. can direct harmful gases into the air-fuel intake system?
AIR can take in some oxygen so as to ignite the unburned fuel.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
4
EGR sends some exhaust gases back into the cylinders.
H2O is the clearest emission.
TWC is mounted on the exhaust pipe.
EVAP can trap the evaporative emissions from the fuel tank.
PCV can direct harmful gases into the air-fuel intake system.
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 15
1 _________________
2 _________________
3 _________________
4 _________________
Fill in the following blanks and describe how the EGR system works. The following language patterns can be useful.
5
EGR valve
intake
cylinder
exhaust
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 16
A: Good morning, Miss Green. _______________________
B: ________________ The check engine light turns on this morning.
A: I see. _____________________________________
__________________________________________
B: It sounds a little serious, doesn’t it?
A: In fact, _________________ I have to check the car first.
B: OK. I have to go now, ____________________________
_____________________
A: Yes, of course. __________________________________
Choose a suitable expression for each blank to complete the following dialogue.
6
Situation: A is a mechanic in a 4S store, B is a customer.
1. Good morning.
2. I will contact you as soon as possible.
3. It usually means that there is something wrong with the emission system.
4. so can you contact me if you find the problem?
5. What can I do for you?
6. I’m not sure yet.
What can I do for you?
I’m not sure yet.
Good morning.
I will contact you as soon as possible.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
It usually means that there is something
wrong with the emission system.
so can you contact me if you
find the problem?
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 17
Complete the word search.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
7
c | a | n | i | s | t | e | r | x
a | p | o | s | i | t | i | v | e
r | a | c | m | d | f | n | u | t
b | r | e | c | v | q | e | i | r
o | y | v | a | p | o | r | z | a
n | p | i | g | n | i | t | e | p
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 18
Thank you!