## Slide 1
AUTOMOBILE ENGLISH
汽车专业英语
Shanxi Institute of Mechanical & Electrical Engineering
山西机电职业技术学院
Lesson 3 Principle of operation
工作原理
Unit 2 Engines

## Slide 2
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
principle | intake
operation | compression
combustion | exhaust
internal combustion engine | vacuum
stroke | valve
piston | prior to
cycle | explode
inventor | explosion
cylinder | crankshaft
reciprocate | 
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 3
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Choose the correct answer for each question below.
1. ___________ is important for a car and called the heart of a car.
A. The engine B. The body
C. The chassis D. The door
2. How many pistons does each cylinder of the four stroke engine have?
A. one B. two C. three D. four
1
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 4
Fill in the blanks with the missing words.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Internal combustion engines | Most internal combustion engines are 1__________ engines. This type of engine is named 2_____________ after its inventor, Nikolaus Otto. Each cylinder of the four-stroke engine has a 3_________ which reciprocates within the cylinder.
Intake stroke | During the intake stroke, the piston moves 4__________ to the bottom dead center, a vacuum is created in the 5___________. The 6___________ valve opens and the 7___________ mixture enters the cylinder.
Compression stroke | During the compression stroke, the air-fuel mixture is compressed as the piston moves 8__________. The 9_________ is fired to ignite the air-fuel mixture before the piston being at the 10_______________.
2
four-stroke
Otto cycle
piston
downwards
cylinder
intake
air-fuel
upwards
spark plug
top dead center
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 5
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Power stroke | The movement that the air-fuel mixture 11________________ and the explosion drives the piston 12______________ again is called the power stroke.
Exhaust stroke | The exhaust stroke refers to the process when the piston starts to move 13________________ again, the 14____________________ is opened. The piston moving up forces the 15________________ out of the cylinder.
explodes
downwards
upwards
exhaust valve
exhaust gases
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 6
The engine is the heart of a car. It is used to turn fuel into the energy that moves the car. Generally, a car is operated by internal combustion engines.
Most internal combustion engines are four-stroke engines, for they need four piston strokes to complete one cycle. This type of engine is also known as Otto cycle, after the name of its inventor, Nikolaus Otto. Each cylinder of the four-stroke engine has a piston which reciprocates within the cylinder. These four strokes are intake stroke, compression stroke, power stroke and exhaust stroke.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 7
During the intake stroke, the piston moves downwards to the bottom dead center so that a vacuum is created in the cylinder. The intake valve opens and the air-fuel mixture enters the cylinder.
During the compression stroke, the air-fuel mixture is compressed as the piston moves upwards. The spark plug is fired to ignite the air-fuel mixture prior to the piston being at the top dead center. Both the intake and the exhaust valves are closed.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 8
The air-fuel mixture explodes, and the explosion drives the piston downwards again. This movement, called the power stroke, turns the crankshaft. During the power stroke, the intake and the exhaust valves are still closed.
As the piston starts to move upwards again, the exhaust valve is opened, and the exhaust gases are forced out of the cylinder. This is the exhaust stroke. Thus the whole cycle is completed.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 9
发动机是汽车的心脏，用于把燃料转化为驱动汽车的能量。一般来说，汽车是由内燃机驱动的。
大多数内燃机都是四冲程发动机，需要四个活塞冲程完成一个循环。这种类型的发动机也被称为奥托循环，是以其发明者的名字尼古拉·奥托命名的。四冲程循环发动机的每个气缸都有一个活塞在气缸内往复运动。四个冲程分别是进气冲程、压缩冲程、动力冲程和排气冲程。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 10
在进气冲程中，当活塞向下移动到下止点时，气缸内就会产生真空。进气门打开，空气燃料混合物进入气缸。
在压缩冲程中，当活塞向上运动时，空气燃料混合物被压缩。在活塞到达上止点之前，火花塞发出电火花以点燃空气燃料混合物。注意两个阀门都是关闭的。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 11
空气燃料混合物燃烧膨胀，燃烧膨胀驱使活塞再次向下。这个过程被称为动力冲程，曲轴转动。此时，两个阀门都是关闭的。
当活塞再次开始向上运动时，排气阀打开，废气从气缸中排出。这是排气冲程。整个循环完成。
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 12
Name the parts of the strokes.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
3
1 | __________ | 2 | __________ | 3 | __________ | 4 | __________ | 5 | _________
6 | __________ | 7 | __________ | 8 | __________ | 9 | __________ | 10 | _________
intake valve
cylinder
crankshaft
spark plug
piston
exhaust valve
power
intake
exhaust
compression
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 13
Complete the sentences by using the words in Task 3. Change the form when necessary.
1. The air-fuel mixture is ignited by a __________ to produce an explosion, which forces
the ________ to move downwards.
2. With the ________ valve open, the engine takes in the fuel and air.
3. A 6-cylinder engine is more _________ than a 4-cylinder engine.
4. The size of the engine determines the power. The more _________ there are, the
more powerful the engine is.
5. The up and down motion of the piston is converted into rotational motion by the
__________.
6. With the ________ valve open, the piston in the cylinder moves upwards.
7. The air and the fuel are __________ in a combustion chamber before being ignited.
spark plug
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
4
piston
intake
powerful
cylinders
crankshaft
exhaust
compressed
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 14
Complete the following table and introduce to each other the four stroke cycle of the engine.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
5
Four-stroke engine
stroke | intake valve | exhaust valve | piston | air-fuel mixture | exhaust gases
intake stroke |  |  | downwards |  | ——
 |  | closed |  | is compressed and ignited in the cylinder | ——
 | closed |  | downwards |  | ——
 |  | open |  | —— | are forced out of the cylinder
open
closed
enters the cylinder
compression stroke
closed
upwards
power
stroke
closed
explodes
exhaust stroke
closed
upwards
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 15
A: Good morning. Can I help you?
B: Oh, I’m interested in this model. ________
A: It’s a 4.2-litre V8 engine.
B: ________________________
A: The top speed is 250 km/h. And it has an acceleration from 0-60 in only 6 seconds.
B: That’s impressive. _________________________
A: Yes. Here you are. You can find my phone number on it. ___
B: I’ll do that. Thanks a lot for your time.
A: You’re welcome. ______________
Choose a suitable expression for each blank to complete the following conversation.
6
Situation: A is a receptionist at a car show, B is a customer.
3
1
4
5
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
1. So what’s the top speed?
2. Enjoy the rest of the show.
3. And I want to know how big its engine is.
4. Do you have a brochure?
5. If you have any questions, just call me.
2
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 16
A: Good morning. Can I help you?
B: Oh, I’m interested in this model. _______________________________________
A: It’s a 4.2-litre V8 engine.
B: ________________________
A: The top speed is 250 km/h. And it has an acceleration from 0-60 in only 6 seconds.
B: That’s impressive. _________________________
A: Yes. Here you are. You can find my phone number on it.
__________________________________
B: I’ll do that. Thanks a lot for your time.
A: You’re welcome. ___________________________
Choose a suitable expression for each blank to complete the following conversation.
6
Situation: A is a receptionist at a car show, B is a customer.
And I want to know how big its engine is?
So what’s the top speed?
Do you have a brochure?
If you have any questions, just call me.
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Enjoy the rest of the show.
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 17
Complete the word search.
7
c | o | m | p | r | e | s | s | a
a | s | t | b | t | n | r | p | q
o | t | r | s | k | g | c | t | y
p | r | i | n | c | i | p | l | e
e | o | r | s | v | n | t | i | q
r | k | c | t | a | e | l | k | e
a | e | x | p | l | o | d | e | f
t | n | o | p | v | r | s | l | g
e | m | l | k | e | j | i | y | h
New words & expressions
Reading & speaking
Tasks before class
Tasks in class
Notes: 模板来自 http://docer.mysoeasy.com/

## Slide 18
Thank you!