## Slide 1: 机电工程专业英语
2.1 MONITOR
监护仪

## Slide 2
【Text】
The concept of a monitor
Medical monitoring instruments can continuously monitor the physiological parameters of the human body for a long time, and can store, display, analyze, and control the test results. When abnormal situations occur, alarms are issued to remind medical staff to handle them in a timely manner.
Figure 1-4 Schematic diagram of the monitor
The purpose of the monitor
This patient monitor is intended to be used for monitoring, displaying, reviewing, storing and transferring of multiple physiological parameters including ECG, heart rate (HR), respiration (Resp), temperature (Temp), SpO2, pulse rate (PR), non-invasive blood pressure (NIBP), invasive blood pressure (IBP), cardiac output (C.O.), carbon dioxide (CO2), oxygen (O2), anesthetic gas (AG), impedance cardiograph (ICG), bispectral index (BIS) and respiration mechanics (RM) of single adult, pediatric and neonatal patients.
Interpretation of resting 12-lead ECG and C.O. monitoring are restricted to adult patients only. The ICG is only for use on adult patients who meet the following requirements: height: 122 to 229 cm, weight: 30 to 159 kg. The arrhythmia detection, ST-segment, BIS and RM monitoring are not intended for neonatal patients.
This monitor is to be used in healthcare facilities by clinical professionals or under their direction. It is not intended for helicopter transport, hospital ambulance, or home use.

## Slide 3
【Text】
Introduction to the Display Screen of the Monitor
This patient monitor adopts a high-resolution TFT LCD to display patient parameters and waveforms. A typical display screen is shown below.
Figure 1-5 Typical Monitor Display Interface
1. Patient Information Area
This area shows the patient information such as department, bed number, patient name, patient category and paced status.

## Slide 4
【Text】
3. Technical Alarm Area
This area shows technical alarm messages and prompt messages. When multiple messages come, they will be displayed circularly. Select this area and the technical alarm list will be displayed.
4. Physiological Alarm Area
This area shows physiological alarm messages. When multiple alarms occur, they will be displayed circularly. Select this area and the physiological alarm list will be displayed.
5. Waveform Area
This area shows measurement waveforms. The waveform name is displayed at the left upper corner of the waveform. Select this area and the corresponding measurement setup menu will be displayed.
6. Parameter Area A
This area shows measurement parameters. Each monitored parameter has a parameter window and the parameter name is displayed at the upper left corner. The corresponding waveform of each parameter is displayed in the same row in the waveform area. Select this area and the corresponding measurement setup menu will be displayed.
7. Parameter Area B
For the parameters displayed in this area, their corresponding waveform are not displayed.
8. Prompt Message Area
This area shows the prompt messages, network status icons, battery status icons, date and time, etc. For details about battery status symbols, refer to the chapter 28 Batteries.

## Slide 5
【Text】
Clinical application of medical monitors
According to different clinical nursing objects and monitoring purposes, clinical monitors are used for the following nursing monitoring: monitoring during and after surgery; Delivery monitoring and fetal monitoring; Monitoring of critically ill patients; Monitoring of patients during the recovery period; Monitoring of patients undergoing treatment (kidney dialysis, hyperbaric oxygen chamber, radiation therapy, mental illness, etc.).
Various special monitors, also called monitoring systems, are used in departments and wards as needed, mainly including: critical patient monitors, coronary heart disease monitors, delivery monitors, neonatal and preterm infant monitors, Intracranial pressure monitors, anesthesia monitors, sleep monitors, etc.

## Slide 6
【Text】
Physiological and biochemical parameters monitored by the monitor: such as ECG monitoring, respiratory monitoring, non-invasive blood pressure monitoring, invasive blood pressure monitoring, airway carbon dioxide monitoring, airway oxygen monitoring, blood volume auxiliary monitoring, blood oxygen saturation/blood volume monitoring, temperature monitoring, pH value monitoring, blood gas monitoring, etc. In addition to the monitoring function, the medical monitor also has the function of disease diagnosis and treatment, as well as the rescue function, such as Holter monitor, blood pressure monitor, heart defibrillation monitor, etc.
Structure of medical monitors
Modern medical monitoring instruments mainly consist of four parts, namely vital sign measurement components, host and system, connection interfaces, and sensors and electrodes. The brief description of the functions of each part is as follows:
The vital sign measurement component mainly includes various measurement components for measuring human vital signs such as electrocardiogram, respiration, body temperature, blood pressure, pulse oxygen saturation, and end-breathing carbon dioxide.
The host and system mainly include the main control board, display, keyboard, recorder and operation software, and other external expansion equipment.
There is a requirement for bidirectional communication between the vital sign measurement component and the host interface, so it is necessary to set feature recognition for each vital sign measurement module to facilitate targeted operations by the host.
The connection forms of sensors, connecting cables, and vital sign measurement components are divided into hard connection and intelligent connection.

## Slide 7
【Words and phrases】
monitor n.监护仪，显示器，班长；v.监视，监听
physiological parameter 生理参数
display n.显示，陈列;v.表演，展览，显示
ECG abbr. 心电图（Electrocardiograph）
respiration n. 呼吸；（医）一次呼吸
pulse rate 脉搏率：心脏每分钟跳动的次数
non-invasive blood pressure(NIBP) 无创血压(NIBP)
carbon dioxide (CO2) 二氧化碳
anesthetic gas (AG) 麻醉气体
impedance cardiograph (ICG) 阻抗心电图
bispectral index (BIS) 双光谱指数
respiration mechanics (RM) 呼吸力学（原理）
pediatric adj.儿科的
neonatal adj. 新生的；初生的
Patient Demographics病人的人口统计
Physiological Alarm Area 生理报警区
kidney dialysis 肾脏透析
hyperbaric oxygen chamber [临床] 高压氧舱

## Slide 8
【Course practice】
Complex Sentence Analysis
(1) This patient monitor is intended to be used for monitoring, displaying, reviewing, storing and transferring of multiple physiological parameters including ECG, heart rate (HR), respiration (Resp), temperature (Temp), SpO2,and etc.
be intended to +do sth是用来做某事，为了；+to be 规定为，确定为。
be used for +doing 被用来做某事，用来做某事；+for used as 被用来做
译：该病人监护仪用于监测、显示、查看、存储和传递心电图、心率(HR)、呼吸(Resp)、体温(Temp)、SpO2等多项生理参数。
(2) Interpretation of resting 12-lead ECG and C.O. monitoring are restricted to adult patients only.
be restricted +to sth. 限于，被限制在…范围内；+by sth. 被…限制
译：静息12导联心电图和C.O.监测的解释仅限于成人患者。
(3) The arrhythmia detection, ST-segment, BIS and RM monitoring are not intended for neonatal patients.
be intended for 打算为…所用，预定给。
译：心律失常检测、st段、BIS和RM监测不适合新生儿患者。
(4) The safety performance is in line with international standards.
be in line with 符合，与…一致，标识某事物与另一事务在目标、原则上一致。
“符合”的其他英语表达：accord with （与某物相符）, conform to（与某规范相符）。
译：安全性能符合国际标准。