## Slide 1: 机电工程专业英语
2.1 INTRODUCTION OF MECHATRONICS
机电一体化概论

## Slide 2
【Text】
Introduction of Mechatronics
The Japanese coins the term of “Mechatronics” in 1970s to describe the integration of mechanical and electronic engineering The concept is anything but new, since we can all look around us and see a myriad of products that utilize both mechanical and electronic disciplines. Mechatronics. however, specifically refers to a multidisciplinary, integrated approach to product and manufacturing system design. It represents the next generation of machines, robots and smart mechanisms necessary for carrying out work in a variety of environments-primarily, factory automation, office automation and home automation.
By both implication and application, mechatronics represents a new level of integration for advanced manufacturing technology and processes. The intent is to force a multidisciplinary approach to these systems as well as to reemphasize the role of process understanding and control. This mechatronics approach is currently speeding up the already rapid Japanese process for transforming ideas into products.
Currently, mechatronics describes the Japanese practice of using fully integrated teams of product designers, manufacturing, purchasing, and marketing personnel acting in concert with each other to design both the product and the manufacturing system.
The Japanese recognized that the future in production innovation would belong to those who learned how to optimize the marriage between mechanical and electronic systems. They realized, in particular, that the need for this optimization would be most intense in application of advanced manufacturing and production systems where artificial intelligence, expert systems, smart robots, and advanced manufacturing technology systems would create the next generation of tools to be used in the factory of the future.

## Slide 3
【Text】
From the very beginnings of recorded time, mechanical systems have found their way into every aspect of our society. Our simplest mechanisms, such as gears, pulleys, and wheels have provided the basis for our tools. Our electronics technology, on the other hand, is completely twentieth-century, all of which was created within the past 85 years.
Until now, electronics were included to enhance mechanical systems performance, but the emphasis remained on the mechanical product. There had never been any master plan on how the integration would be done. In the past, it had been done on a case-by-case basis. More recently, however, because of the overwhelming advances in the world of electronics and its capability to physically simplify mechanical configurations, the technical community began to reassess the marriage between these two disciplines.
The most obvious trend in the direction of mechatronics innovation can be observed in the automobile industry. There was a time when a car was primarily a mechanical marvel with a few electronic appendages.
Electronics has repeatedly improved the performance of mechanical systems, but that innovation has been more by serendipity than by design. That is the essence of mechatronics-the preplanned application of, the efficient integration of, and mechanical and electronics technology to create an optimum product.
Comparisons were made in three categories: basic research, advanced development, and product implementation. In the advanced development and product implementation areas, Japan is equal to or better than the United States, and is continuing to pull ahead at this time.

## Slide 4
【Text】
To close the gap, we need to go much further than creating new tools. If we accept the fact that mechanical systems optimally coupled with electronic components will be the wave of the future, then we must also understand that the ripple effect will be felt all the way back to the university, where we now keep the two disciplines of mechanics and electronics separated and allow them to meet only in occasional overview sessions.
We need to rethink our present-day approach of separating our engineering staffs both from each other and from the production engineers. Living together and communicating individual knowledge will create a new synergistic effect on product development.
The definition of mechatronics is much more significant than its combined words. It can change the way we design and produce the next generation of high technology products. The nation that fully implements the rudiments of mechatronics and vigorously pursues then will lead the world to a new generation of technology innovation with all its profound implications.
II. Benefits of Mechatronics
Mechatronics may sound like utopia to many product and manufacturing managers because it is often presented as the solution to nearly all of the problems in manufacturing. In particular, it promises to increase productivity in the factory dramatically. Design changes are easy with extensive use of mechatronics elements such as CAD; CAP and MIS systems help in scheduling; and flexible manufacturing systems, computer aided design, and computer integrated manufacturing equipment cut turn around time for manufacturing. These subsystems minimize production costs and greatly increase equipment utilization. Connections from CAE, CAD, and CAM help create designs that are economical to manufactures; control and communications are improved, with minimal paper flow; and CAM equipment minimizes time loss due to setup and materials handling.

## Slide 5
【Text】
Many companies that make extensive use of computers view their factories as examples of mechatronics concepts, but on close examination their integration is horizontal-in the manufacturing area only-or at best includes primarily manufacturing and management. General Electric, as part of its effort to become a major vendor of factory automation systems, has embarked on ambitious plans for integration at several of its factories, including its Erie Locomotive Plant, its Schenectady Steam Turbine Plant» and its Charlottesville Controls Manufacturing Division. The primary benefits of mechatronics, with an emphasis on advanced manufacturing technology and factory automation, are summarized below.
(1) High Capital Equipment Utilization
Typically, the throughput for a set of machines in a mechatronics system will be up to three times that for the same machines in a stand-alone job shop environment. The mechatronics system achieves high efficiency by having the computer schedule every part to a machine as soon as it is free, simultaneously moving the part on the automated material handling system and downloading the appropriate computer program to the machine. In addition, the part arrives at a machine already fixed on a pallet, this is done at a separate work station, so that the machine does not have to wait while the part is set up.
(2)Reduced capital equipment costs
The high utilization of equipment results in the need for fewer machines in the mechatronic system to do the same work as in a conventional system. Reductions of 3:1 are common who replacing machining centers in a job-shop situation with a mechatronics system.

## Slide 6
【Text】
(3)Reduced Direct labor Costs
Since each machine is completely under computer control, full-time oversight is not required direct labor can be reduced to the less skilled personnel who fix and release the parts at the station, and a machinist lo oversee or repair the work stations, plus the system supervisor. While the fixing personnel in mechatronics environment require less advanced skills than corresponding workers, labor cost reduction is somewhat offset by the need for computing and other skills which may not be required in traditional workplaces.
(4)Reduced Work-in-Process Inventory and Lead Time
The reduction of work-in-process in a mechatronics system is quite dramatic when compared to a job-shop environment. Reductions of 80 percent have been reported at some installations and max be attributed to a variety of factors which reduce the time a part waits for metal-cutting operations. These factors include concentration of all the equipment required to produce part into a small are: reduction in the number of fixture required; reduction in the number of machines a part must travel through because processes are combined in work cells; and efficient computer scheduling of parts batched into and within the mechatronics system.
(5)Responsiveness to Changing Production Requirements
A mechatronics system has the inherent flexibility to manufacture different products as the demands of the marketplace change or as engineering design changes are introduced. Further more, required spare part production can be mixed into regular runs without significantly disrupting the normal mechatronics system production activities.
(6)Ability to Maintain Production
Many mechatronics systems are designed to degrade rationally when one or more machines fail. This is accomplished by incorporating redundant machining capability and a material handling system that allows failed machines to be by passed. Thus, throughput is maintained at a reduced rate.

## Slide 7
【Text】
(7)High Product Quality
Sometimes, an over looked advantage of a mechatronics system especially when compared to machines that have not been federated into a cooperative system, is improved product quality. The basic integration of product design characteristics with production capability, the high level of automation, the reduction in the number of fixtures and the number of machines visited, better designed permanent fixtures, and greater attention lo part/machine alignment all result in good individual part quality and excellent consistency from one work-piece to another, further resulting in greatly reduced costs of rework.
(8)Operational Flexibility
Operational flexibility offers a significant increment of productivity. In some facilities, mechatronics systems can run virtually unattended during the second and third shift. This nearly unmanned, mode of operation is currently the exception rather than the rule. It should, however become increasingly common as better sensors and computer controls are developed to detect and handle unanticipated problems such as tool breakages and part-flow jams. In this operational mode, inspection, fixture, and maintenance can be performed during the first shift.
(9)Capacity Flexibility
With correct planning for available floor space, a mechatronics system can be designed for low production volumes initially; as demand increases new machines can be added easily to provide the extra capacity required.

## Slide 8
【Words and phrases】
I
mechatronics n. 机械电子学，机电一体化
term n. 术语
coin v. 创造，杜撰（新词、新语）
integration n. 结合，一体化
integrate v. 使一体化，使结合
discipline n. 学科
generation n. （一）代
smart adj. 灵敏的，灵巧的
implication n. 含义，本质
multidisciplinary adj. 包括多种学科的
reemphasize v. 反复强调
purchase v. 购买， 采购
market v. 销售
innovation n. 改革，革新
optimization n. 优化
optimize v. 使最佳化
marriage n. 结合， 结婚
performance n. 性能，特性
overwhelming adj. 压倒的，不可抵抗的
simplify v. 简化
configuration n. 结构， 外形
community n. 团体， 界
reassess v. 对……再评价
serendipity n. 善于发掘新奇事物的才能
preplan v. 预先计划，规划
staff n. （全体）工作人员
synergistic adj. 叠加的，复合的
implement v. 实现，提供方法
rudiment n. 基础，入门
vigorously adv. 强有力地
pursue v. 推行，贯彻
profound adj. 意义深远的

## Slide 9
【Words and phrases】
II
sound v. 听起来
Utopia n. 乌托邦，理想的完美境界
promise v. 有……可能
dramatically adv. 显著地
element n. 组成部分
scheduling n. 编制进度
cut n． 削减
turnaround n．工作周期
subsystem n．子系统
minimize v．使……减至最小
utilization n．利用(率)
create v．产生，形成，创造
communication n． 通讯，联络
setup v．装卡；安装
horizontal adj. 横向的，水平的
vendor n．卖主
embark v． 从事，着手
Erie 伊利(美国东部城市)
locomotive n．火车头
Schenectady 斯克奈塔第(美国纽约州东部城市)
Charlottesviile 夏洛茨维尔(美国北卡罗来纳州南部城市)
turbine n． 透平(机)，汽轮机，涡轮(机)
volume：产量。
fix v．夹紧，固定； n．夹具
pallet n．托板
oversight n．监督，观察
full-time adv.全部时间的，全部工作日的
skilled adj. 熟练的，需要技能的
division n．部门
summarize n．概括，摘要
capital adj. 主要的，基本的，资本的
throughput n．生产量
schedule n．安排，调度，排定
simultaneously adv. 同时地
download n．下行传输，下载
machinist n．机械工人，机械师
oversee n．监视；照料
supervisor n．管理人员，检查员
skill n．技能，技术
offset v．抵消
workplace n．车间，工厂；工作面．
inventory n．库存
installation n．装置
attribute v．由…引起
batch n．分批
responsiveness n．响应度，反应性

## Slide 10
【Words and phrases】
inherent adj. 固有的，先天的
flexibility n．灵活性，适应性，柔性
introduce v．提出，引进，介绍
significantly adv．大大地；有意义地 ．
disrupt v．中断，干扰
degrade v．降低(等级)；减少
gracefully adv．适度地
fail n．失效，损坏
incorporate v．使结合
redundant adj. 多余的
bypass v． 绕过，走旁路
overlook v．漏掉，未注意到
federate v．联合
cooperative adj. 合作的，协作的
visit v．逗留，拜访
permanent adj. 永久性的
alignment n．校正，调整
consistency n．一致性
work-piece n．工件
rework n．, v．返工，再制
facility n．设备，设施
virtually adv．实质上，实际上
unattended adj. 无人(看管)的
shift n．(轮班工作制的)班次
unmanned adj. 无人(驾驶)的
mode n．方式
exception n．例外
increasingly adv．日益
sensor n．传感器
handle v．处理
unanticipated adj. 非预期的
breakage n. 划伤
jam n．，v．阻塞，卡住
inspection n．检验，验收
maintenance n．维修，保养

## Slide 11
【Course practice】
Complex Sentence Analysis
(1) The Japanese coins the term of “Mechatronics” in 1970s to describe the integration of mechanical and electronic engineering.
the term of “Mechatronics”- “机电一体化”术语。
译：日本人在七十年代新造了“机电一体化” 这个术语，用来描述机械工程与电子工程的结合。
(2) The concept is anything but new, since we can all look around us and see a myriad of products that utilize both mechanical and electronic disciplines.
译：这个概念其实并不新奇，因为我们可以看到我们周围数不清的机电一体化产品。
(3) It represents the next generation of machines, robots, and smart mechanisms necessary for carrying out work in a variety of a environments—primarily, factory automation, office automation, and home automation.
smart mechanism-智能机械/智能装置。
译：它描述了所需要的下一代机器、机器人、和智能机械，它们能在不同的环境下进行工作。基本上能实现工厂自动化、办公室自动化和家庭自动化。
(4) This mechatronic approach is currently speeding up the already-rapid Japanese process for transforming ideas into products.
speed up- 加速。
译：目前，机电一体化加速了日本已经从理念到产品的更快速的转化。

## Slide 12
【Course practice】

## Slide 13
【Course practice】

## Slide 14
【Course practice】
Complex Sentence Analysis
(12) Connections from CAE, CAD, and CAM help create designs that are economical to manufacture; control and communications are improved, with minimal paper flow; and CAM equipment minimizes time loss due to setup and materials handling．
此句也是并列句，由三个简单句组成：第一句是Connections…to manufacture；第二句是control and …paper flow;第三句是 and CAM…material handling.
CAE（computer-aided engineering）: 计算机辅助工程——为检查一项设计的基本误差或使工艺性、经济性、生产率和性能达到最佳而使用信息处理系统的设计方法。
CAM（computer-aided manufacturing）:计算机辅助制造——使用计算机来帮助制造业人员生产工业产品的加工体系。计算机用于制造业的两大方面：其一是面向工厂的管理和维护(包括仓库管理、计划调度、机器控制、信息管理和质量控制等)，是管理与生产信息的处理联成一体; 其二是面向制造工序的实际控制(包括对数控机床、其它加工机械、各种运输装置、机器人的控制)，形成自动化工厂，使整个生产过程从始至终都处于计算机控制之下。
译：将CAE，CAD和 CAM联系起来，可以产生经济生产的设计；在最小的图纸流量下增强控制和交流；同时CAM 设备可以减少安装和处理原材料的时间。
(13) The mechatronic system achieves high efficiency by having the computer schedule every part to a machine as soon as it is free, simultaneously moving the part on the automated material handling system and downloading the appropriate computer program to the machine．
by having…, moving…and downloading…是三个并列的动名词作介词by的宾语，与by组成短语，作方式状语。
automatic material handling system： 自动材料输送系统。
download: 下行传输——把一个程序或数字文件从中央计算机向远程计算机或智能终端的存储器传输的过程。
译：当机器空闲下来时，就让计算机调度每个零件到这台机器，同时在自动材料输送系统中使零件运动，并且把适当的计算机程序下行传输到这台机器，这样就能使机电一体化系统达到很高的效率。