## Slide 1: 机电工程专业英语
2.2 DEFIBRILLATOR
除颤仪

## Slide 2
【Text】
Concept of defibrillator
In a very short period of time, a strong current is supplied to the heart (currently, direct current is used), which can depolarize all cardiac autonomic cells at the same time in an instant, and inactivate all possible reentry channels. Then the Sinoatrial node, which has the highest autonomy in the cardiac pacing system, can regain its dominant position to control the heart beat, so the heart rhythm returns to sinus.
Types of defibrillators
1. Unidirectional waveform defibrillator
The energy selection is from 0 to 360J, and different energies are selected based on the patient's age and weight adjustment.
2. Bidirectional waveform defibrillator
The energy selection is from 0 to 200J, which is safer and more effective than unidirectional waveform defibrillators. Therefore, bidirectional waveform defibrillators are now commonly used in clinical practice.
Figure 1-1 Physical image of defibrillator(1)
Figure 1-2 Physical image of defibrillator(2)

## Slide 3
【Text】
Types of defibrillation
1. Synchronous defibrillation:
It is used for cardioversion of Atrial fibrillation, flutter, supraventricular and ventricular tachycardia. Using the R wave on the patient's electrocardiogram to trigger discharge, the electrical pulse occurs at the descending branch of the R wave. Energy selection starts from low. Monitor the patient's ECG during defibrillation. If it does not revert to Sinus rhythm, it can be increased; Electric power, electric defibrillation again.
2. Non synchronous defibrillation:
It is only used for Ventricular fibrillation and flutter. At this time, the patient has lost consciousness, and should be immediately defibrillated. After defibrillation, observe whether the patient's heart rhythm changes to sinus rhythm through the electrocardiograph. Multiple intermittent defibrillation is possible, with energy ranging from low to high.
(1) Indications
1) Ventricular fibrillation and flutter are absolute evidences of electric cardioversion.
2) Atrial fibrillation and flutter with hemodynamic disorder.
3) Paroxysmal supraventricular tachycardia and ventricular tachycardia that are ineffective or have severe hemodynamic disorders treated with drugs and other methods. Preexcitation syndrome with tachyarrhythmia.

## Slide 4
【Text】
(2) Contraindications
1) With a long medical history, there is significant cardiac hypertrophy and fresh thrombus formation in the atrium, or a history of thrombus formation within the past 3 months.
2) Atrial fibrillation or flutter with high or complete atrioventricular block.
3) Heterotopic tachyarrhythmia with sick Sinoatrial node syndrome.
4) When there is a history of digitalis poisoning and Hypokalemia, it is not suitable for electrical cardioversion.
Use of defibrillators
1. Non synchronous electric defibrillation
If the patient experiences ventricular fibrillation or flutter, electric defibrillation should be performed as early as possible. The early onset of ventricular fibrillation is generally coarse fibrillation, and defibrillation is easy to succeed at this time, so it should be attempted within 2 minutes. Defibrillators are commonly used in emergency situations for patients with cardiac arrest, as shown in Figures 1-3. The curve between defibrillation time and patient survival rate is shown in Figures 1-4.

## Slide 5
【Text】
Operating Steps
(1) Prepare for defibrillation, and prepare various rescue equipment and drugs: defibrillator, electrocardiograph, oscilloscope, and rescue equipment and drugs required for Cardiopulmonary resuscitation.
(2) The patient is lying flat on a hard bed, with an open venous passage that fully exposes the chest wall.
(3) Perform routine electrocardiogram and electrocardiogram monitoring before surgery. After completing the electrocardiogram recording, remove the lead wire from the electrocardiograph to avoid electric shock damage to the electrocardiograph.
(4) Select a suitable electrode plate and evenly apply conductive adhesive. Clean the skin of the patient's defibrillation site with a piece of physiological saline, water, and gauze. Apply the negative electrode (Apex) to the left midline and three transverse fingers under the armpit (apex of the heart). At the positive electrode (Stenal): at the right edge of the right subclavian sternum (at the base of the heart).

## Slide 6
【Text】
(5) Select asynchronous electric cardioversion.
(6) Choose the appropriate energy: The unidirectional waveform defibrillator is generally chosen for adults at 300-360J, and for children at 2J per kilogram of body weight. Adults generally choose a bidirectional waveform defibrillator of 150-200J, while children weigh 2J per kilogram.
(7) Charging: Before charging, instruct other personnel not to come into contact with the patient, the hospital bed, and the instruments and equipment connected to the patient to avoid electric shock. Then, press the charging switch, and the screen will display the predetermined energy to be fully charged.
(8) After charging, place the two electrodes correctly on the patient's skin according to the diagram on the electrode, and apply appropriate pressure to ensure that the electrode plate is in good contact with someone else's skin. Press the discharge button on the electrode plate with both hands and thumbs at the same time.
(9) After defibrillation, immediately observe whether the patient's ECG reverts to Sinus rhythm.
(10) If ventricular fibrillation, flutter, etc. continue to occur and cardioversion fails, it should be recharged and the steps repeated after a certain interval of time.
(11) After the operation is completed, reset the energy switch to zero, position the patient, monitor heart rate and rhythm, and follow the doctor's instructions for medication.
(12) Keep records.

## Slide 7
【Text】
2. Synchronous electric cardioversion
If the patient has Atrial fibrillation, flutter, supraventricular and ventricular tachycardia, synchronous cardioversion is feasible.
Operating Steps
(1) Those who chose to have cardioversion stopped using digitalis for 1-3 days before operation and were given drugs to improve heart function and correct Hypokalemia and Acidosis.
(2) Take quinidine, procainamide and other drugs 1-2 days before cardioversion to prevent arrhythmia recurrence after cardioversion.
(3) On the day of cardioversion, fast and empty the bladder.
(4) Establish a venous channel, connect an electrocardiogram machine and an electrocardiogram monitor, perform a full lead electrocardiogram before surgery, and select a lead with a larger R wave to test the synchronization of electrical cardioversion.
(5) Propofol, etomidate and other Anesthetic should be properly used, or Diazepam 0.3-0.5mg/Kg should be slowly injected intravenously until the patient's eyelash reflex begins to disappear during the deep substitute anesthesia process, and breathing should be closely observed. If there is respiratory depression, oxygen should be given to the mask.
(6) Select synchronous electric cardioversion.
(7) Select appropriate energy, Atrial fibrillation is 150J~200J, Atrial flutter is 80J-100J, and supraventricular tachycardia is 100J.
(8) Charging: Before charging, instruct other personnel not to come into contact with the patient, hospital bed, or instruments connected to the patient to avoid electric shock. Then, press the charging switch, and the screen will display the predetermined energy to indicate full charge.

## Slide 8
【Text】
(9) After charging, place the two electrodes correctly on the patient's skin according to the diagram on the electrode, and press the discharge button on the electrode board with both hands and thumbs simultaneously.
(10) After discharge, observe whether the patient's ECG has reverted to Sinus rhythm. If it has not reverted to Sinus rhythm, increase the electric power and restore the rhythm again.
(11) After the operation is completed, return the energy switch to the zero position, set the patient's A-curve to measure the heart rhythm, and follow the doctor's instructions for medication.
(12) Keep records.
Precautions
1.The defibrillator should be regularly checked for performance, charged in a timely manner, and disinfected after use.
2.When applying conductive paste to the electrode plate, it is not allowed to rub the two electrode plates against each other. The electrode plate should be in close contact with the patient's skin to ensure good conductivity.
3.If the patient is thin or has uneven skin, two gauze blocks dipped in physiological saline can be placed directly on the patient's defibrillation site.
4.During an electric shock, no one should come into contact with the patient or hospital bed to avoid electric shock.

## Slide 9
【Text】
For patients with fine fibrillation type ventricular fibrillation, cardiac compression, oxygen therapy, and medication should be performed first to turn it into coarse fibrillation, followed by electric shock to improve the success rate.
6.The skin at the shock site may have mild erythema, pain, or Myalgia, which can be relieved by itself after 3-5 days.
7.During open chest defibrillation, the electrodes are placed directly on the front and rear walls of the heart, and the defibrillation energy is generally 5-10J.
8.For ventricular tachycardia that can clearly distinguish QRS and T waves, synchronous electrical cardioversion should be performed. For those that cannot be distinguished, asynchronous electrical defibrillation should be used.

## Slide 10
【Words and phrases】
Depolarize vt. 去偏光；去偏极
Cardiac adj. 心脏的；（与）贲门（有关）的；n.<非正式>心脏病患者
cardiac autonomic cells 心脏自主细胞
inactivate vt. 使不活动；使不活泼；阻止活动
reentry n .[航] 再入；再进
reentry channel 再入通道
Sinoatrial n, 窦房
Node n. 茎节；结，结节；结点
Sinoatrial node 窦房结
autonomy n. 自治，自治权；
the heart rhythm 心律
Unidirectional adj. 单向的；单向性的
Unidirectional waveform defibrillator 单向波形除颤器
Bidirectional waveform defibrillator 双向波形除颤器
clinical adj. 诊所的，医务室的；临床的
Synchronous adj. 同步的；同时的
Synchronous defibrillation 同步除颤
cardioversion n. 复律法；心律转变法
Atrial adj. 心房的；门廊
Atrial fibrillation 房颤
flutter v. 飘动，颤动；
supraventricular n, 室上性
ventricular adj. 心室的；脑室的；膨胀的；腹部的
tachycardia n. [内科] 心动过速；心跳过速
ventricular tachycardia 室性心动过速
electrocardiogram n. [内科] 心电图
trigger v. 引发，激发；
ECG abbr. 心电图（Electrocardiograph）
Sinus rhythm 窦性心律
Ventricular fibrillation 室颤
Consciousness n. 知觉，清醒
intermittent adj. 间歇的，断断续续的
hemodynamic adj. 血液动力学的
hemodynamic disorder 血流动力学紊乱
hypertrophy n. [病理] 肥大；过度增大
syndrome n. 综合征，征群，综合症状；
electrocardiograph n. [内科] 心电图仪，[内科] 心电图描记器
oscilloscope n. [电子] 示波器；示波镜

## Slide 11
【Course practice】
Complex Sentence Analysis
(1) If it does not revert to Sinus rhythm, it can be increased.
do not revert to不要返回到/恢复到
译：若不能恢复窦性心律，它可能会增加。
(2) When there is a history of digitalis poisoning and Hypokalemia, it is not suitable for electrical cardioversion.
…is not suitable for…不适合
译：当有洋地黄中毒和低钾血症史时，不宜电复律。
(3) The early onset of ventricular fibrillation is generally coarse fibrillation, and defibrillation is easy to succeed at this time, so it should be attempted within 2 minutes.
…be attempted…试图/尝试
coarse fibrillation粗颤
译：室性颤动的早期起病一般为粗颤，此时除颤易成功，应在2分钟内尝试完成。
(4) Charging: Before charging, instruct other personnel not to come into contact with the patient.
come into contact with…接触：指与某物或某人直接或间接地相互作用或沟通。
译：充电:充电前，提醒其他人员不要与患者接触。