## Slide 1: 机电工程专业英语
1.3 HEAT EXCHANGER
热交换机

## Slide 2
【Text】
If a material is to be cooled, a shell-and-tube heat exchanger can also be used. The cooling medium is normally water, chilled water, or cold brine. Brine (a solution of salt in water) is used because it freezes at a lower temperature than pure water. Sometimes liquids are cooled by circulating them through pipes exposed the atmosphere; this is called an air-cooled heat exchanger. The cooling process is speeded if a fan is used to blow cool air rapidly over the tubes.
When a shell-and-tube heat exchanger is used for cooling, the material to be cooled may be either on the tube-side or the shell-side, with the cooling medium on the other side. If one of the two liquids is more corrosive than the others (brine, for example, can be corrosive) it is usually on the tube-side. The tubes can then be made of a corrosion-resistant material, with a cheaper material for the shell. If a corrosive material is used on the shell-side-in contact with both the inner surface of the shell and the outer surface of the tubes-both the tubes and shell must be able to withstand corrosion.

## Slide 3
【Text】
It is possible to operate shell-and-tube heat exchangers in either the horizontal or vertical position, but horizontal exchangers are most common. When steam is used for heating, it is always introduced through the upper opening, or nozzle, in the shell, so that the lower opening can be used for draining condensate. If a pool of condensate builds up in such an exchanger (usually due to malfunctioning functioning or wrongly sized steam trap) and submerges some of the tubes, the heat transfer suffers because condensing steam transfers heat more rapidly than does hot water.
When a liquid is used on the shell-side，it is always introduced through the lower nozzle and withdrawn through the upper nozzle. In this way the engineer can be assured that the exchanger remains full, with liquid surrounding all the tubes.

## Slide 4
【Text】
Shell-and-tube heat exchangers are so widely used that they are available as stock items from many manufacturers. There are a number of standard designs used throughout the industry. However, no group of standard exchangers could fulfill all needs, so many exchangers are custom designed and manufactured. The size of the shell-and-tube heat exchanger needed for any particular job depends mainly on the amount of heat to be transferred and the volume of fluid to be handled. The calculations are learned in college by most engineers, but computer programs now do them automatically.

## Slide 5
【Words and phrases】
shell n. 贝壳, 壳, 外形, 炮弹
shell-and-tube heat exchanger 管壳式换热器
medium n. adj. 媒体, 方法, 媒介；中间的, 中等的,
chill n. adj. v. 寒冷的；使冷, 变冷, 冷藏
brine n. 盐水
solution n. 解答, 解决办法, 溶解, 溶液
freeze v. 冻结
circulate v. （使)流通, (使)运行, (使)循环, (使)传播
air-cooled heat exchanger 空冷器
corrosive adj. n. 腐蚀的, 腐蚀性的腐蚀物, 腐蚀剂
corrosion n. 侵蚀, 腐蚀状态
withstand vt. 抵挡, 经受住
horizontal adj. 地平线的, 水平的
vertical position 竖直位置
nozzle n. 管口, 喷嘴
draining n. 排水 泄水 排泄
withdrawn adj. 性格内向的,偏僻的, 孤独的
condensate n. 冷凝物
submerge v. 浸没, 淹没, 掩没； vi.潜水
assure vt. 确告, 保证, 担保
fulfill vt. 履行, 实现, 完成(计划等)
custom n. 习惯, 风俗 v.定制, 承接定做活的
calculation n. 计算, 考虑
automatically adv. 自动地, 机械地

## Slide 6
【Course practice】
Complex Sentence Analysis
(1) Sometimes liquids are cooled by circulating them through pipes exposed the atmosphere; this is called an air-cooled heat exchanger.
Sometimes liquids are cooled by circulating them through pipes exposed the atmosphere与this is called an air-cooled heat exchanger是并列句。
在前一句中liquids是主语，are cooled是谓语部分，by circulating them through pipes exposed the atmosphere是现在分词短语作状语，其中的exposed the atmosphere是过去分词短语做定语修饰pipe.
译：有时，液体通过暴露在大气中的管道循环冷却;这被称为风冷式热交换器。
(2) When a shell-and-tube heat exchanger is used for cooling, the material to be cooled may be either on the tube-side or the shell-side, with the cooling medium the other side.
在句中When a shell-and-tube heat exchanger is used for cooling是状语从句, the material 是主语to be cooled 是不定式做定语修饰the materials，may be either on the tubeside or the shellside是谓语部分, with the cooling medium the other side是介词短语作伴随状语，省略了 介词on，即with the cooling medium on the other side 。
译：当采用管壳式换热器进行冷却时，待冷却物料可以在管侧，也可以在壳侧，冷却介质在另一侧。

## Slide 7
【Course practice】
Complex Sentence Analysis
(3) If a corrosive material is used on the shellside—in contact with both the inner surface of the shell and the outer surface of the tubes---both the tubes and shell must be able to withstand corrosion.
If引导条件状语从句a corrosive material is used on the shellside，“in contact with both the inner surface of the shell and the outer surface of the tubes”是插入语，做补充说明。both the tubes and shell must be able to withstand corrosion是主句。
译：如果在外壳上使用腐蚀性材料—与外壳的内表面和管的外表面都接触—管子和外壳都必须能够承受腐蚀。
(4) If a pool of condensate builds up in such an exchanger (usually due to malfunctioning functioning or wrongly sized steam trap) and submerges some of the tubes, the heat transfer suffers because condensing steam transfers heat more rapidly than does hot water.
本句中If a pool of condensate builds up in such an exchanger (usually due to malfunctioning functioning or wrongly sized steam trap) and submerges some of the tubes是条件状语从句，the heat transfer suffers是主句，because condensing steam transfers heat more rapidly than does hot water为原因状语从句，译为蒸汽冷凝比热水要快的多。
译：如果在这样的交换器中积聚了一池冷凝水(通常是由于故障或尺寸错误的蒸汽疏水阀)并淹没了一些管道，传热就会受到影响，因为冷凝蒸汽传递热量的速度比热水更快。

## Slide 8
【Course practice】
Complex Sentence Analysis
(5) The size of the shell-and-tube heat exchanger needed for any particular job depends mainly on the amount of heat to be transferred and the volume of fluid to be handled.
这是一个单句，The size of the shell-and-tube heat exchanger needed for any particular job是主语，其中needed for any particular job 是过去分词短语做后置定语修饰heat exchanger。
译：任何特定作业所需的管壳式热交换器的尺寸主要取决于要传递的热量和要处理的流体体积。