## Slide 1: 机电工程专业英语
2.3 PROGRAMMABLE LOGIC CONTROLLER
PLC

## Slide 2
【Text】
A programmable logic controller, PLC, or programmable controller is a small computer used for automation of real-world processes, such as control of machinery on factory assembly lines. The PLC usually uses a microprocessor. The program can often control complex sequencing and is often written by engineers. The program is stored in battery-backed memory and/or EEPROMs.
PLCs have the basic structure, shown in Figure 1-1.
From the figure, the PLC has four main units: the Programme memory, the Data memory, the Output devices and the Input devices. The Programme memory is used for storing the instructions for the logical control sequence. The status of switches, interlocks, past values of data and other working data is stored in the Data memory.
The main differences from other computers are the special input/output arrangements. These connect the PLC to sensors and actuators. PLCs read limit switches, temperature indicators and the positions of complex positioning systems. Some even use machine vision. On the actuator side, PLCs drive any kind of electric motor, pneumatic or hydraulic cylinders or diaphragms, magnetic relays or solenoids. The input/output arrangements may be built into a simple PLC, or the PLC may have external I/O modules attached to a proprietary computer network that plugs into the PLC.

## Slide 3
【Text】
PLCs were invented as less expensive replacements for older automated systems that would use hundreds or thousands of relays and cam-timers. Often, a single PLC can be programmed to replace thousands of relays. Programmable controllers were initially adopted by the automotive manufacturing industry, where software revision replaced the rewiring of hard-wired control panels.
The functionality of the PLC has evolved over the years to include typical relay control, sophisticated motion control, process control, Distributed Control Systems and complex networking.
The earliest PLCs expressed all decision making logic in simple ladder logic inspired from the electrical connection diagrams. The electricians were quite able to trace out circuit problems with schematic diagrams using ladder logic. This was chosen mainly to reduce the apprehension of the existing technicians.
Today, the PLC has been proven very reliable, but the programmable computer still has a ways to go. With the IEC 661131-3 standard, it is now possible to program these devices using structured programming languages, and logic elementary operations.
A graphical programming notation called Sequential Function Charts is available on certain programmable controllers.

## Slide 4
【Text】
However, it should be noted that PLCs no longer have a very high cost (often thousands of dollars), typical of a “generic“ solution. Modem PLCs with full capabilities are available for a few hundred USD. There are other ways for automating machines, such as a custom micro­controller-based design, but there are differences among both: PLCs contain everything needed to handle high power loads right out of the box, while a microcontroller would need an electronics engineer to design power supplies, power modules, etc. also a microcontroller based design would not have the flexibility of in-field programmability of a PLC. That is why PLCs are used in production lines, for example.
These typically are highly customized systems so the cost of a PLC is low compared to the cost of contacting a designer for a specific, one-time only design. On the other hand, in the case of mass-produced goods, customized control systems quickly pay for themselves due to the lower cost of the components.

## Slide 5
【Words and phrases】
Actuator n. [自] 执行机构；激励者；促动器；致动器
Electric actuator 电动执行机构；电力传动装置；电动装置
Piezoelectric actuator 压电传动装置，气压传动装置
Linear actuator 直线驱动器；线性致动器
Valve actuator 阀门驱动装置；阀门执行机构
Hydraulic actuator 液压执行器；液动装置
Rotary actuator 旋转引动器；摇动液压缸；旋转式激励器；旋转式致动装置
Pneumatic adj. 气动的，气力的，n.气胎
Hydraulic adj. 水力的，水压的，液压的，n. 液压传动装置
Relay n. ［电工］继电器
Solenoid n. ［电］螺线管
Cam n. 凸轮
Automate adj. 自动化的; v.使自动化
Initially adv. 最初，开头
Ladder n. 梯子，梯形
Inspire vt. 作为…原因或根源；引起；激励，鼓励：激发行动
Trace out 促动，描绘出
Apprehension n. 担心，忧虑
Circuit n. 电路
Load n. 负载，重荷；v.装上，装进；承载，装载
power supply 电源
module n. 模数，模块
flexibility n. 弹性，适应性，柔韧性
battery-backed memory and/or EEPROM 随机存储器和/或电可擦写可编程只读存储器
Distributive control system 分布式控制系
IEC 国际电工委员会
sequential function chart 顺序功能图

## Slide 6
【Course practice】
Complex Sentence Analysis
(1) The program is stored in battery-backed memory and/or EEPROMs.
其中，battery-backed memory and/or EEPROM 为：随机存储器和/电可擦写可编程只读存储器。
译：程序通常存储在随机存储器和(或)电可擦写可编程只读存储器中。
(2) PLCs were invented as less expensive replacements for older automated systems that would use hundreds or thousands of relays and cam-timers.
that would use hundreds or thousands of relays and cam-timers是一定语从句，修饰older automated systems, that在定语从句作主语，指older automated systems,定语从句可以翻译成older automated systems定语。
译：用可编程控制器替代要使用成千上百个继电器和凸轮的早期的自动控制系统更加实惠。
(3) However, it should be noted that PLCs no longer have a very high cost (often thousands of dollars), typical of a “generic" solution.
it should be noted that……值得注意的是…
这是一主语从句，it是形式主语，that PLCs no longer have a very high cost (often thousands of dollars), typical of a “generic" solution才是真正的主语，that只是引导词，在主语从句不充当任何成分。
译：然而，值得注意的是，PLC不再是非常昂贵的产品(通常要数千美元)，而是一种普通的产品。
(4) Modem PLCs with full capabilities are available for a few hundred USD.
available- adj.可用的，可获得的；有空的，有闲暇的；未婚的
…be available for… …可供...使用
译：现在，功能完善的PLC也只要数百美元。USD: United States Dollar,美元。