## Slide 1: 机电工程专业英语

## Slide 2
【Text】
I. Numerical Control Technology Applications
One of the most fundamental concepts in the area of advanced manufacturing technologies is numerical control (NC).
Controlling a machine tool using a punched tape or stored program is known as numerical control (NC). NC has been defined by the Electronic Industries Association (EIA) as “a system in which actions are controlled by the direct insertion of numerical data at some point. The system must automatically interpret at least some portion of this data”. The numerical data required to produce a part is known as a part program.
A numerical control machine tool system contains a machine control unit (MCU) and the machine tool itself (Fig.1-1). The MCU is further divided into two elements: the data processing unit (DPU) and the control loops unit (CLU). The DPU processes the coded data from the tape or other media and passes information on the position of each axis, required direction of motion, feed rate, and auxiliary function control signals to the CLU. The CLU operates the drive mechanisms of the machine, receives feedback signals concerning the actual position and velocity of each of the axes, and signals of the completion of operation. The DPU sequentially reads the data. When each line has completed execution as noted by the CLU, another line of data is read.
Fig. 1-1 Numerical control system

## Slide 3
【Text】
Geometric and kinematic data are typically fed from the DPU to the CLU and CLU then governs the physical system based on the data from the DPU.
Numerical control was developed to overcome the limitation of human operators, and it has done so. Numerical control machines are more accurate than manually operated machines, they can produce parts more uniformly, they are faster, and the long-run tooling costs are lower. The development of NC led to the development of several other innovations in manufacturing technology:
  Electric discharge machining
  Laser-cutting
  Electron beam welding
Numerical control has also made machine tools more versatile than their manually operated predecessors. An NC machine tool can automatically produce a wide variety of parts, each involving an assortment of widely varied and complex machining processes. Numerical control has allowed manufacturers to undertake the production of products that would not have been feasible from an economic perspective using manually control led machine tools and processes.
II. Principles of NC Machines
An NC machine can be controlled through two types of circuits：open-loop and closed-loop. In the open-loop system (Fig. 1-2(a)), the signals are sent to the servomotor by the controller, but the movements and final positions of the worktable are not checked for accuracy.

## Slide 4
【Text】
The closed-loop system (Fig. 1-2 (b)) is equipped with various transducers, sensors, and counters that measure accurately the position of the worktable. Through feedback control, the position of the worktable is compared against the signal. Table movements terminate when the proper coordinates are reached. The closed-loop system is more complicated and more expensive than the open-loop system.
Fig. 1-2 Schematic illustration of NC machine
III. Types of Control Systems
There are two basic types of control systems in numerical control, point-to-point and contouring.
1) In a point-to-point system, also called positioning, each axis of the machine is driven separately by leadscrews and, depending on the type of operation, at different velocities. The machine moves initially at maximum velocity in order to reduce nonproductive time, but decelerates as the tool approaches its numerically defined position. Thus, in an operation such as drilling (or punching a hole), the positioning and cutting take place sequentially.

## Slide 5
【Text】
After the hole is drilled or punched, the tool retracts upward and moves rapidly to another position, and the operation is repeated. The path followed from one position to another is important in only one respect. It must be chosen to minimize the time of travel, for better efficiency. Point-to-point systems are used mainly in drilling, punching, and straight milling operations.
2) In a contouring system (also known as a continuous path system), the positioning and the operations are both performed along controlled paths but at different velocities. Because the tool acts as it travels along a prescribed path, accurate control and synchronization of velocities and movements are important. The contouring system is typically used on lathes, milling machines, grinders, welding machinery, and machining centers.

## Slide 6
【Words and phrases】

## Slide 7
【Course practice】
Complex Sentence Analysis
(1) NC has been defined by the Electronic Industries Association (EIA) as“a system in which actions are controlled by the direct insertion of numerical data at some point. The system must automatically interpret at least some portion of this data”.
EIA(美国电子工业协会)广泛代表了设计生产电子元件、部件、通信系统和设备的制造商以及工业界、政府和用户的利益，在提高美国制造商的竞争力方面起到了重要的作用。
该句引号中的前一句为as的宾语从句。
译：美国电子工业协会对数字控制所下的定义为：“一种各项工作都由在各点上直接插入的数字来控制的系统。该系统必须至少能够自动解释这些数字中的部分。”
(2) The CLU operates the drive mechanisms of the machine, receives feedback signals concerning the actual position and velocity of each of the axes, and signals of the completion of operation.
CLU为本句的主语，后带三个动词作并列谓语。第二个分句中的feed back signals为动词宾语, concerning引导的现在分词短语对其进行修饰。第三个分句中的signal为动词，表示“发出信号”，与前两个动词时态相同，构成并列谓语。
译：控制单元操作机床的机械驱动装置，接收关于每个轴的实际位置和速度的反馈信号，并且发出控制信号完成操作。
(3) Numerical control has allowed manufacturers to undertake the production of products that would not have been feasible from an economic perspective using manually control led machine tools and processes.
that引导的定语从句对名词短语production of products进行修饰。
From an economic perspective从经济的观点出发，从经济的角度来看
译：数字控制使得制造者们可以承担产品的加工，其产品的加工从经济的观点上看使用人工控制机床和加工过程是不太可行的。
(4) The closed-loop system is more complicated and more expensive than the open-loop system.
“more… than …” 在此为“比…更…”
译：闭环系统比开环系统更复杂更昂贵。