## Slide 1: 机电工程专业英语
2.2 AIRFRAME CONSTRUCTION
机身机构认知

## Slide 2
【Text】
The airframe of a fixed-wing aircraft is generally considered to consist of five principal units：the fuselage, wing, stabilizers, flight control surface, and landing gear (The power plant of the airplane is normally optional.) (Figure 1-1, Figure 1-2). Helicopter airframes consist of the fuselage, main rotor and related gearbox, tail rotor (on helicopters with a single main rotor), and the landing gear.
The airframe components are constructed from a wide variety of materials and are joined by riveting, bolting, screwing, welding or adhesive. The aircraft components are composed of various parts called structural members (i. e., stringers, longerons, ribs, bulkheads, etc.)

## Slide 3
【Text】
The fuselage is the main structure or body of the aircraft. It provides space for cargo, controls, accessories, passengers, and other equipment. In single engine aircraft, it also houses the power plant. In multi-engine aircraft, the engines may either be in the fuselage, attached to the fuselage, or suspended from the wing structure. They vary principally in size and arrangement of the different compartments.
The typical design of fuselage may be divided into three classes:(1)monocoque, (2)semi-monocoque, or(3)reinforced shell. The true monocoque construction (Figure 1-3) uses formers, frame assemblies, and bulkheads to give shape to the fuselage, but the skin carries the primary stresses. Since no bracing members are present, the skin must be strong enough to keep the fuselage rigid. thus, the biggest problem involved in monocoque construction is maintaining enough strength while keeping the weight within allowable limits.
To overcome the strength/weight problem of monocoque construction, a modification called semi-monocoque construction (Figure 1-4) was developed. In addition to formers, frame assemblies, and bulkheads, the semi-monocoque construction has the skin reinforced by longitudinal members.
The reinforced shell has the skin reinforced by a complete framework of structural members.
Different portions of the same fuselage may belong to any one of the three classes, but most aircraft are considered to be of semi-monocoque type construction.
The semi-monocoque fuselage is constructed primarily of the alloys of aluminum magnesium, although steel and titanium are found in areas of high temperatures.

## Slide 4
【Text】
Primary bending loads are taken by the longerons, which usually extend across several points of support. The longerons are supplemented by other longitudinal members, called stringers. Stringers are more numerous and lighter in weight than longerons. The stringers are served as fillings. They have some rigidity, but are chiefly used for giving shape and for attachment of the skin. Stringers and longerons prevent tension and compression from bending the fuselage.
The vertical structural members are referred to as bulkheads, frames, and formers. The heaviest of these vertical members are located at intervals to carry concentrated loads and at points where fittings are used to attach other units, such as the wings, power plants, and stabilizers.
The strong, heavy longerons hold the bulkheads and formers, and these, in turn, hold the stringers. All of these joined together form a rigid fuselage framework.
The metal skin or covering is riveted to the longerons, bulkheads, and other structural members and carries part of the load.

## Slide 5
【Text】
There are a number of advantages in the use of the semi-monocoque fuselage. The bulkheads, frames, stringers, and longerons facilitate the design and construction of a streamlined fuselage, and add to the strength and rigidity of the structure. The main advantage，however, lies in the fact that it does not depend on a few members for strength and rigidity. This means that a semi-monocoque fuselage, because of its stressed-skin construction, may withstand considerable damage and still be strong enough to hold together.
Fuselages are generally constructed in two or more sections. On small aircraft, they are generally made in two or three sections, while larger aircraft may be made up of as many as six sections.
Quick access to the accessories and other equipment carried in the fuselage is provided by numerous access doors, inspection plates, landing gear wheel wells, and other openings.
Wing
The structure of a typical wing consists of a spar-rib framework enclosed by a thin covering of metal sheet. The spar, or beam, extends from the fuselage to the wing-tip. One or more spars may be used in the wing, but the two-spar design is most common. The ribs, normally at right angles to the spars, give the wing its external shape. If the covering is of metal sheet, it contributes its own share of strength to the wing. This “stressed skin” type of wing is used in all large planes.
The size and shape of wing vary widely, depending on specific aerodynamic considerations. Wings of many supersonic planes have a high degree of sweepback (arrowhead tapering from the nose of the plane) and are as thin as possible, with a knife-like leading edge. Such a shape helps to reduce the shock of compression when the plane approaches the speed of sound.

## Slide 6
【Words and phrases】
airframe n. 机体，飞机骨架
fixed-wing n. 固定翼
fuselage n. 机身
stabilizer n. 安定面
control surface 操纵面（舵面）
landing gear 起落架
helicopter a. 直升机
component n. 元件，部件
structural member 结构件
stringer n. 纵材，桁条，长桁
longeron n. 纵梁，大梁
bulkhead n. 隔框（通常指封闭的或半封闭的隔框）
rudder n. 方向舵
elevator n. 升降舵
flap n. 襟翼
aileron n. 副翼
spoiler n. 扰流板
slat n. 缝翼
tail cone 尾锥
wing tip 翼尖
engine strut 发动机挂架
pylon （发动机）吊架，挂架
main landing gear 主起落架
nose landing gear 前起落架
cargo 货物
monocoque 硬壳式（结构）
semi -monocoque 半硬壳式
frames/former 构架
assembly 组装，组件 强度
strength 力量
framework 框架，边框/框架，隔框（通常指空心隔框）
portion n. 部分
rigidity n. 刚度
streamlined adj. 流线型的
stress n. 压力，应力, 加压力
withstand v. 经受，承受
access door 接近门
contribute to 有助于……的
consideration n. 考虑，需要考虑的事项
sweepback n. 后掠角
Leading Edge(LE) 前部，前缘
rear adj. 后面的
stationary adj. 固定的，静止的，不变的
auxiliary adj. 辅助的
trim tab 配平调整片
spring tab 弹簧调整片
speed brake 减速板
shock strut 减震支柱
mechanism n. 机械装置，机构，机制
wheel brake 机轮刹车
maneuver v. 操纵，机动

## Slide 7
【Course practice】
Complex Sentence Analysis
(1) The airframe components are constructed from a wide variety of materials and are joined by riveting, bolting, screwing, welding or adhesive.
分析：联系前后文，这句中的“riveting, bolting, screwing”应翻译成“物接、螺栓 连接、螺钉连接”。
译：机体部件由各种材料组成，通过钾接、螺栓连接、螺钉连接、焊接、胶接相连。
(2) The stationary section of the vertical surface is called the fin, and the movable section, the rudder.
分析：本句是省略句，为使语言简洁，"the rudder”前省略了“is called”。
译：不能动的垂直安定面称为垂尾，上面可动的部分称为方向舵。
(3) The metal skin or covering is riveted to the longerons, bulkheads, and other structural members and carries part of the load.
分析：A be riveted to B A被铆接在B上；与此类似，be threaded to 表螺纹连接。
译：金属外壳或覆盖物被铆接在纵梁、隔板和其他构件上，并承担部分载荷。