## Slide 1: 机电工程专业英语
1.2 TOOLS AND EQUIPMENT
制冷用设备与工具

## Slide 2
【Text】
The air-conditioning technician must work with electricity. It is necessary to use safely the various tools and equipment. Special tools are needed to install and maintain electrical service to air-conditioning units. Wires and wiring should be installed according to the National Electrical Code (NEC). Following is a brief discussion of the more important tools used by the electrician in the installation of air conditioning and refrigeration equipment.
Pliers
Pliers come in a number of sizes and shapes designed for special applications, See Fig.1-1a. Pliers are available with either insulated or un-insulated handles. Although pliers with insulated handles are always used when working on “hot” wires，they must not be considered sufficient protection alone. Other precautions must be taken. Long-nose pliers are used for close work in panels or boxes.
Fuse Puller
The fuse puller is designed to eliminate the danger of pulling and replacing cartridge fuses by hand Fig.1-1b. It is also used for bending fuse clips, adjusting loose cutout clips, and handling live electrical parts. It is made of a phenolic material, which is an insulator. Both ends of the puller are used. Keep in mind that one end is for large-diameter fuses; the other is for small-diameter fuses.

## Slide 3
【Text】
Screwdrivers
Screwdrivers come in many sizes and tip shapes. Those used by electricians and refrigeration technicians should have insulated handles. For safe and efficient use, screwdriver tips should be kept square and sharp. They should be selected to match the screw slot. See Fig. 1-1c.
The Phillips-head screwdriver has a tip liking a star and is used with a Phillips screw. These screws are commonly found in production equipment. The presence of four slots assures that the screwdriver will not slip in the head of the screw.
Wrenches
Three types of wrenches used by the air-conditioning and refrigeration trade are shown in Fig.1-2.
The adjustable open-end wrenches are commonly called crescent wrenches.
Monkey wrenches are used on hexagonal and square fittings such as machine bolts, hexagonal nuts, or conduit unions.
Pipe wrenches are used for pipe and conduit work. They should not be used where crescent or monkey wrenches can be used. Their construction will not permit the application of heavy pressure on square or hexagonal material. Continued misuse of the tool in this manner will deform the teeth on the jaw face and mar the surfaces of the material being worked.

## Slide 4
【Text】
Soldering Equipment
The standard soldering kit used by electricians consists of the same equipment that the refrigeration mechanics use. See Fig.1-3a. It consists of a non-electric soldering device in the form of a torch with propane fuel cylinder or an electric soldering iron, or both.
Tool Kits
Some tool manufacturers make up tool kits for the refrigeration. See Fig.1-3b for a good example. In the Snap-on tool kit，the leak detector is part of the kit. The gages are also included. An adjustable wrench, tubing cutter, hacksaw, flaring tool, and ball-peen hammer can be hung on the wall and replaced when not in use. One of the problems for any repairperson is keeping track of tools.

## Slide 5
【Words and phrases】
the National Electrical Code (NEC) 国家电气规程
pliers n. 钳子；老虎钳（plier的复数形式）
fuse puller 熔丝拔钳
cartridge fuses 熔线筒
cartridge fuse 熔断丝管 | 熔丝管 | 筒式熔断器
phenolic n. adj. [胶粘] 酚醛树脂 [有化] 酚的
screwdrivers n. 螺刀；螺丝批；螺丝起子
crescent n. 新月，弦月，新月形的东西
hexagonal adj. 六边的，六角形的
propane n. [有化]丙烷
hacksaw n. 钢锯；可锯金属的弓形锯vt. 用钢锯锯断
flaring tool [机]扩口工具|胀管器

## Slide 6
【Course practice】
Complex Sentence Analysis
(1) Following is a brief discussion of the more important tools used by the electrician in the installation of air conditioning and refrigeration equipment.
句中Following是主语，brief discussion是补语；介词短语of the more important tools修饰discussion；used by引导的过去分词短语修饰tools。
brief意为“ 简明扼要的”, 例：Now please be brief - my time is valuable. 现在请长话短说–我的时间很宝贵。
译：下面简单介绍一下电工在安装空调制冷设备时使用的比较重要的工具。
(2) Pliers come in a number of sizes and shapes designed for special applications.
句中，Pliers是主语 come in 为谓语a number of sizes and shapes是宾语。过去分词短语 designed for special applications修饰sizes and shapes。
come in意为“开始使用；起作用；出现。例如：
Nylon stockings came in soon after the end of the war. 战后不久尼龙袜子就时兴起来。
Here is the plan of attack, and this is where you come in. 这是进攻示意图，你负责这个地区。
That's where the trouble often comes in. 那就是经常出现纠纷之处。
译：钳子有多种尺寸和形状，专为特殊应用而设计。

## Slide 7
【Course practice】
Complex Sentence Analysis
(3) Their construction will not permit the application of heavy pressure on square or hexagonal material.
句中construction 是主语，will not permit 为谓语，the application 为宾语。借此短语of heavy pressure 和on square or hexagonal material用来修饰宾语。
permit意为“许可；允许”。例如：
Try to go out for a walk at lunchtime, if the weather permits.如果天气条件允许，午饭时尽量出去散散步。
Smoking is not permitted.不许吸烟。
译：它们的结构不允许在方形或六边形材料上施加重压。
(4) Continued misuse of the tool in this manner will deform the teeth on the jaw face and mar the surfaces of the material being worked.
用这种方式滥用管钳，会使钳口牙齿磨损，并且在材料的工作面上留下瑕疵。句中Continued misuse of the tool in this manner 做主语，后面是并列成分。will deform 和mar是谓语，the teeth 和the surfaces是宾语。
misuse意为“滥用；误用”。例如：
I hate to see her misusing her time like that.我不愿看到她把时间用在不正当的事情上。
the misuse of power and privilege.…权力和特权的滥用。
译：以这种方式继续滥用工具将使颚面上的齿变形，并损坏被加工材料的表面。