## Slide 1: 机电工程专业英语
2.2 METAL-CUTTING PROCESSES
金属切削过程

## Slide 2
【Text】
Metal-cutting processes are extensively used in the manufacturing industry. They are characterized by the fact that the size of the original workpiece is sufficiently large that the final geometry can be circumscribed by it, and that the unwanted material is removed as chips, particles, and so on. The chips are a necessary means to obtain the desired tolerances, and surface roughness. The amount of scrap may vary from a few percent to 70%~80% of the volume of the original work material.
Owing to the rather poor material utilization of the metal-cutting processes, the anticipated scarcity of materials and energy, and increasing costs, the development in the last decade has been directed toward an increasing application of metal-forming processes. However, die costs and the capital cost of machines remain rather high; consequently, metal-cutting processes are, in many cases, the most economical, in spite of the high material waste, which only has value as scrap. Therefore, it must be expected that the material removal processes will for the next few years maintain their important position in manufacturing. Furthermore, the development of automated production systems has progressed more rapidly for metal-cutting processes than for metal-forming processes.
Metal-cutting processes remove material from the surface of a workpiece by producing chips. This requires that the cutting tool material be harder than the workpiece material. The final geometry of the workpiece is thus determined from the geometry of the tool and the pattern of motions of the tool and the workpiece. The basic process is mechanical：actually, a shearing action combined with fracture.

## Slide 3
【Text】
As mentioned previously, the unwanted material in metal-cutting processes is removed by a rigid cutting tool, so that the desired geometry，tolerances, and surface roughness are obtained. Examples of processes in this group are turning, drilling, reaming, milling, shaping, planning, broaching, grinding, honing, mid lapping.
Most of the cutting or machining processes are based on a two-dimensional surface creation, which means that two relative motions are necessary between | the cutting tool and the work material. These motions are defined as the \ primary motion, which mainly determines the cutting speed, and the feed motion, which provides the cutting zone with new material.
In turning the primary, motion is provided by the rotation of the j workpiece, and in planning it is provided by the translation of the table; in turning die feed motion is a continuous translation of the tool, and in planning it is an intermittent translation of the tool. Figure 1-1 shows basic machining parameters in turning.
Figure 1-1 basic machining parameters in turning

## Slide 4
【Text】
Cutting Speed
The cutting speed v is the instantaneous velocity of the primary motion of the tool relative to the workpiece (at a selected point on the cutting edge).
The culling speed for turning, drilling, and milling processes can be expressed as；
v = πdn (m/min) (1.1)
where v is the cutting speed in m/min, d the diameter of the workpiece to be cut in meters,; and n the workpiece or spindle rotation in rev/min. Thus v, d,and n may relate to the work material or the tool, depending on the specific kinematic pattern. In grinding the cutting speed is normally measured in m/s.
Feed
The feed motion f is provided to the tool or the workpiece and, when added to the primary motion, leads to a repeated or continuous chip removal and the creation of the desired machined surface. The motion may proceed by steps or continuously. The feed speed vf, is defined as the instantaneous velocity of die feed motion relative to the workpiece (at a selected point on the cutting edge).
For turning and drilling, the feed f is measured per revolution (mm/rev) of the workpiece or the tool; for planning and shaping f is measured per stroke (mm/stroke) of the tool or the workpiece. In milling the feed is measured per tooth of the cutter fz ( mm/tooth); that is, fz is the displacement of the workpiece between the cutting action of two successive teetli. The feed speed vf (mm/min) of the table is therefore the product of the number of teeth z of the cutter, the revolutions per minute of the cutter n , and the feed per tooth (vf = nzfz).

## Slide 5
【Text】
A plane containing the directions of the primary motion and the feed motion is defined as the working plane, since it contains the motions responsible for the cutting action.
Depth of Cut(Back Engagement)
In turning (Fig. 1-1 ) the depth of cut a (sometimes also called engagement) is the distance that the cutting edge engages or projects below the original surface of the workpiece. The depth of cut determines the final dimensions of the workpiece. In turning, with an axial feed, the depth of cut is a direct measure of the decrease in radius of the workpiece and with radial feed the depth of cut is equal to the decrease in the length of workpiece.
Chip Thickness
The chip thickness h1 in the undeformed state is the thickness of the chip measured perpendicular to the cutting edge and in a plane perpendicular to the direction of cutting (see Fig. 1-1 ). The chip thickness after cutting ( i.e., the actual chip thickness h2)is larger than the undeformed chip thickness, which means that the cutting ratio or chip thickness ratio r = h1/h2 is always less than unity.
Chip Width
The chip width b in the undeformed state is the width of the chip measured along the cutting edge in a plane perpendicular to the direction of cutting.
Area of Cut
For single-point tool operations, the area of cut A is the product of the undeformed chip thickness h1 and the chip width b (i.e., A=h1 b). The area of cut can also be expressed by the feed f and the depth of cut a as follows：
h1=f sink and b = a/sink (27.2)
where K is the tool cutting edge angle.
Consequently, the area of cut is given by A =fa (27.3)

## Slide 6
【Words and phrases】

## Slide 7
【Course practice】
Complex Sentence Analysis
(1) the feed f is measured per revolution (mm/rev) of the workpiece or the tool.
① is measured 被测量
② …per revolution每转…
译：进给量是工件或刀具每转一圈(mm/rev)来测量的。
(2) metal-cutting processes are, in many cases, the most economical, in spite of the high material waste, which only has value as scrap.
① in spite of 尽管
② in many cases 多数情况下
译：金属切削过程，在许多情况下，是最经济的，尽管存在较高的材料浪费（仅存在废料价值的材料）。