## Slide 1: 机电工程专业英语
2.1 AERODYNAMICS BASICS
空气动力学基础

## Slide 2
【Text】
An aircraft in straight-and-level un-accelerated flight has four forces acting on it (in turning, diving, or climbing flight, additional forces come into play).These forces are：lift, an upward-acting force；drag, a retarding force of the resistance to lift and to the friction of the aircraft moving through the air；weight, the downward effect that gravity has on the aircraft； and thrust, the forward-acting force provided by the propulsion system (or, in the case of unpowered aircraft, by using gravity to translate altitude into speed). Drag and weight are elements inherent in any object, including an aircraft. Lift and thrust are artificially created to enable an aircraft to fly (Figure 1-1).
Lift
Bernoulli' s principle states that when a fluid flowing through a tube reaches a con­striction t or the narrowest part of the tube, the speed of the fluid flowing through that con­striction is increased and its pressure decreased. The cambered (curved) surface of an air- foil(wing) affects the airflow exactly as a constriction in a tube affects airflow.

## Slide 3
【Text】
Figure 1-2 illustrates this similarity. In Figure 1-2, the effect of air flowing over a curved surface, such as an airfoil, is similar to the effect of air flowing through a limit on the upper surface of a wing, where the air flow is faster and the pressure is lower. In contrast, on the lower surface of the wing, the air velocity is slower and the pressure is stronger. In this way, the air flow creates a pressure difference (the difference in pressure) between the upper and lower surfaces of the wing, which in turn creates the lifting force of the aircraft.
It needs to be emphasized that air flowing over the top surface of the wing must reach the trailing edge of the wing in the same amount of time as the air flowing under the wing. To do this, the air passing over the top surface moves at a greater velocity than the air passing below the wing because of the greater distance it must travel along the top surface. This increased velocity, according to Bernoulli' s principle, means a corresponding decrease in pressure on the surface. Thus, a pressure differential is created between the upper and lower surfaces of the wing, forcing the wing upward in the direction of the lower pressure. In the other words, the difference in curvature of the upper and lower surfaces of the wing builds up the lift force.

## Slide 4
【Text】
Three-fourths of the total lift of an airfoil is the result of the decrease in pressure over the upper surface. Hie impact of air on the under surface of an airfoil produces the other one-fourth of the total lift. Within limits, lift can be increased by increasing the angle of attack, the wing area, the free-stream velocity, or the density of the air, or by changing the shape of the airfoil.
Weight
Weight is a force that acts opposite to lift. Designers thus attempt to make the aircraft as light as possible. Because all aircraft designs have a tendency to increase in weight during the development process, modem aerospace engineering staffs have specialists in the field controlling weight from the beginning of the design. In addition, pilots must control the total weight that an aircraft is permitted to carry (passengers, fuel, and freight) both in amount and in location. The distribution of weight (i.e., the control of the center of gravity of the aircraft) is as important aerodynamically as the amount of weight being carried.
Thrust
Thrust, the forward-acting force, opposed to drag as lift is opposed to weight. Thrust is obtained by accelerating a mass of ambient air to a velocity greater than the speed of the aircraft；the equal and opposite reaction is for the aircraft to move forward. In reciprocating or turboprop-powered aircraft, thrust derives from the propulsive force caused by the rotation of the propeller, with residual thrust provided by the exhaust. In a jet engine, thrust derives from the propulsive force of the rotating blades of a turbine compressing air, which then expanded by the combustion of introduced fuel and exhausted from the engine.

## Slide 5
【Text】
Drag
Acting in continual opposition to thrust is drag, which has two elements：parasitic drag and induced drag.
Parasite Drag
Parasite drag includes all drag created by the airplane, except that drag directly associated with the production of lift. It' s created by the disruption of the flow of air around the airplane’ s surfaces. Parasite drag is normally divided into three types：form drag, skin friction drag, and interference drag. .
Form Drag
Form drag is created by any structure which protrudes into the relative wind. The amount of drag created is related to both the size and shape of the structure. For example, a square strut creates substantially more drag than a smooth or rounded strut. Streamlining reduces form drag.
Skin Friction Drag
Skin friction drag is caused by the roughness of the airplane' s surfaces. Even though these surfaces may appear smooth, under a microscope they may be quite rough. A thin layer of air clings to these rough surfaces and creates small eddies which contribute to drag.
Interference Drag
Interference drag occurs when varied currents of air over an airplane meet and interact. This interaction creates additional drag. One example of this type of drag is the mixing of the air where the wing and fuselage is joined.

## Slide 6
【Text】
Each type of parasite drag varies with the speed of the airplane. The combined effect of all parasite drag varies proportionately to the square of the air speed. In other words, if air speed doubled, parasite drag increases by a factor of four.
For most flights it is desirable to have all drag reduced to a minimum, and for this reason considerable attention is given to streamlining the form of the aircraft by eliminating as much drag-inducing structure as possible (e.g., retracting the landing gear, using flush riveting, and painting and polishing surfaces). Some less obvious elements of drag include the relative disposition and area of fuselage, wing, engine, and empennage surfaces; the intersection of wings and tail surfaces.
Induced Drag
Induced drag is the main by-product of the production of lift. It is directly related to the angle of attack of the wing. The greater the angle, the greater the induced drag.
Over the past several years the winglet has been developed and used to reduce induced drag. As discussed earlier in this article, the high pressure air beneath the wing tends to spill over to the low pressure area above the wing, producing a strong secondary flow. If a winglet of the correct orientation and design is fitted to a wing tip, a rise in both total lift and drag is produced. However, with a properly designed winglet, the amount of lift pro­duced is greater than the additional drag, resulting in a net reduction in total drag.

## Slide 7
【Text】
As the angle of attack increase, so does drag; at a critical point, the angle of attack can become so great that the airflow is broken over the upper surface of the wing, and lift is lost while drag increases. This critical condition is termed the stall (Figure 1-3).
The aerodynamics of supersonic flight is complex. The Mach number (M) refers to the method of measuring airspeed that was developed by the Austrian physicist Ernst Mach. Mach number is the speed of an object moving through air, or any other fluid substance, divided by the speed of sound as it is in that substance for its particular physical conditions, including those of temperature and pressure.
The critical Mach number for an aircraft has been defined as that at which on some point of the aircraft, the airflow has reached the speed of sound.
At Mach numbers in excess of the critical Mach number (that is, speeds at which the airflow exceeds the speed of sound at local points on the airframe), there are significant changes in forces, pressures, and moments acting on the wing and fuselage caused by the formation of shock waves. One of the most important effects is very large increase in drag as well as a reduction in lift.

## Slide 8
【Words and phrases】
level adj. 水平的；平坦的；齐平的
un-accelerated adj. 未加速的
dive v. 向下俯冲，
come into play 开始起作用，开始运行
retard…v. 延迟
resistance n. 反对，抵制；抵抗，反抗；抵抗力
friction n. 摩擦，摩擦力
inherent adj. 固有的，内在的，与生俱来的
artificially adv. 人工地，人为地
constriction n. 约束，束紧
camber n. 拱曲度（路面中间微拱的曲面）；拱形; v.成弧形；使拱起
curved adj. 成曲线形的；
resemblance n. 相似之处
illustrate v. 图解说明，阐明
trailing edge 后缘
velocity n. 速度
pressure differential 压差
curvature n. 弯曲，曲率
freight n. 货物
aerodynamically adv. 空气动力学地
mass n. 块；质量；大量
ambient adj. 周围的，外界的
reciprocating adj. 往复式发动机的，活塞式发动机的
propulsive adj. 推进的，有推进力的
propeller n. 螺旋桨；推进器
residual adj. 剩余的，残留的
exhaust v. 排气，废气
blade n. 叶片，桨叶
turbine n. 涡轮，涡轮机
compress v. 压缩
combustion n. 燃烧
parasitic adj. 寄生的；附加的
induced adj. 诱导的；感应的
interference n. 干扰，阻碍
eliminate v. 排除，消除，消灭
retract v. 收回，缩进，缩回
flush adj. 齐平的
rivet n. 铆钉; vt.铆接；固定
disposition n. 配置；排列；部署
empennage n. 机尾；尾翼面
intersection n. 相交点
winglet n. （翼梢）小翼
spill v. 溢出；溅出
orientation n. 方向，方位，定位，定向
critical adj. 临界的；关键的
stall v. n. 失速
supersonic adj. 超音速的 超音速
in excess of 超过
reduction n. 减小，减少

## Slide 9
【Course practice】
Complex Sentence Analysis
(1) An aircraft in straight-and-level un-accelerated flight has four forces acting on it (in turning, diving, or climbing flight, additional forces come into play).
分析：科技英语注重对概念给予精确的定义，注意此句的主语用多个词汇的定语加 以描述。
【译文】：对于一架水平直飞、无加速度的飞机，有4种力作用于其上(当飞机进行转弯、俯冲、爬升飞行时，额外的力将作用于其上)。
(2) The cambered (curved) surface of an airfoil(wing) affects the airflow exactly as a constriction in a tube affects airflow.
分析：“exactly as”翻译为“正如……”，注意affect、effect、effort等拼写相近的词汇词义的差别.
【译文】：一段翼剖面(大翼)的拱形曲面对气流的影响，正如一段管子的节流处对气流的影响。
(3) As the angle of attack increases, so does drag；at a critical point, the angle of attack can become so great that the airflow is broken over the upper surface of the wing, and lift is lost while drag increases. This critical condition is termed the stall.
分析：注意“So do sth.”的翻译，以及“so... that”句型。
【译文】：当迎角增大，阻力也随之地大，在临界点，迎角变得如此之大，以至于气流在大翼上表面分离，升力丧失而阻力增加。这种临界状态称为失速。