## Slide 1: 机电工程专业英语
1.1 SLUSH SUPPLY PUMP
供浆泵

## Slide 2
【Text】
1.General Description
Model GJ Slush Supply Pump is a vertical single-suction submerged pump suitable for transporting mud, ore slush, sewage, and other similar liquid in oil field, metallurgy, construction, environmental protection and other industries. The suction inlet is on upper pump, with vane suction inlet upward, so there is no need to use any shaft seal and the frequent faults of former submersed pump's shaft seal are also solved. The advantage of this structure is no shaft seal such as filler seal, mechanical seal, etc. so that power loss(shaft seal friction force)is reduced and stopping fault caused by changing and maintaining shaft seal parts is also avoided. The axial force generated by the pump during operation is upward, balances the rotor weight(partly or wholly), which improves the operation condition for upper bearing,extends the life span of bearing. The structure of this model pump is national patent.
2.Model Meaning

## Slide 3
【Text】
4.Structure Introduction
The model pump is Vertical single-stage centrifugal pump, consisting of casing,vane, shaft, pump cover, shaft seal body, linking pipeline, support, motoi; etc.Casing, pump cover, bearing bodyjinking pipeline,support compose flow-conducting parts and support parts;vane and shaft compose rotor parts,which are supported in support parts by upper and lower bearings.The vertical motor is fixed on the topjined by the claw shape coupling and pump shaft. Between two bearings there is refueling oil cup or oil hole.(See the structure drawing for more details )
5.Working Principles and Features
When the pump is working,the motor revolves pump shaft through shaft coupling. Liquid is drawn into vane though upper casing enters casing after getting energy, and drains from pump discharge.
Because structure of this model pump is special, the pump can operate normall without leaking though there is no shaft seal.The trouble caused by renewing and maintaining shaft seal is avoided and shutdown time for repairing is reduced. The axial force generated by the pump during operation can balance the rotor weight, which improves operation condition for bearing, reduces power loss(friction force), and heightens the pump efficiency accordingly.
6.Operation and Maintenance
(l)Check if all tight parts are tightened before operating pump.
(2)Fill lithium-lubricating grease into the upper bearing, machine oil No.20 into the lower one.
(3)Check if the motor rotation is correct. This type of pump rotates counterclockwise from the motor direction.
(4)During pump use, the bearing temperature should be checked, and the maximum temperature should not exceed 80 ℃.

## Slide 4
【Text】
(5)Add lubricating oil (grease) every 10-15 days during use.
(6)Check the sealing condition of the sealing packing. If the packing gland is too loose and properly pressed, remove the old packing and replace it with a new one every month of operation.
(7)If the pump stops for a long time in winter, measures should be taken to avoid damaging the pump components due to liquid freezing.
7. Possible faults and solutions of the slurry pump
Table 1-2 slurry pump faults and solutions

## Slide 5
【Text】

## Slide 6
【Words and phrases】

## Slide 7
【Course practice】