## Slide 1: 机电工程专业英语
2.3 MILLING OPERATIONS
铣削加工

## Slide 2
【Text】
After lathes, milling machines are the most widely used for manufacturing applications. In milling, the work piece is fed into a rotating milling cutter, which is a multi-edge tool as shown in Fig.1-1. Metal removal is achieved through combining the rotary motion of the milling cutter and linear motion of the workpiece simultaneously.
Figure 1-1 Schematic diagram of a milling operation
Each of the cutting edges of a milling cutter acts as an individual single- point cutter when it engages with the workpiece metal. Therefore, each of those cutting edges has appropriate rake and relief angles. Since only a few of the cutting edges are engaged with the work piece at a time, heavy cuts can be taken without adversely affecting the tool life. In fact, the permissible cutting speeds and feeds for milling are three to four times higher than those for turning or drilling. Moreover, the quality of surfaces machined by milling is generally superior to the quality of surfaces machined by turning, shaping, or drilling.
As far as the directions of cutter rotation and work piece feed are concerned, milling is performed by either of the following two methods.

## Slide 3
【Text】
(1)Up milling (conventional milling)
In up milling the cutting tool rotates in the opposite direction to the table movement, the chip starts as zero thickness and gradually increases to the maximum size as shown in Fig. 1-2a. This tends to lift the workpiece from the table. There is a possibility that the cutting tool will rub the workpiece before starting the removal. However, the machining process involves no impact loading, thus ensuring smoother operation of the machine tool.
The initial rubbing of the cutting edge during the start of the cut in up milling tends to dull the cutting edge and consequently have a lower tool life. Also since the cutter tends to cut and slide alternatively, the quality of machined surface obtained by this method is not very high. Nevertheless, up milling is commonly used in industry, especially for rough cuts.
(2)down milling (climb milling)
In down milling the cutting tool rotates in the same direction as that of the table movement, and the chip starts as maximum thickness and goes to zero thickness gradually as shown in fig.1-2 b.
(a)up milling (b)down milling
Fugure 1-2 milling methods

## Slide 4
【Text】
The advantages of this method include higher quality of the machined surface and easier clamping workpieces, since cutting forces act downward. Down milling also allows greater feeds per tooth and longer tool life between regrinds than up milling. But, it cannot be used for machining castings (see. Fig.1-3) or hot rolled steel, since the hard outer scale will damage the culler.
Figure 1-3 Castings
There are a large variety of milling cutters to suit specific requirements. The cutters most generally used, shown in Fig.1-4, are classified according to their general shape or the type of work they will do.
Plain milling cutters
They are basically cylindrical with the cutting teeth on the periphery, and the teeth may be straight or helical, as shown in Fig.1-4a. The helical teeth generally are preferred over straight teeth because the tooth is partially engaged with the workpiece as it rotates. Consequently, the cutting force variation will be smaller, resulting in a smoother operation. The cutters are generally used for machining flat surfaces.
Face milling cutters
They have cutting edges on the face and periphery. The cutting teeth, such as carbide inserts, are mounted on the cutter body as shown in Fig.1-4b.

## Slide 5
【Text】
Most larger-sized milling cutters are of inserted-tooth type. The cutter body is made of ordinary steel, with the teeth made of high speed steel, cemented carbide, or ceramics, fastened to the cutter body by various methods. Most commonly, the teeth are indexable carbide or ceramic inserts.
Slitting saws
They are very similar to a saw blade in appearance as well as function (Fig. 1-4c). The thickness of these cutters is generally very small. The cutters are employed for cutting off operations and deep slots.
Side and face cutters
They have cutting edges not only on the periphery like the plain milling cutters, but also on both the sides (Fig. 1-4d). As was the case with the plain milling cutter, the cutting teeth can be straight or helical.
Angle milling cutters
They are used in cutting dovetail grooves and the like. Figure 28.4e indicates a milling cutter of this type.
T-slot cutters
T-slot cutters (Fig.1-4f) are used for milling T-slots such as those in the milling machine table.
Figure 1-4.Types of milling cutters

## Slide 6
【Text】
End mills.
There are a large variety of end mills. One of distinctions is based on the method of holding, i. e., the end mill shank can be straight or tapered. The straight shank is used on end mills of small size. The tapered shank is used for large cutter sizes. The culler usually rotates on an axis perpendicular to the workpiece surface.
Figure 1-4g shows three kinds of end mills. The cutter can remove material on both its end and its cylindrical culling edges. Vertical milling machines and machining centers can be used for end milling of various sizes and shapes.

## Slide 7
【Words and phrases】

## Slide 8
【Course practice】