## Slide 1: 机电工程专业英语
1.4 MOULD DESIGN AND MANUFACTURING
模具设计及制造

## Slide 2
【Text】
I.Introduction to Mould
Mould is a fundamental technological device for industrial production. Industrially produced goods are formed in moulds which are designed and built specially for them. The mould is the core part of manufacturing process because its cavity gives its shape. There are many kinds of mould, such as casting & forging dies, ceramic moulds, die-casting moulds, drawing dies, injection moulds, glass moulds, magnetic moulds, metal extruding moulds, plastic and rubber moulds, plastic extruding moulds, powder metallurgical moulds, compressing moulds, etc.
Compression Moulding
Compression moulding is the least complex of the moulding processes and is ideal for large parts or low-quantity production. For low-quantity requirements it is more economical to build a compression mould than an injection mould. Compression moulds are often used for proto-typing, where samples are needed for testing fit and forming into assemblies. This allows for further design modification before building an injection mould for high-quantity production. Compression moulding is best suited for designs where tight tolerances are not required.

## Slide 3
【Text】
Fig.1-1 A Compression Mould 1. top plate；2. opening bar slot；3. handle；4. dowel pin & bushing；5. flash & tear trim gate；6. part cavity；7. bottom plate.
Injection Moulding
Injection moulding is the most complex of the moulding processes. Due to the more complex design of the injection mould, it is more expensive to purchase than a cast or compression mould. Although tooling costs can be high, cycle time is much faster than other processes and the part cost can be low, particularly when the process is automated. Injection moulding is well suited for moulding delicately shaped parts because high pressure (as much as 29 000psi) is maintained on the material to push it into every corner of the mould cavity.
(a) Horizontal Type (b) Vertical Type
Fig.1-2 An Injection Mould
1.injection runner；2. nozzle bushing；3. stripper bolt；4. top plate；5. sprue；6. opening bar slot；7. bottom plate；8. flash & tear trim gate；9. part cavity；10. dowel pin and bushing；11. ejector；12. fixed plate；13. movable plate.

## Slide 4
【Text】
Cast Moulding
There are two types of casting, open casting and pressure casting. With open casting, the liquid mixture is poured into the open cavity in the mould and allowed to cure. With pressure casting, the liquid mixture is poured into the open cavity, the cap is put in place and the cavity is pressurized. Pressure casting is used for more complex parts and when moulding foam materials.
Extrusion Moulding
Although extrusion moulds are quite simple the extrusion moulding process requires great care in the setting up and manufacture and final processing to ensure consistency of product. Pressure is forced through the die plate that has the correct profile cut into it. Variations in feed rate, temperature and pressure need to be controlled.
II. Mould Design and Manufacturing
CAD and CAM are widely applied in mould design and mould making. CAD allows you to draw a model on screen, then view it from every angle using 3-D animation and, finally, to test it by introducing various parameters into the digital simulation models. CAM, on the other hand, allows you to control the manufacturing quality. The advantages of these computer technologies are legion: shorter design times (modifications can be made at the speed of the computer), lower cost, faster manufacturing, etc. This new approach also allows shorter production runs, and to make last-minute changes to the mould for a particular part. Finally, also, these new processes can be used to make complex parts.

## Slide 5
【Text】
Computer-Aided Design (CAD) of Mould
Traditionally, the creation of drawings of mould tools has been a time-consuming task that is not part of the creative process. Drawings are an organizational necessity rather than a desired part of the process.
Computer-Aided Design (CAD) means using the computer and peripheral devices to simplify and enhance the design process. CAD systems offer an efficient means of design, and can be used to create inspection programs when used in conjunction with coordinate measuring machines and other inspection equipment. CAD data also can play a critical role in selecting process sequence.
A CAD system consists of three basic components: hardware, software, users. The hardware components of a typical CAD system include a processor, a system display, a keyboard, a digitizer, and a plotter. The software component of a CAD system consists of the programs which allow it to perform design and drafting functions. The user is the tool designer who uses the hardware and software to perform the design process.
Detailing the functional components and adding the standard components complete the mould (as shown in Fig.1-3). This all happens in 3-D. Moreover, the mould system provides functions for the checking, modifying and detailing of the part. Already in this early stage, drawings and bill of materials can be created automatically.
Fig.1-3 3-D Solid Model of Mould

## Slide 6
【Text】
Through the use of 3-D and the intelligence of the mould design system, typical 2-D mistakes—such as a collision between cooling and components/cavities or the wrong position of a hole—can be eliminated at the beginning. At any stage a bill of materials and drawings can be created—allowing the material to be ordered on time and always having an actual document to discuss with the customer or a bid for a mould base manufacturer.
Computer-Aided Manufacturing (CAM) of Mould
One way to reduce the cost of manufacturing and reduce lead-time is by setting up a manufacturing system that uses equipment and personnel to their fullest potential. The foundation for this type of manufacturing system is the use of CAD data to help in making key process decisions that ultimately improve machining precision and reduce non-productive time. This is called as computer-aided manufacturing (CAM). The objective of CAM is to produce, if possible, sections of a mould without intermediate steps by initiating machining operations from the computer workstation.

## Slide 7
【Words and phrases】
I
Mould n. 模具，模(型)，模塑，压模
Cavity n. 模腔，型腔，空洞
Die n. 模(子，片，具)，压模，塑模
casting & forging die 铸、锻模
ceramic mould 陶瓷模
die-casting mould 压铸模
drawing die 拉丝模
injection mould 注塑模
magnetic mould 磁铁成形模
extruding mould 挤压成形模
powder metallurgical mould 粉末冶金模
compressing mould 冲压模
moulding n. 成型
proto-typing 初始制模
assembly n. 装配件，组件
tolerance n. 公差，容许
affordable adj. 提供得起的
fasten v. 连接，固定，夹紧
secure v. 固定，紧固
ejector n. 脱模销，推顶器
runner n. 浇道，流道
Sprue n. 流道，浇道
parting line 合模线，拼缝线
core n. 模芯，中间层
cure v. 固化，塑化
urethane n. 聚氨酯
abrasion n. 磨蚀，磨损
flex fatigue 弯曲疲劳
insert n. 插件，嵌件
pin n. 销，杆
tool steel 工具钢
maraging steel 马氏体时效钢
porosity n. 多孔性，有孔性
venting hole 排气孔，通风孔
evacuate v. 排出，抽空
autoclave n. 高压釜
salt bath curing system 盐浴固化系统
silicone extrusion 硅橡胶挤压

## Slide 8
【Words and phrases】
II
Animation n. 动画
digital simulation model 数字模拟模型
legion n. 多，大批，无数
peripheral adj. 外围的，周边的
split adj. 分割的，对分的
run-off n . 流出口，流放口
shut-off n. 截流，断流
ejection system 脱模系统，缷料装置
collision n. 打击，碰撞
tedious adj. 沉闷的
lead-time n. 研制周期
tool-path n. 方法路径
CNC 计算机数字控制
Redundant adj. 多余的，冗余的
in a nutshell 总之

## Slide 9
【Course practice】
Complex Sentence Analysis
(1) Although tooling costs can be high, cycle time is much faster than other processes and the part cost can be low, particularly when the process is automated.
① tooling costs：模具成本
② particularly when the process is automated：条件状语从句放在后面，用于进一步说明，译为：尤其当工艺过程为自动操作时
【译文】虽然模具成本可能很高，但其制造周期短，比其他工艺过程快得多，零件成本会很低，尤其是当工艺过程为自动操作时。
(2) Injection moulding is well suited for moulding delicately shaped parts because high pressure (as much as 29000psi) is maintained on the material to push it into every corner of the mould cavity.
① is well suited for：最适合用于
② delicately shaped parts：外形精致的零件
③ psi：英制压力单位，磅/平方英寸
【译文】注射成型非常适合成型形状精致的零件，因为在材料上的高压(高达29000磅/平方英寸)会将其推入到模腔的每个角落。
(3) Since the mould materials have no natural porosity and the molten metal rapidly flows into the mould during injection, venting holes and passageways must be built into the moulds at the parting line to evacuate the air and gases in the cavity.
① since引导状语从句，表示原因，译为由于……
② venting hole：排气孔
③ parting line：合模线
【译文】由于模具材料没有天然孔隙，在注射过程中，当熔融金属迅速流入模具时，必须在模具的合模线上建立排气孔和通道，以排出型腔中的空气和其他气体。
(4) Although extrusion moulds are quite simple the extrusion moulding process requires great care in the setting up and manufacture and final processing to ensure consistency of product.
① in the setting up and manufacture and final processing：在建立、制造和最终加工过程中
② to ensure consistency of product：以确保产品的一致性，表示目的
【译文】虽然挤出模具相当简单，但在挤出成型过程中，设置、制造以及最终加工中需要非常小心，以确保产品的一致性。

## Slide 10
【Course practice】
Complex Sentence Analysis
(5) CAD allows you to draw a model on screen, then view it from every angle using 3-D animation and, finally, to test it by introducing various parameters into the digital simulation models (pressure, temperature, impact, etc.).
① draw，view和test表示3个并列的操作。
② digital simulation model：数字模拟模型。
【译文】CAD软件使你能在屏幕上绘制模型，然后用3d动画从各个角度查看它，最后通过将各种参数引入数字仿真模型(压力，温度，冲击等)来测试它。
(6) At any stage a bill of materials and drawings can be created—allowing the material to be ordered on time and always having an actual document to discuss with the customer or a bid for a mould base manufacturer.
① a bill of materials：材料清单。
② allowing和having引导两个现代分词短语，做伴随状语。
【译文】在任何阶段都可以创建材料清单和图纸，以便按时订购材料，并始终有实际的文件与客户讨论或为模具基础制造商投标。
(7) The objective of CAM is to produce, if possible, sections of a mould without intermediate steps by initiating machining operations from the computer workstation.
① if possible：插入语，译成：如可能，是if it is possible的省略语，试比较：
If possible, I will visit you in Chicago next month.
I will lend you some money to help you with the present difficulty if possible.
② by：通过……方式。
【译文】CAM（计算机辅助制造）的目标是生产制造，如果可能的话，部分模具在计算机工作站就可以开始加工，而省略中间环节。

## Slide 11
【Course practice】
Complex Sentence Analysis
(8) With the emphasis in the mould making industry today on producing moulds in the most efficient manner while still maintaining quality, mould makers need to keep up with the latest software technologies-packages that will allow them to program and cut complex moulds quickly so that mould production time can be reduced.
① with：译为：随着……，引导的介词短语作状语，修饰整个句子。试比较：
With the development of the economy in China, the people around the country are living a happy life.
② in the most efficient manner饰producing moulds。
③ keep up with：紧跟。
④ that：在这里引导了一个宾语从句，修饰前面的 software technologies-packages。
【译文】由于当前模具制造行业强调要以最高效的方式生产制造的同时，还要保持质量，模具制造商们则需要获取最新的技术软件包，使他们能够快速编程和切割复杂模具，从而减少模具生产时间。