## Slide 1: 机电工程专业英语
2.6 CAE/CIMS

## Slide 2
【Text】
I.CAE
CAE made it possible to achieve a decisive improvement in mold design, to optimize the process, and, above all, to improve and speed up the design of injection molds.
Simulation Software Simplifies Injection Mold Design
C-MOLD, as one of simulation software, is a set of integrated CAE (computer aided engineering ) simulations for plastics molding processes, including injection molding filling, post-filling, and cooling; part shrinkage and warpage; co-injection molding; gas-assisted injection molding, reactive molding; blow molding; thermoforming; injection/compression molding; and microchip encapsulation. C-MOLD provides solutions in all stages of design and manufacturing, to improve productivity and enhance part quality. Key features include a motif graphical user interface; a sophisticated geometry modeler and finite-element mesher tailored to plastics applications; seamless integration with major CAD and structural CAE applications; a polymer database containing over 11 000 materials; CAE analyses that provide critical information for optimizing part, mold, and process design in plastics molding operations; and an easy-to-use data visualizer for viewing analysis results.
Simulation Software Simplifies Progressive Die Design
In this era of global warp speed and virtual reality, calculating the deep draws of progressive dies or the spring-back of metal is performed by simulation software instead of the earlier trial-and-error method. These software programs essentially replace the artistic methods of die-making with scientific formulas. For more than a decade tool engineers have been designing parts, progressive die sequences, and dies and detailing cutter paths as a continuous process using computer-aided design (CAD).

## Slide 3
【Text】
Progressive die design used to be considered as just a road map for the die-maker during the build process. First the form stations were cut and given to the assembly department to be mounted on the die shoes. Later the die was taken to the press, where tryout began. This process was labor- intensive and required many hours of press time.
Today die-makers begin building by running simulations on the part without webs attached. The simulations are done for the forming stations of the die, such as draw stations, flange stations, and restrike stations. Two tools in the software, the forming limit diagram (FLD) and the thickness plot, then are evaluated to determine if the process can produce a part without fractures or wrinkles.
The FLD shows points plotted on two curves that are created from the material properties. All points should fall into the area below the first curve. Points above the first curve and below the second are in the marginal zone, areas of the part that are prone to fractures. For parts in this zone, any variation in the process-such as material property changes, thickness changes, or even a change in lubrication-could cause part failure. Points above the second curve are fractures in the part.
Designing Carrier Webs
Today, a web is taken out of the CAD design and set up in the simulation with locator pins in the pilot holes. The locator pins lock that area of the web so that it will not move during the simulated press stroke.

## Slide 4
【Text】
The remaining webs react by stretching as they will be in the real press, which shows where clearances are needed in steels for the movement of the stretch webs. They must have adequate stretch to allow the part to form, but enough strength to advance the part through the tool.
With today's forming simulations, the blanking and trimming stations are developed virtually. The finished-part geometry is projected onto the simulation result, and the software reverses the forming process, producing a part that becomes what is cut for the final trim steels.
Virtual tryout allows the whole tool to go directly into machining and assembly. With this process, the die-maker knows that the die can produce the part when it is in the press. The die-maker then adjusts the part to bring it into tolerance.
Under Pressure
Simulation software can accurately calculate how much pressure will be required to hold the part for each of the forming stations, thus allowing an accurate estimate of the number of nitrogen cylinders that are required. This is important because if the pressure is too low, the binder may gap, which might cause uncontrolled material flow, thinning, or wrinkles in the part. On flange stations, if the pressure is incorrect, the center of the part may bow upward, which causes spring- back in the flange walls.

## Slide 5
【Text】
Reducing tryout Time
While simulation software will not tell the die-maker how to build the tooling, it will accurately predict the result of the chosen process and help the designer develop a robust process to produce the part.
When coupled with a solid modeling CAD program, the software allows a virtual construction and tryout of the die in the computer before any steel is sent to the CNC machining center. This allows for the complete assembly of 95 percent of all tools before they make the first hit, greatly reducing the amount of tryout time.
II. CIMS
Computer integrated manufacturing (CIM) is the term used to describe the most modern approach to manufacturing. Although CIM encompasses many of the other advanced manufacturing technologies such as computer numerical control (CNC), CAD/CAM, robotics and just-in-time (JIT) delivery, it is more than a new technology or a new concept. Computer integrated manufacturing is actually an entirely new approach to manufacturing or a new way of doing business.

## Slide 6
【Text】
To understand CIM, it is necessary to begin with a comparison of modem and traditional manufacturing. Modem manufacturing encompasses all of the activities and processes necessary to convert raw materials into finished products, deliver them to the market and support them in the fields. These activities include the following.
(1) Identifying a need for a product;
(2) Designing a product to meet the needs;
(3) Obtaining the raw materials needed to produce the product;
(4) Applying appropriate processes to transform the raw materials into finished products;
(5) Transporting product to the market;
(6) Maintaining the product to ensure a proper performance in the field.
This broad, modem view of manufacturing can be compared with the more limited traditional view that focuses almost entirely on the conversion processes. The old approach separates such critical pre-conversion elements as market analysis research. development, and design for manufacturing, as well as such after-conversion elements as product delivery and product maintenance. In other word, in the old approach to manufacturing. only those processes that take place on the shop floor are considered manufacturing. This traditional approach of separating the overall concept into numerous specialized elements alone was not fundamentally changed with the advent of automation. While the separate elements themselves became automated (i.e. computer aided drafting and design and CNC in machining). they remained separate. Automation alone did not result in the integration of these islands of automation

## Slide 7
【Text】
With CIM, not only are the various elements automated. but also the islands of automation are all linked together or integrated. Integration means that a system can provide complete and instantaneous sharing of information. In modem manufacturing, integration is accomplished by background computers. With this CIM can now be defined as the total integration of all manufacturing elements through the use of computers.
Furthermore, such an illustration can show that research, development, design, marketing, sales, shipping, receiving, management and pre-execution personnel all have instant access to all information generated in this system. This is exactly the inside meaning of a CIM system. Progress is being made toward the eventual realization of CIM in manufacturing. When this is accomplished. fully integrated manufacturing firms will realize a number of benefits from CIM:
(1) Product quality increases;
(2) Lead time is reduced;
(3) Direct labor costs are reduced;
(4) Product development time is reduced;
(5) Inventories are reduced;
(6) Overall productivity increases;
(7) Design quality increases.

## Slide 8
【Words and phrases】
I.
Microstructure n. 微观结构
thermo-mechanics 热力学
ultimate adj. 最终的，根本的
mathematical modeling 数学建模
computer simulation 计算机模拟
in view of 由于，考虑到
utilization n. 利用
computer aided engineering ( CAE ) system 计算机辅助工程系统
discontinuous adj. 不连续的，间断的
process parameter 工艺参数
speed up 加速
groundwork n. 地基，基础
parallel adj. 平行的，相同的，类似的
metrology n. 度量衡学，测量学
thermoplastic adj. 热塑性的
decisive adj.决定性的
optimize v. 使最优化
above all 最重要，首先
injection molding filling 注射成型填充（模拟）
post-filling 保压（模拟）
cooling n. 冷却（模拟）
part shrinkage and warpage 制品收缩与翘岗（模拟）
co-injection molding 共注成型（模拟）
gas assisted injection molding 气辅注射成型（模拟）
reactive molding 反应成型（模拟）
Thermoforming n. 热成型（模拟）
injection/compression molding 压注成型（模拟）
microchip encapsulation 微芯片封装（模拟）
key feature 主要特点
motif graphical 功能图形
user interface 用户界面
geometry modeler 几何图形建模器
finite-element mesher 有限元网格划分器（模块），剖分（模 块）
seamless integration with major CAD and structural CAE applications polymer 具有主要CAD软件和结构化CAE软件应用的无缝集成
database data 材料（性能）数据库
visualizer 数据可视化（功能模块）

## Slide 9
【Words and phrases】
lease v. 出租，租出
in-house program 内部程序
engineering consulting office 工程咨询机构
progressive die 渐进模具：一种用于金属冲压加工的工具
warp speed 高速飞驰
trial-and-error method 反复试验法
computer-aided design (CAD) 计算机辅助设计
road map 路线图
forming limit diagram (FLD) 形成膨极限图
thickness plot 料厚变化图
fall into 位于
be prone to 易于
locator pin 定位销
pilot hole 定位孔
be projected onto 投射在
be coupled with 加上
Computerized Numerical Control (CNC) 计算机数字控制
machining center 加工中心
II.CIMS
computer integrated manufacturing ( CIM ) 计算机集成制造
encompass v. 包围,环绕
computer numerical control ( CNC ) 计算机数控
just-in-time ( JIT) 即时交货
delivery n. 递送.交付
more than... or... 与其说……还不如说
convert v. 转变.变换
raw material 原料
finished product 成品，产品
identify v. 认出，识别
appropriate adj. 适当的
maintain v. 维持，保持
ensure v. 保证
performance n. 履行，执行
be compared with.. 与……比较
product maintenance 产品维护
on the shop floor 车间一线；工作现场
advent n. 出现，到来
integrated adj. 整合的，完整的
instantaneous adj. 瞬间的，即刻的
modern manufacturing 现代制造业
accomplish v. 实现，完成
background n. 背景，后台
inventory n. 详细目录

## Slide 10
【Course practice】
Complex Sentence Analysis
(1) CAE made it possible to achieve a decisive improvement in mold design, to optimize the process, and, above all, to improve and speed up the design of imection molds.
make it possible to do…译为”使做…成为可能"。
句中"it”为形式宾语，真正的宾语是“to achieve a decisive improvement in mold design, to optimize the process, and, above all, to improve and speed up the design of injection molds”.
译：CAE使得在模具设计方面取得决定性的进步成为可能，使工艺过程最优化，尤其是改进和加速了注射模具设计。
(2) Simulation software can accurately calculate how much pressure will be required to hold the part for each of the forming stations, thus allowing an accurate estimate of the number of nitrogen cylinders that are required.
本句为宾语从句，句中“calculate"后接从句"how much pressure will be required to hold the part for each of the forming stations“，而由“thus”引导出的结构为伴随状语，说明前部分。.
译：仿真软件能够准确地计算出每一个成形工位上支撑零件所需的压力大小，从而可以准确地估计出所需氮气缸的数量。
(3) Although CIM encompasses many of the other advanced manufacturing technologies such as computer numerical control (CNC) . CAD/CAM. robotics and just-in-time (JIT) delivery, it is more than a new technology or a new concept.
句型：more…than…译为”与其说，还不如说”：句中more than... or...译为“大(多.甚)过……或……,不止(只,仅)……或……,不只是……或……"。
译：虽然CIM包括许多如计算机数控(CNC)、CAD/CAM,机器人技术和即时（JIT）交货等其他的先进制造技术，但不仅仅是一种新技术或新概念。

## Slide 11
【Course practice】
(4) Modern manufacturing encompasses all of the activities and processes necessary to convert raw materials into finished products, deliver them to the market. and support them in the fields.
本句属于necessary to do...句型，为形容词短语作后置定语修饰“activities and processes”，意思是“做……所必需的“convert... into…”译为“把……转换成……”。
译：现代制造包括了把原材料转换成产品、把产品投向市场和进行技术支持所必需的一切活动和过程。
(5) This traditional approach of separating the overall concept into numerous stand-alone specialized elements was not fundamentally changed with the advent of automation.
动名词短语separating the overall…与介词一起构成后度定语修饰"approach"。
译：这种将整体概念分离为许多独立的专门元素的传统方法并没有随着自动化的出现而从根本上改变。
(6) Automation alone did not result in the integration of these islands of automation.
译：自动化本身并没有使这些自动化孤岛完成整合。
(7) With this CIM can now be defined as the total integration of all manufacturing elements through the use of computers.
译：借助这种CIM，现在可以将之定义为通过使用计算机对所有制造要素进行全面集成。