## Slide 1: 机电工程专业英语
1.2 CENTRIFUGE
离心机

## Slide 2
【Text】
1.General description
Type LW400-NY-G and LW500-NY centrifuges (brief for the two-type centrifuges) are special devices to separate solid phase from well drilling liquid, which are new generation type developed and designed according to the actual demands of oil drilling and on the base of studying current domestic and foreign centrifuges. The max. disposal of type LW500-NY may reach 60 m3/h which make the well drilling liquid higher quality and shorten the time of liquid disposal. Without disassembling the belt wheel, type LW400-NY-G centrifuge can complete the transformation from slow speed to high speed only using one belt wheel, i.e. the drum can complete two rotating speed:1800r/h and 2400r/h. This solve the problem of choosing different centrifuge to match different well drilling mine shaft. Hard alloy is inlayed in the conveyor vaes of the two-type centrifuges lengthening their using life several times.
2.Application
The two-type centrifuges mainly used to control the density and viscosity, to reduce the solid content of well drilling liquid, to remove the harmful solid phase or recover barite, and to recover and reuse the bottom flow so as to guarantee the high performance of well drilling liquid and raise drilling speed.
After the well drilling liquid is processed, not only the density and the viscosity are controlled, its sand content is also cut down greatly. Therefore, the machine using life is extended. The economic benefit and social benefit are obviously obtained.
Because the two-type centrifuges have features of reasonable design, good adaptability, high processing volume, easy operation and convenience of maintenance, and timely supply of parts, they are very popular with customers.

## Slide 3
【Text】
3.Main technical parameters
3.1 Description of machine type
3.2 Main parameters
Construction & Working principle
4.1Construction
The two-type centrifuges consist of main motor, coupler, differential, drum assembly, upper cover of plough, body of plough, auxiliary motor, isolated anti-exploration control unit, General base and other auxiliary equipment. (Drawing 1)
4.1.1 Drum assembly
Drum assembly consists of straight drum, corn drum, flange shaft with big and small end, conveyor, and other parts. Straight drum, corn drum and conveyor are concentrically fixed on the both end bearing base of plough through flange shaft. The spline of the differential is connected with the spline Jacket of the conveyor through spline shaft. The shell is driven by the flange shaft which connects the big flange and drum assembly. Various speed can be obtained through adjusting therotating speed of input shaft of the differential. There are 6 adjustable overflow plates on the flange of big flange shaft. The subsidence area will be controlled through changing the covering area of the damper one overflow hole, thus the separating result will be changed.

## Slide 4
【Text】
The conveyor consists of column & corn drum body, closure, rail splice, screw vanes welding assembly, flange shaft, spline and spline shaft. The screw vanes are evenly welded on the drum body. The vanes are inlayed hard alloy, so that wearability of vanes is raised and the using life is extended. There are 26 holes(F50mm) on the corn drum (LW400-NY-G22,LW500-NY26). Wear-resisting alloy is sprayed on the circle of the holes. The spline Jacket is connected with the spline on the column drum section.
4.1.2 Differential
This differential is involute epicycilc gear type. It consists of two stage epicyclic gear. The surface of sun and epicyclic gears are hard processed, so that they have higher ability of bearing load. One safe bolt is placed on the input shaft end. When the push torque of conveyor is overload, the bolt will be cut down and the drum will be synchronous running with the conveyor and thus the centrifugal will be protected. Before restarting, the bottom end cover should be open and replace new bolt.
4.1.3 Electric control unit
Interlocking unit is adopted to control both main and aux.motors. When starting the machine, the aux.Motor should be started firstly and then the main motor will be started in 20 seconds. When stopping the machine, the main motor stops while pressing the button, the interlocking unit will automatically cut down the aux.Motor in 30 seconds after the main motor stops. Meanwhile, a special anti-exploration breaker is provided slush-supplying pump.

## Slide 5
【Text】
4.2 Working principle (see Drawing III attached)
The well drilling liquid to be processed is sent to the input pipe of the drum small end by slush supplying pump and then to the liquid chamber, finally into drum through the suction of conveyor. The solid phase of well drilling liquid, on the action of centrifugal force produced by the drum rotation at high speed, is thrown to the drum inner wall and subside down. Meanwhile, the conveyor, driven by the output spline of differential, rotates as the same direction as the drum, however conveyor speed is a little slower than the drum. In this case, the speed difference is formed between the drum and the conveyor. The conveyor scrapes subsided slag on the inner wall of the drum and pushes them to the dry zone at the small end of the drum. The slag is drained from the slag outlet to slag land. The separated well liquid will overflow from the overflow port at the big end of drum and them drain out through the discharging hole on the plough. Now the separation has realized.
5.Parameters of attached device
5.1 Slush supplying pump
5.1.1 Main parameters of slush supplying pump

## Slide 6
【Text】
5.1.2 performance
Slush supplying pump supplies slush for the centrifuge, which is desirable device to deliver fluid containing solid fiber impurity slush. It has features as high efficiency, energy saving, low noises table vibration etc.
5.2 Hydraulic coupler
5.2.1 Main technical parameters
5.2.2 Performance
It is a power delivery device by using hydraulic delivery, which has features of steady start with load. lt can improve motors starting performance and protect motor when overload. lt can also isolate twisting vibration and impact.

## Slide 7
【Text】
5.2.3 Notes in the operation
a. The wording temperature is not over 90OC
b. it is not allowed to open the eutectic plug so as not to occur scald accident.
c.It is not allowed to change the wording liquid medium of coupler randomly. Any filling should be done strictly in accordance with specific regulation.
d.Do not disassemble the coupler randomly so as not to break sealing ring and balance precision.
e.To check the working oil quality after 3000 hours of running. The oil should be changed if it is found bad.
6.Installation & Adjustment
6.1 Centrifuge should be horizontally and firmly mounted on top of No.3 tank far from inlet of slush pump in the circulation system. The rotation center of drum should be consistent with liquid flow direction. lt can be arranged according to local actual condition as well.
6.2 Connect the slush supplying pump with pipe and put the pipe in No.2 tank. Connect circuit of slush supplying pump with anti-exploration switch.
6.3 The inclining angle of the slag draining land is not less than 60 degree, while the angle of the overflow pipe must be over 45 degree so that the bottom flow and the overflow can be drained out of centrifuge rapidly.
6.4 An additional power switch should be mounted beside the electric control box of the centrifuge. Do not use the control box of centrifuge as power switch, so as to cut down power when fault occurred.

## Slide 8
【Text】
7.Operation & Maintenance
Properly use and maintenance of centrifuge is the prerequisite of utilizing its excellent performance and extending its using life.
7.1 Preparation before start
Before starting a new or a long time no use centrifuge, be sure to check all parts.
7.1.1 To check if the fasten parts are loose and there is no object that influence rotating around the rotating parts.
7.1.2 To check the lubricant condition of all parts (new centrifuge has been fully filled before sale), and make sure that the oil volume of the bearing base and the oil level of the differential and the coupler reaches to the specified standard.
7.1.3 To check tightness of triangle belt or narrow v-belt: Use hand to turn main motor wheel for 3 cycles and then check in there is block and unusual sound. The tightness of v-belt should be proper.
7.1.4 For long time no use centrifuge, firstly open the dear water valve ,and then clean the drum and conveyor, restart it when there is no block inside.
7.2 Start running
7.2.1 Turn off power switch, press the button of aux.Motor and (hen check if there is unusual sound,20 seconds late, press the button of main motor. And then check the rotating direction for both motors. If the rotation direction is wrong, stop to adjust it.

## Slide 9
【Text】
7.2.2 After the centrifuge has been running well without load for 10 to 15 minutes, start the slush supplying pump, and open the control valve from small to big until the supplying volume is proper.
7.2.3 Viscosity is one of the important factor of influencing the separating ability. Filling water may speed up the subsidence of solid phase. Open the water valve for dilution when the viscosity is too high(normal 30 to 40 second).The value of dilution water is normal 15 to 201/min.
7.2.4 To check the running condition regularly. If there is unusual high temperature in some part, unusual sound or pipe leakage has been found, make the reason clear and rectify it.
7.2.5 Efficient vibration or other abnormal appearance had been found, shut down power at once, stop slush supplying, close slush pump and valve, open water valve and clean drum and conveyor
7.3 Stop running.
7.3.1 Close slush pump and open water valve.
7.3.2 Keep centrifuge running for 10 to 15 minutes. When the slag inside the drum has been completely washed out and clear water flow out, shut down slush valve and main motor. The aux.Motor will stop automatically in 30 seconds.
7.4 Maintenance
7.4.1 Before operation, operator must carefully understand the construction, performance and operating skill requirement, and let the machine run strictly in accordance with the operating rules and regulations.
7.4.2 Operator should regularly check the motor current and the bearing temperature, check the tightness of triangle belt, the temperature of the differential, the oil level of differential and coupler after machine stops.
7.4.3 The lubricant of main bearing and conveyor bearing
For No.2 lithium base grease. lt is necessary to fill every 100 hours running. The filling hole of the main bearing is on the bearing base, while the filling hole of the conveyor is on the flange shaft of big and small flange of drum.

## Slide 10
【Text】
7.4.4 The lubricant of differential
For No.15 or No.18 by hyperbolic gear lubricant.
The abrasive period for a new differential is 150 hours and then the gear oil must be' changed, and after then, the gear oil should be changed every 500 hours. The changing procedure is as following:
a)Drain out the old lubricant
b)Fill in 4kg diesel oil and put on oil cap
c)Turn on the differential by hand for several circles and then drain out the diesel oil.
d)Fill in 3 litre gear lubricant, which should be filtered by 80 to 100 mesh screen before filling.
e)Set the filling hole to level position. If the lubricant is overflow, it shows that the lubricant is enough.
7.4.5 The working oil of coupler
No.20 or lNo.30 turbine oil are adopted, after running 3000hours more or less, testing aging or changing oil is necessary.
7.4.6 Take care of the assembling marks when disassembling or assembling rotating parts. The assembling surface must be clean and no burr or object in order to keep its dynamic balancing precision.
7.4.7 It is not allowed to beat with metal when dismantling or assembling bearing so as not to influence its precision or to be broken. Be careful not to damage the sealing surface when disassembling sealing ring.
7.4.8 Check the electric connection regularly and check if nut outside the column is loose.

## Slide 11
【Text】
7.5 Warning
7.5.1 When using the machine in winter, check if it is frozen by turning the wheel manually if it is frozen, heat it with steam or other method. Remember to drain out the slush from the drum so as not to be frozen when stopping machine in winter.
7.5.2 It is not allowed to open drum cover or belt cover during running.
7.5.3 The flow volume does not exceed the processing capability of the centrifuge, or lead to overload or safety bolt cutting.
7.5.4 If the viscosity of well drilling liquid is too high, fill appropriate water for dilution so as to speed up the slush subsidence and raise the processing capability of the centrifuge.
7.5.5 Short phase running is prohibited.
8. Illustration of electric control
The main circuit diagram and control circuit diagram of the centrifugal pump are shown in Figures 1-1 and 1-2.

## Slide 12
【Text】
①Time accumulate organ ②time ③Assistant machine ④Main machine ⑤Liquid supplying pump
8.1 Press button SB1 to start aux.motor, 20 seconds later press SB3 to start main motor, meanwhile the chronography starts working to show the working times. The slush pumping system starts working.
8.2 After the washing is completed, press button SB2, shut down the main motor and the slush pump, the aux.motor keeps working for 30 seconds under the control of a time relay and then stop.
8.3 If you press SB1 button other than SB3 button, the aux.motor is only working for 30 seconds and then stop. If you firstly press button SB3, the main motor will not start because of the action of interlocking unit.

## Slide 13
【Text】
9.Possible fault & solution
The possible faults and their solutions that may occur during the use of centrifugal pumps are shown in table 1-4.

## Slide 14
【Text】
10.List of quick-wear parts & standard parts
The vulnerable parts and standard parts of centrifugal pumps are shown in table 1-5.
Table 1-5 List of vulnerable parts & standard parts

## Slide 15
【Text】
11.Accessories attached
The centrifugal pump accessories are shown in table 1-6.
Table 1-6 Accessories attached

## Slide 16
【Text】
12.Layout drawing (Drawing I)
As shown in figure 1-3, the assembly diagram of the centrifugal pump is shown in table 1-7, which shows the centrifugal pump model and minimum size parameters.
Fig.1-3 Centrifugal pump diagram
1. Differential 2.screw in oil bole 3.Body of plough 4.Oil cup 5.upper cover of plough 6.Drum assembly 7.Bearing base 8.slush-inlet assembly 9.Hydraulic coupler 10.Reducer11.Main motor 12.Anti-exploration control device 13Aux.motor 14.Bearing base 15.General base

## Slide 17
【Text】
13.structure drawing of differential(Drawing II)
The schematic diagram of the differential structure is shown in figure 1-4.
Fig.1-4 Structure drawing of differential
1.oil cup M8*l 2.Bearing end cover 3.Gear bearing 4.Safety bolt 5.Bearing cover 6.Bearing 213 7. Bearing 60213 8. Bearing body 9.Aux.belt
14.Structure drawing (Drawing lII)
The schematic diagram of the drum shaft assembly is shown in figure 1-5.
Fig.1-5 The overall structure of the device
1.Aux.belt 2.Differential 3.Connecting flange of the differential 4.Bearing base 5.Oil cup 6.Flange shaft with big end 7.Straight Drum 8.Conveyor 9.Upper cover of plough l0.Corn Drum 11.Bearing base 12.Main belt wheel 13.O-ring 14.Angular contact ball bearing 15.Ball-shape bearing in deep channel 16.inner cauda flange shaft 17.Ball Shape bearing in deep channel 18.Flange shaft with small end 19.Slag discharging port 20.Slush inlet pipe 21.Body of plough 22.Spline Jacket 23.Oil seal 24.O-ring 25.Slush outlet 26.Ball-shape bearing in deep channel 27.Gas-outlet screw 28.Short-cyliuder-shape rolling bearing 29.Spline shaft

## Slide 18
【Words and phrases】
disposal n. 处理，清除；（土地、财产等的）变卖，转让
disassembling n. 拆卸；反汇编v.拆开；分散（disassemble的ing形式）
belt wheel 皮带轮
transformation n. （彻底或重大的）改观，变化，转变
centrifuge n. 离心机v.用离心机分离；使……受离心作用
vae abbr. 醋酸乙烯-乙烯共聚乳液
viscosity n. 黏性；黏度
barite n. [矿物]重晶石
convenience n. 方便，便利；便利的事物，便利设施；公共厕所
screw n. 螺丝（钉）；螺杆，螺丝杆；螺旋桨
screw discharging centrifuge 螺旋卸料离心机
Auxiliary adj. 辅助的；备用的，后备的;n.助手，辅助人员；
Differential adj. 微分的；差别的；特异的;n.微分；差别
drum assembly [机] 摩擦鼓部件
plough v. 耕，犁；（用或仿佛用犁）划出（沟或线）
flange n. （机）法兰；（机）（古生）凸缘；轮缘；边缘;vt.给……装凸缘
therotating speed 穿引速度；引纸抄速
conveyor n. 传送带，传送装置；传播者，传达者

## Slide 19
【Course practice】
Complex Sentence Analysis
(1) The conveyor scrapes subsided slag on the inner wall of the drum and pushes them to the dry zone at the small end of the drum.
slag on随便穿上；胡乱涂上；断然拒绝
译：输送机将沉降渣刮落在滚筒内壁上，并将其推至滚筒小端干燥区。
(2) The slag is drained from the slag outlet to slag land.
Be drained from被抽干; drain 排出，滤干，喝光
译：渣从出渣口排至渣地。
(3) Centrifuge should be horizontally and firmly mounted on top of No.3 tank far from inlet of slush pump in the circulation system.
Be mounted on安装在：指某物被固定或安装在另一物体上。
far from远离：表示距离、程度或关系上相距甚远，不接近。
译：离心机应水平牢固地安装在3号槽顶部，远离循环系统的泥浆泵入口。