## Slide 1: 机电工程专业英语
2.5 CAD/CAM

## Slide 2
【Text】
If you are involves with CNC machines, you are probably involved with CNC programming CAD/CAM systems. CAD (Computer Aided Design) is widely used to describe any software capable of defining a mechanical component with geometry, surfaces, or solid models. CAM (Computer Aided Manufacturing) is software used to develop NC program.
Three different purposes
Engineering design and manufacturing uses CAD/CAM software for three distinctly different purposes:
Design modeling
A mechanical design engineer uses CAD software to create a part. This definition of the part can be called its model. This model can be represented as a drawing or a CAD data file.
A manufacturing engineer or NC programmer, uses CAD software to:
Develop a computer model of a part defined by a drawing.
Evaluate and repair the design CAD data to manufacturing tolerances.This is a surprisingly common task.
Create new part models from the original design to allow for manufacturability. This would include adding draft angles or developing models of the part for different steps in multi-process manufacturing

## Slide 3
【Text】
Design models of fixtures, mold cavities, mold cores, mold bases, and other tooling. An example of what manufacturing modeling needs to be done before a part can be machined NC Programming.
A manufacturing engineer or NC programmer uses CAM software to select tools, methods, and procedures to machine the models defined in the manufacturing modeling section described above.
In the beginning, there were only CAD systems. Engineers used only CAD systems to draw pictures of parts. The first CAM systems helped an NC programmer/machinist/manufacturing engineer program from these drawings. This making of drawings, and programming parts from drawings, was ( and still is ) time consuming and subject a lot of human error. Someone got the bright idea to eliminate this to-and-from drawing step, and integrated CAD/CAM was born.
Machining methods
You can cut imported CAD models two ways: Generate the tool path from the surfaces and tool geometry, applying edge protection to the surfaces, or generate the tool path directly from the solid, using Boolean operators and accounting for the sweep volume of the tool.

## Slide 4
【Text】
The second requires lots of calculations based on the intersection of the solids, because it has to be continuously calculated as the tool moves along. Because the math is complex, risk of error is high and the probability of gouging is much increased. It is common to generate 10 000 to 100 000 individual tool path moves, and an error in a single move stops machining altogether. Any compromise gives a bad finish.
No software or hardware wizardry can speed up NC programming if the CAM system uses an inefficient technique to generate tool paths. The most robust method tessellates the part into polyhedrons consisting of numerous triangles (facets or planes), where user-defined accuracy determines the number of facets. Finished part accuracy is typically between 0.0005 and 0.0001 inch, so the math solution to the intersection of tool shape and facets is quicker and more reliable than the formulas to generate tool paths directly from solid.
It’s easier to plan, organize and reorder cutting routines if your CAM system includes a module that lets you graphically cut and paste into an efficient operations manager. This sort of feature lets you view and recorder NC parameters associated with tool paths, and provides a history of machining strategies for family of parts programming. Tool, material and step-over settings used for one NC operation can be applied to different geometry for new tool paths generation.

## Slide 5
【Text】
Cutting features
Good math is only half of what a CAM system is about. The other half is good machining practice. Following are some features and methods for machining.
Gouge-free tool support
Today’s CAM systems should offer support for square-nosed, bull-nosed and ball-nosed end mills, with full gouge avoidance on each. Because each tool advantages in machining various shapes, the better systems do not limit the operator's choice of tools. Rough cutting with bull-nosed tools is faster and, depending on the job, can also be effective for finish cutting.
Surface edge protection
Individual shapes that make up a free-form surface or solid model may have gaps, and how they're handled differs among CAM systems. Some will simply add a straight line between the surfaces on either end of the gap, but this risks gouging. The more reliable method is to “edge protect” each of the individual surfaces. With this method the tool path is guaranteed not to gouge the interior or edges of surface.
Tool path bounding
The extent of the tool path should be limited to cut only a portion of the model. For quick tool path generation, the bounding needs to be done at tool path creation time rather than waiting until after the full tool path is generated. This is especially significant if a portion of the model is all you want to cut anyway.

## Slide 6
【Text】
a set boundary
Fixed-distance step-overs and scallop height control
CAM software should allow the user to specify a fixed distance between each cut, and specify the maximum scallop height and maximum surface tolerance. Then the software will calculate the proper step-over to develop the shortest possible NC code and fastest machining cycles.
Feed between moves
Tool path generation usually follows rows as it cuts the parts. When the tool comes to the end of a row, the CAM system decides how to position the tool at the start of the next row. Some use a simple “up and over” algorithm, but, watch out, this can gouge if the software doesn’t check first. To avoid gouging, better system will offer the option of following the part in the transition to the start of the next row.
The lead-in move positions the machine tool to the start of the first cutting row. The machinist needs a variety of options to engage and to leave the part gently, such as spiral, arc, and ramp motions, to guarantee they won't gouge.
Cutting methods
Cutting techniques for both solid and surface models are Z-level roughing, Z-level finishing, planar, single surface flow, multi-surface flow cutting (includes radial cutting), and project cutting. The machinist should have the option to specify various cutting methods for any portion of the model.

## Slide 7
【Text】
Z-level roughing is the most efficient way to remove the majority of excess material which slices a model with constant Z-level planes to generate spiral or zigzag paths. If there are overhanging areas on the part, you want the CAM system to avoid gouging with the shank of the tool as well as the tip.
Z-level finishing is the best way to finish areas of a part that are almost vertical. It is important that the operator be able to apply a boundary curve to limit the area of path generation.
Planar cutting is the oldest and most well-known method of cutting complex models. It allows the operator to generate parallel planar tool paths over any number of underlying surfaces. Current systems vary widely in the speed and quality of tool paths generated. Even systems that claim to generate gouge-free tool paths may gouge on complex shapes. If you are choosing a new CAM system, be sure to test it on the most complex part you're likely to cut.
Single-surface flow cutting leaves the best surface when a part's geometry is defined by only a few surfaces. It cuts only a single surface at a time, but the CAM system must be capable of gouge
checking that surface against any number of surrounding surfaces.

## Slide 8
【Text】
Multi-surface flow cutting is a powerful feature. For machining a boomerang-shaped part, or any part with a bend or a lot of bends, it is important that the CAM system can generate tool paths that flow along or across a specified flow surface while remaining essentially perpendicular to it. On a round, oval or odd-shaped part, mold or die, this feature lets you cut perpendicular to shape around the part's periphery, regardless of its shape. The machinist can control tool-path direction to produce the finest detail.
Projected cutting is useful when machining an irregularly shaped part with a particular 2D tool path, as for engraving. See Fig. 10-10. Your CAM system should be able to create this tool path, project it onto the complex model and cut-all with full gouge avoidance.

## Slide 9
【Words and phrases】
computer-aided design (CAD) 计算机辅助设计
computer aided manufacturing ( CAM ) 计算机辅助制造
computer-aided process planning ( CAPP ) 计算机辅助工艺计划(CAPP)
design terminal 设计终端
tape reader 磁带播放器
software package 软件包
be referred to as... 被称为，被认为是
module n. （机器、建筑物等的）组件，模件；（课程的）单元，模块
operating system 操作系统
be concerned with 关注，从事于，涉及
accumulate v. 积累，积攒
engineering analysis 工程分析
automatically Programmed Tool ( APT ) 自动编程工具(APT)
NC machine tool 数控机床
user program 用户程序
cutter n. 刀具，切割机；切割者
general-purpose software computer 通用软件计算机
graphics n. （商业设计或插图中的）图形；图样，图案制图学；制图法
bill of material 物料清单
detect v. 查明，察觉；测出，检测，识别
inconsistency n. 不一致；易变
wire frame 线框图：计算机图形学中的一种表示方法
solid modeling 实体建模；[计] 实体造型
boundary representation [计] 边界表示法
pattem n.模式，方式；图案，花样；v.用图案装饰，给……加上花样；仿照，模仿
cylinder n. 圆柱体，圆筒；汽缸
sphere n. 范围，领域；球体；vt.使……成球形；包围
cone n.圆锥体；圆锥形物；锥形路标
Boolean algebra 布尔代数
Symmetric adj. 对称的
process planning 工艺规划
geometric model 几何模型
on-line assembly 在线装配
execute v. 执行，实施；处决；完成
computer programming expert 计算机编程专家
cavity n.洞，腔；(牙齿的) 龋洞

## Slide 10
【Words and phrases】
gouge vt.用半圆凿子挖；欺骗；n.沟；圆凿；以圆凿刨
wizardry n.巫术，魔法
tessellate adj.镶嵌细工的；嵌成花纹的; vt.把……镶装花纹
slice n. （切下的食物）薄片，片; v.把……切成薄片；切，割，划
remote control 远程控制
square-nosed end mill ( cylindrical end mill) . 方头立铣刀(圆柱立铣刀)。
bull-nosed end mill 牛头立铣刀
Boolean operator 布尔运算算子
scallop height 残留高度
near-vertical slope 近乎垂直的斜率

## Slide 11
【Course practice】
Complex Sentence Analysis
(1) A manufacturing engineer or NC programmer uses CAM software to select tools, methods, and procedures to machine the models defined in the manufacturing modeling section described above.
制造工程师或数控编程员使用CAM软件选择刀具、加工方法和加工工序加工上述定义的制造模型。上述直译，改为意译：“为了加工上述定义的制造模型，制造工程师或数控编程员使用CAM软件选择刀具、加工方法和加工工序”，符合汉语的表达习惯。
(2) It is important that the operator be able to apply a boundary curve to limit the area of path generation.
该句为虚拟语气，故that后从句谓语系动词为原形be, 也可为should be。
译：操作员能够运用边界曲线限制刀具轨迹的生成区域是很重要的。