## Slide 1: 机电工程专业英语

## Slide 2
【Text】
I.The Computer Numerical Control (CNC) System
Numerical Control, NC for short, is an automatic control method on the machine using digitized signals (numeric and signs). The NC concept was proposed in the late 1940s by John Parsons of Traverse City, Michigan. Numerical Control (NC) is any machining process in which the operations are executed automatically in sequences as specified by the program that contains the information for the tool movements. ® In its earliest stages, NC machines were able to make straight cuts efficiently and effectively.
CNC machine tools are known as machine tools with numerical control technology. According to the 5th Technical Committee of International Federation for Information Processing (IFIP), CNC machine is a machine tool with procedures numerical control system, which can process the program prescript by specific code and other symbolic coding in a logic way.
Compared to the ordinary manual machine tools, the CNC machine operates automatically under the program control (processing instruction). When Numerical Control is performed under computer supervision; it is called Computer Numerical Control (CNC) (Fig. 1-1). CNC system has the computer system instead of a numerical control device. As defined by the EIA-owned CNC Standardization Committee, CNC is a computer with a stored program, performing some or all of a the NC device features according to the control program stored in the computer read/write memory; the only device outside computer is the interface. CNC system is composed of procedures, input and output devices, computer numerical control devices, programmable logic controller (PLC), the spindle drive and feed drive device.

## Slide 3
【Text】
Computers are the control units of CNC machines; they are built in or linked to the machines via communications channels. When a programmer inputs some information in the program by tap disk and so on, the computer calculates all necessary data to get the job done.
Fig.1-1 components of CNC
The Types of NC Machine
Since its introduction, NC technology has found many applications, including lathes and turning centers, milling machines and machining centers, punches, electrical discharge machines (EDM), flame cutters, grinders, and testing and inspection equipment. The most - complex CNC machine tool is the turning center (Fig. 1-2). And the machining center (MC) u (Fig. 1-3) (Vertical machining center, with the tool magazine on the left and the control panel on the right, which can be swiveled by tbe operator) and Horizontal machining center (Fig. 1-4) (Horizontal) machining center, equipped with an automatic tool changer). The EDM and flame cutter are special type of NC machines ( Fig. 1-5 and Fig.1-6).
Fig.1-6 a flame cutter machine

## Slide 4
【Text】
II.The Advantages and Disadvantages of CNC Machines
(1) The Advantages of CNC Machines
CNC machines have many advantages over conventional machines, some of them are as follows.
① There is a possibility of performing multiple operations on the same machine in one set-up.
② Because of the possibility of simultaneous multi-axis tool movement, special profile tools are not necessary to cut unusual part shapes.
③ The scrap rate is significantly reduced because of the precision of the CNC machine and lesser operator impact.
④ It is easy to incorporate part design changes when CAD/CAM systems are used.
⑤ It is easier to perform quality assurance by a spot-check instead of checking all parts.
⑥ Production is significantly increased.
(2) CNC Machines also have some Disadvantages
① They are quite expensive.
②They have to be programmed, set up, operated, and maintained by highly skilled personnel.
Obviously, CNC machines have more advantages than disadvantages. The companies that adopt CNC technology are increasing their competitive edge. As always with new technology, the cost per CNC unit is being cut further and more companies can afford CNC equipment, which enables them to answer the increasingly strong requirements for production speed and quality that competitive markets demand. In the future the broader use of CNC machines will be one of the best ways to enhance automation in manufacturing.

## Slide 5
【Text】
III.The Composition of CNC Machine Tools and Functions of Each Part
(1) CNC Machining Process
①Carry on the processing process study; determine the processing plan, technologiCal parameter and displacement data according to the pattern.
②Write the processing program to work part with the prescriptive code and format; or build the processing program file for parts with the automatic programming software, and perform the CAD/CAM work.
③Input or output the program. The manual-written program will be input on the NC machine operation panel; the program generated by software will be transferred through serial communication interface (such as RS232c etc.) of the computer to the numerical control unit of CNC machine tool.
④The process program in the CNC numerical control unit will operate test run and tool path simulation etc.
⑤Run the program, complete parts processing through the proper operation of CNC machine tools.
The basic principle of CNC machine tools:
First, write program based on components partem combined with processing technology. Then input the program to numerical control device through the keyboard or other input device (such as perforated paper tape. floppy disks, etc.), the numerical control device decodes, stores and interpolates the program, give the command signal to the servo system of all the coordinates, in order to drive servo motor rotation, hold the relative position of the tool and workpiece and carry out their movement through the transmission, ensure theirs position accuracy through the position detection feedback. At the same time, initiate other necessary supporting actions through the PLC system, such as automatic transmission, the automatic opens and stops of the cooling lubricant, the automatic clamp and release of the workpiece, the automatic change of tools, etc. All of these operations. together with the feed movement, guarantee the automatic processing of parts.

## Slide 6
【Text】
(2)Composition of CNC Machine and the Function of each part
CNC machine tools comprises of six parts: control media, NC system, servo system, feedback devices, assistive devices and machines body, as shown in fig. 1-7.
Fig. 1 -7 Block diagram of the system of CNC machine tools
Control media, also known as the information carrier, is the physical medium between people and computers, reflecting all the information in the NC.
CNC system is the core of the CNC machine tools, which ensure the automatic processing. It mainly consists of input devices, monitors, control system, programmable logic controller (PLC), input and output interfaces and so on.
Monitors are composed by the display and keyboard. Display could be digital LED, CRT, LCD and other forms. It shows the NC program, various parameters, interpolation value, coordinates, fault information, man-machine dialogue programming menu, part graphics, and dynamic cutting tool path.
The main control system consists of CPU, memory, controller and other components. There are two ways of control, computing process control and timing logic control.
Interpolation operation module in the master controller data can carry on the tool path interpolation operation after decoding and coding the input program, and control the displacement of the coordinate axis by comparison to the feedback signals of each axis' position and velocity.
The sequential logic control completes task by programmable logic controller (PLC). It coordinates the requirements of each operation in the machining, determine the detection signals logically, and then control the machine tools to work methodically.

## Slide 7
【Text】
Servo system is the electric transmission link between the numerical control system and machine tool body. It consists of a servo motor, drive control system and position sensing feedback device and other components. It is used to control the servo of feed and spindle.
Feed servo system is the executive part of the teed movement, including the position control unit, speed control unit, servo motor, measuring feedback unit and other parts. It receives various commands of moves from computer to drive the servo motor movement. Servo motors has three types, stepper motors, DC servo molor and AC servo motor. Performance of feed servo system has immediate affects on the machining accuracy and production efficiency of CNC machine tools.
Spindle servo system is the part that transmits torque in cutting machine, generally divided into gear variable speed and electric continuously variable speed. Spindle servo pump is composed of the spindle drive control system, the spindle motor, and spindle mechanical transmission etc.
④ feedback devices include optical pulse encoder, grating position sensor, linear sensor synchronizer and other devices.
⑤Auxiliary devices include automatic tool changer, automatic change pallet table mechanical,；damping and release mechanical, rotary table, hydraulic control systems, lubrication equipment,；cutting fluid devices, chip removal device, overload and protection devices.
⑥ CNC machine tool body is the mechanical structure of ontology entities, composed by the main transmission, table, bed and spindle components. Compared with ordinary machine tools CNC machine tools have had a sweeping change in its overall layout, appearance, transmission, tool system and operating mechanism, and, specifically summarized as follows:

## Slide 8
【Text】
Has the great transmission power, high stiffness, good vibration and small thermal deformation with high performance main drive spindle parts.
Has the short transmission chain, simple mechanism, high driving precision with the good transmission parts, such as the ball screw, synchronous gear belt etc, so as to ensure the transmission accuracy.
Has the perfect tool automatic exchange and management system (especially the CNC machining center).
Generally, has the mechanism of automatic exchange workpiece, clamping and relaxing workpiece in CNC machining centers.
The machine itself has a very high dynamic and static stiffness with some high precision and small friction coefficient components, such as plastic coated guide rails, linear roller guides rail and static guides rail etc.
Totally enclosed cover. As the CNC machine processes in an automatic way, for safety’s sake, the machine's machining parts are totally enclosed with lagging and moving door.

## Slide 9
【Text】
IV.CNC Machining Object
(1)The Advantages and Characteristics of CNC Machining
Processability of complex-surfaced workpiece.
High machining precision, good size consistency.
High production efficiency.
Low labor intensity.
Obvious economic benefits.
Accurate cost calculation and production schedule.
The foundation for CAD/CAM technology and advanced manufacturing.
(2)The Application Range of CNC Machine Tools
The parts produced in much variety and little batch; the parts in new product trial.
The parts with complex geometry.
The parts demanding multi-processing procedures.
The parts demanding expensive process equipment when use general machining.
⑤ High-precision demanding parts
⑥ The parts need repeated modifying in technical design.
⑦ The expensive key parts not allowed scraped.
⑧ The parts require the shortest production cycle.
The application range of CNC machine tools is shown in Fig. 1-8.
The relationship between processing batch of various machine tools and their cost is shown in Fig. 1-9.

## Slide 10
【Text】
V. The Construction of CNC Machines
CNC machine tools are complex assemblies. However, in general, any CNC machine tool consists of the following units:
Computers
Control systems
Drive motors
Tool magazine and changers
(1) Computers
The computer reacts on. As with all computers, the CNC machine computer works on a binary principle using only two characters 1 and 0, for information processing precise time impulses from the circuit. There are two states, a state with voltage, 1, and a state without voltage, 0. Series of ones and zeroes are the only states in which the computer distinguishes a so-called machine language; it is the only language the computer understands. When creating the program, the programmer need not care about the machine language. He or she simply uses a list of codes and keys in the meaningful information. Special built-in software compiles the program into machine language and the machine moves the tool by its servomotors. However, the programmability of the machine is dependent on whether there is a computer in the machine's control. If there is a minicomputer programming, say, a radius (which is a rather simple task), the computer will calculate all the points on the tool path. On the machine without a minicomputer, this may prove to be a tedious task, since the programmer must calculate all the points of intersection on the tool path. Modem CNC machines use 32-bit processors in their computers that allow fast and accurate processing of information.

## Slide 11
【Text】
Control Systems
There are two types of control systems on NC/CNC machines: open loop (fig. 1-10; and closed loop (Fig, 1 -11). the type of control loop used determines the overall accuracy of the machine.
The open-loop control system does not provide positioning feedback to the control unit. The movement pulses are sent out by the control unit and they are received by a special type of servomotor called a stepper motor. The number of pulses that the control unit sends to the stepper motor controls the amount of the rotation of the motor. The stepper motor then proceeds with the next movement command. Since this control system only counts pulses and cannot identify discrepancies in positioning, the machine will continue this inaccuracy until somebody finds the error.
The open-loop control can be used in applications in which there is no change in load conditions, such as the NC drilling machine. The advantage of the open-loop control system is that it is less expensive, since it does not require the additional hardware and electronics needed for positioning feedback. The disadvantage is the difficulty of detecting a positioning error.

## Slide 12
【Text】
In the closed-loop control system, the electronic movement pulses are sent from the control unit to the servomotor, enabling the motor to rotate with each pulse. The movements are detected and counted by a feedback device called a transducer. With each step of movement, a transducer
sends a signal back to the control unit, which compares the current position of the driven axis with the programmed position. When the numbers of pulses sent and received match, the control unit starts sending out pulses for the next movement.
Closed-loop systems are very accurate. Most have an automatic compensation for error, since the feedback device indicates the error and the control unit makes the necessary adjustments to bring the slide back to the position. They use AC, DC or hydraulic servomotors.
(3) Drive Motors
The drive motors control the machine slide movement on NC/CNC equipment. They come in four basic types®:
① Stepper motors；
② DC servomotors；
③ AC servomotors；
④ Hydraulic servomotors.
Stepper motors are used in open-loop control systems, while AC, DC and hydraulic servomotors are used in closed-loop control systems.
(4) Tool magazine and changers
Most of the time, several different cutting tools are used to produce a part. The tools must be replaced quickly for the next machining operation. For this reason, the majority of NC/CNC machine tools are equipped with automatic tool changers, such as magazines on machining centers and turrets on turning centers.

## Slide 13
【Text】
Fig. 1-12 A magazine
They allow tool changing without the intervention of the operator. Typically, an automatic tool changer grips the tool in the spindle, pulls it out, and replaces it with another tool. On most machines with automatic tool changers, the turret or magazine can rotate in either direction, forward or reverse, shown in Fig. 1-12, Fig.1-13.
Fig.1-13 an automatic tool changer
Tool changers may be equipped for either random or sequential selection. In random tool selection. there is no specific pattern of tool selection. On the machining center, when the program calls for the tool, it is automatically indexed into waiting position, where it can be retrieved by the. tool-handing device. On the turning center, the turret automatically rotates, bringing the tool into position.

## Slide 14
【Words and phrases】
numerical control (NC) 数字控制
computer numerical control (CNC) 计算机数字控制
advanced manufacturing technologies 先进制造技术
Massachusetts Institute of Technology (M.I. T.) 麻省理工学院
servo system 伺服系统
measure device 测量装置
impulse n. 脉冲
milling cutter 铣刀
implementation n. 工具，仪器，执行过程
hard-wire n. 硬线连接
two-axis n. 两坐标
versatile adj. 多方面的，多变的，多用途的
advantage n. 优点
disadvantage n. 缺点
perform v. 执行
multiple adj. 多个
simultaneous adj. 联动
conventional adj. 传统的
set up 安装
special profile tools 成形刀具
precision n. 精度
scrap n. 废品
CAD（computer aided design） 计算机辅助设计
CAM（computer aided manufacturing）计算机辅助制造
maintain v. 维护，护养
lathe n. 车床
turning center n. 车削加工中心
milling machine n. 铣床
machining center n. 铣削加工中心
electrical discharge machine (EDM) n. 电火花加工机床
flame cutter n. 线切割机床
grinder n. 磨床
machine center (MC) 加工中心
vertical adj. 立式的，垂直的

## Slide 15
【Words and phrases】
horizontal adj. 水平的，卧式的
automatic tool changer 自动刀具交换机构
tool magazine 刀库
assembly n. 装配，组装件，集合
in general 一般地
consist v. 包括，组成
binary adj. 二进制的
impulse n. 脉冲
sensing n. 传感器
graduate n. 刻度
servomotor n. 伺服电机
tool path 刀具路径
minicomputer n. 微型计算机
tedious adj. 繁琐的
intersection n. 交点
processor n. 处理器
feed back 反馈
discrepancies n. 偏差
transducer n. 传感器
DC (direct current) 直流
AC (alternative current) 交流
open loop 开环
close loop 闭环
control system 控制系统
drive v. , n. 驱动，驾驶
hydraulic servomotors 液压伺服电机，液压马达
automatic tool changers 自动换刀机构
random selection 随机选刀
sequential selection 顺序选刀
stepper motor 步进电机
turret n. 转塔刀架

## Slide 16
【Course practice】
Complex Sentence Analysis
(1) Numerical Control (NC) is any machining process in which the operations are executed automatically in sequences as specified by the program that contains the information for the tool movements.
此句中包含两个定语从句，第一个从句的先行词是machining process，in which引导从句the operations are executed automatically in sequences as specified by the program that contains the information for the tool movements. 在定语从句中that contains the information for the tool movements 作定语从句，修饰the program。
译：数字控制是按照含有机床(刀具)运动信息程序所指定的顺序自动执行操作的加工过程。
(2) When the first Numerically Controlled (NC) machine was controlled by punched tape, and because of that, the NC systems were known as tape-controlled machines.
punched tape-打孔纸带：一种用于存储和传输数据的介质，由纸带上的一系列孔洞表示不同的字符和指令。
译：第一台数控机床的数据是由穿孔纸带控制的，因此数控系统被称为纸带控制机床。
(3)Only the way in which the execution is controlled is different.
此句的主干结构是“the way is different”，“in which the execution is controlled”作为定语从句修饰the way。
译：只是控制执行的方式不同。
(4)Since its introduction, NC technology has found many applications …
此句中 its 指代 NC technology
译：数控技术自发明以来，得到了广泛的应用……
(5)NC machines have many advantages over conventional machines.
over：介词，超过，越过
译：计算机数控机床和传统机床相比具有很多优点。

## Slide 17
【Course practice】
Complex Sentence Analysis
The scrap rate is significantly reduced because of the precision of the CNC machine and lesser operator impact;
because of ：因为，由于……的原因
译：由于计算机数控机床的精度高，受操作者影响小，废品率明显降低。
It is easy to incorporate part design changes when CAD/CAM systems are used;
此句中it作形式主语，真正的主语是“to incorporate part design changes”。
译：采用 CAD/CAM 系统后，对零部件装配设计的修改就变得很容易。
However, the programmability of the machine is dependent on whether there is a computer in the machine’s control.
此句中从句“whether there is a computer in the machine’s control”作介词 on 的宾语从句。
译：然而，机床程序的可编程性是依据于机床控制系统中是否有计算机。
The number of pulses that the control sends to the stepper motor controls the amount of the rotation of the motor.
此句中“that the control sends to the stepper motor”为定语从句，修饰“The number of pulses”。
译：控制单元发送给步进电机的脉冲数控制电机的旋转角度。
They come in four basic types:
come in：归纳起来
译：它们有四种基本类型: