## Slide 1: 机电工程专业英语
1.3 NC PROGRAMMING
数控编程

## Slide 2
【Text】
I.Coordinate System for NC Machines
In a NC system, each axis of motion is equipped with a separate driving source that replaces the hand wheel of the conventional machine. The driving source can be a DC motor, a stepping motor, or a hydraulic actuator. The source selected is determined mainly based on the precision requirements of the machine.
The relative movement between tools and work-pieces is achieved by the motion of the machine tool slides. The three main axes of motion are referred to as the X, Y, and Z-axes. The Z-axis is perpendicular to both the X and Y-axes in order to create a right-hand coordinate system (Fig.1-1). A positive motion in the direction moves the cutting tool away from the work-piece. This is detailed as follows.
1.Z-AXIS
①On a work-piece-rotating machine, such as a lathe, the Z-axis is parallel to the spindle, and the positive motion moves the tool away from the work-piece (Fig. 1-2).
Fig.1-1 a right-hand coorinate system
Fig. 1-2 Coordinate system for a NC lathe

## Slide 3
【Text】
②On a tool-rotating machine, such as a milling or boring machine, the Z-axis is perpendicular to the tool set, and the positive motion moves the tool away from the work-piece (Fig.1-3 and Fig.1-4).
③On other machines, such as a press, a planning machine, or a shearing machine, the Z-axis is perpendicular to the tool set, and the positive motion increases the distance between the tool and the work-piece.
2.X-AXIS
①On a lathe, the X-axis is the direction of tool movement, and positive motion moves the tool away from the work-piece.
②On a horizontal milling machine, the X-axis is parallel to the table.
③On a vertical milling machine, the positive X-axis points to the right when the programmer is facing the machine.
3.Y-AXIS
The Y-axis is the axis left in a standard Cartesian coordinate system.

## Slide 4
【Text】
II.The Control Functions of NC Machine
1.The Control Functions of NC Machine are Summarized as What Follows
①Preparatory functions: the words specify which units, which interpolator, absolute or incremental programming, which circular interpolation plane, cutter compensation, and so on.
②Coordinates: coordinates define axes (including rotational).
③Machining parameters: machining parameters specify feed and speed.
④Tool control: tool control specifies tool diameter, next tool number, tool change, and so on.
⑤Cycle functions: cycle functions specify drill cycle, ream cycle, born cycle, mill cycle, and clearance plane.
⑥Coolant control: coolant control specifies the coolant condition, that is, coolant on/off, flood, and mist.
⑦Miscellaneous control: miscellaneous control specifies all other control specifics, that is, spindle on/off, tape rewind, spindle rotation direction, pallet change, clamps control, and so on.
⑧Interpolators: include linear, circular interpolation, circle center, and so on.
2. These Control Functions are Programmed through Program Words (codes)
(1) G-code
The G-code is also called preparatory code/word; it is used to prepare the MCU for control functions. Modal functions are those that do not change after they have been specified once, such as unit selection. Non-modal functions are active in the block where they are specified. For example, circular interpolation is a non-modal function. Some commonly used G-codes arc listed in Table 1-1

## Slide 5
【Text】
(2) F-Code
The F-Code specifies the feed speed of the tool motion. It is the relative speed between the cutting tool and the work-piece. It is typically specified in mm/min; for example, F100 means the feed speed is 100 mm/min. Feed speed can be changed frequently in a program, as needed. When a F-code is present in a block, it takes effect immediately.
(3) S-Code
The S-code is the cutting-speed code. Cutting speed is the specification of the relative surface speed of the cutting edge with respect to the work-piece. It is the result of the tool (or work-piece in turning) rotation. Therefore, it is programmed in rpm(r/min). The S-code is specified before the spindle is turned on. The S-code does not turn on the spindle. The spindle is turned on by an M-code. To specify an 800-rpm spindle speed, the NC program block is:
N0020 S800 M03.

## Slide 6
【Text】
(4) T-Code
The T-code is used to specify the tool number. It is used only when an automatic tool changer is present. It specifies the slot number on the tool magazine in which the next tool is located. Actual tool change does not occur until a tool change M-code is specified.
(5)R-Code
In a drill-cycle, the R-code is used for cycle parameter. When a drill cycle is specified, one must give a clearance height (R plane) (Fig.1-5). The R-code is used to specify this clearance height.
In Fig.4-5, the drill cycle consists of five operations:
Rapid location;
Rapid down to the R plane;
Feed to the Z point, the bottom of the hole;
Operation at the bottom of the hole, for example, dwelling;
⑤ Rapid back or feed to either the R plane or the initial height.
Fig.1-5 Drill cycle operation
The cycle may be programmed in one block.
N0010G81 X 1.000 Y2.000 Z0.000 R1.300

## Slide 7
【Text】
M-Code
The M-code is called the miscellaneous word and is used to control miscellaneous functions of the machine. Such functions (Table 1-2) include turning the spindle on/off starting/stopping the machine, turning on/off the coolant, changing the tool, and rewinding the program tape.
III. NC Part Programming
In manual part programming, the machining instructions are recorded on a document, called a part-program manuscript (Table 1-3) by the part programmer. The manuscript is essentially an ordered list of program blocks.
Because a part program records a sequence of tool motions and operations to produce the final part geometry, one must prepare a process plan with setups and fixtures before writing the program. The work-piece location and orientation, features (holes, slots, pockets) to be machined, tools and cutting parameters used need to be determined. We will use an example to illustrate how a part is programmed.

## Slide 8
【Text】
Example:
The part drawing is shown in Fig.1-7. The work-piece material is low-carbon steel. We will use TH5632C machining center for the process. The process plan for the part is as follows.
Set the center of the part as the machine zero point (floating-zero programming).
Clamp the work-piece in a vise.
The cutler to mill the profile with a 15mm end mill is made of carbide. From the Machinability Date Handbook, the recommended feed is 100mm/min and the recommended cutting speed is 800 rpm. Fig.1-8 shows the setup, and cutter path.
④During the milling operation, the cutter moves from A1 to B1, B2, B3, B4, B5, B6, B7, B8 and then to B1.

## Slide 9
【Text】
Combining the information from the process plan and the cutter-location date, a part program can be written. The program for the example part is shown as follows:
We will use TH5632C machining center for the process.

## Slide 10
【Words and phrases】
I
coordinate System 坐标系
stepping motor 步进电机
precision n . 精度
slide n . 滑台
parallel v . 平行
spindle n . 主轴
positive adj . 正方向，正的
perpendicular adj . 垂直的
table n . 工作台
Cartesian coordinate system 笛卡尔坐标系
II
control functions 控制功能
preparatory functions 准备功能
interpolation n . 插补
circular interpolation plane 圆弧插补平面
absolute adj. 绝对的
incremental adj. 增量的
cutter compensation 刀具补偿
parameter n . 参数
cycle function 循环功能
fixed cycle function 固定循环功能
coolant control 冷却控制
mist n . 雾状
pallet n . 托盘
miscellaneous control 辅助控制
location n . 定位
MCU 中央控制单元
G-code G代码，准备功能指令
M-code M代码，辅助功能指令
S-code S代码，主轴转速指令
T-code T代码，刀具指令
F-code F代码，进给速度指令
R-code R代码
CW clock wise 顺时针方向
CCW counter clock wise 逆时针方向
III
manual part programming 零件手工编程
manuscript n. 单据，清单
block n . 程序段
sequence n . 次序
geometry n . 几何学
illustrate v . 说明
vise n . 虎钳

## Slide 11
【Course practice】
Complex Sentence Analysis
(1) In a NC system, each axis of motion is equipped with a separate driving source that replaces the hand wheel of the conventional machine.
此句中“that replaces the hand wheel of the conventional machine”作定语从句修饰“a separate driving source”，单独的驱动源。
译：在一个数控系统中，每个运动轴都配备了一个单独的驱动源，以此来代替传统机床上的手轮。
(2) On a work-piece-rotating machine, such as a lathe, the Z-axis is parallel to the spindle, and the positive motion moves the tool away from the work-piece.
此句中，“a work-piece-rotating machine”实际是指机床的主运动是由工件旋转而形成的，下一段中的“a tool-rotating machine”指机床的主运动是由刀具旋转而形成的。
译：在工件旋转的机床上，如车床，Z轴是平行于主轴的，其正方向是刀具远离工件的方向。
On a vertical milling machine, the positive X-axis points to the right when the programmer is facing the machine.
译：在立式铣床上，正X轴方向是当程序员面向机床时，指向右边的方向。

## Slide 12
【Course practice】
Complex Sentence Analysis
The words specify which units, which interpolator, absolute or incremental programming, which circular interpolation plane, cutter compensation, and so on.
此句中“which units, which interpolator, absolute or incremental programming, which circular interpolation plane, cutter compensation, and so on. ”为连续并列宾语。
译：指明程序段的单位，插补方式，绝对或增量编程，什么样的圆弧插补面，刀具补偿等等。
Modal functions are those that do not change after they have been specified once, such as unit selection.
此句中 “that do not change after they have been specified once, such as unit selection.” 为定语从句修饰先行词those。
译：模态功能是指一经代码指定后不会改变其功能，如单位选择。
The T-code is used to specify the tool number. It is used only when an automatic tool changer is present.
T 代码即选刀指令，真正的换刀动作要等到M06指令出现时才发生。
译：T 代码用来指明刀号，它只用于配有自动换刀装置的情况下（它指明了刀库中下一把刀所在的位置号）。