## Slide 1: 机电工程专业英语
1.2 ENGINEERING DRAWING
工程制图

## Slide 2
【Text】
Engineering drawing is a professional basic subject, based on the projection theory of pictorial geometry, with ruler, compass and drawing board as tools, and blackboard, wood model and wall chart as media, with a history of more than 200 years. Mechanical Engineering Drawing is an introductory course that reflects the characteristics of engineering, and it is also one of the basic courses that engineering students must learn. It plays an important role in cultivating students' spatial imagination and ideation ability as the basis of creative thinking and promoting the industrialization process.
Coordinate System
In engineering drawing, the coordinate system is very important. The basic of all input AutoCAD is the Cartesian coordinate system, and the various input (absolute or relative) rely on this system. In addition, AutoCAD has two internal coordinate systems to help you keep track of where you are in a drawing: the World Coordinate System (WCS) and Coordinate system.
The fixed Cartesian coordinate system locates all points on an AutoCAD drawing by defining a series of positive and negative axes to locate positions in space. Fig.1-1 (a) illustrates the axis for two-dimension (2D) drafting. There is a permanent origin point (0,0) which is referenced, an x axis running horizontally in a positive and negative direction from the origin, and a y axis traveling perpendicularly in a vertical direction. When a point is located, it is based on the origin point unless you are working in the three dimension, in which case you will have a third axis, called the z axis (Fig.1-1 (b)).

## Slide 3
Types of Views
Many types of views are used to express the design ideas in engineering design in the area of Engineering drawing.
(1) Projection view An orthographic projection of an object as seen from the front, top, right side, etc, as illustrated in the Fig.1-2. Fig. 1-2 (a) is the object, and Fig. 1-2 (b) is the orthographic projection of the object.
【Text】
(a)two dimension (b)three dimension
Fig.1-1 the coordinate system

## Slide 4
【Text】
(a)an object (b)orthographic projection of an object
Fig.1-2 an orthographic projection of an object
(2) Auxiliary view Any view created by projecting 90°to an inclined surface, datum plane, or along an axis.
(3) General view Any view which is oriented by the user and is not dependent on any other view for its orientation.
(4) Detailed view Any view which is derived by taking a portion of an existing view and scaling it for the purpose of dimensioning and clarification. The following Fig.1-3 is a typical example of detailed view. There are two detailed view in the Fig.1-3 that is Ⅰand Ⅱ.
Fig.1-3 detailed view
(5) Revolved A planar, area cross-section was revolved 90°about the cutting plane line and offset alone, its length.
(6) Full View A view which shows the entire model.
(7) Half View A view which shows only the portion of the model on one side of a datum plane.

## Slide 5
【Text】
(8) Broken View Used on large objects to remove a section between two points and move the remaining section close together.
(9) Section View A view which displays a cross-section for a particular view, as the following Fig.1-4 shown.
Fig.1-4 section view
(10) Exploded Drawing The exploded drawing is a type of pictorial drawing designed to show several parts in their proper location prior to assembly. Although the exploded view is not used as the working drawing for the machinist, it has an important place in mechanical technology. Exploded views appear extensively in manuals and handbooks that are used for repair and assembly of machines and other mechanisms.
(11) Partial view When a symmetrical objects is drafted, two views are sufficient to represent it (typically, one view is omitted). A partial view can be used to substitute one of the two views. Sectional and auxiliary views are also commonly used to present part detail①. Sectional views are extremely useful in displaying the detailed design of a complicated internal configuration. If the section is symmetrical around a centerline, only the upper half needs to be shown.

## Slide 6
【Text】
The lower half is typically shown only in outline. Casting designer often employ sectional views to explode detail. When a major surface is inclined to three projection planes, only a distorted picture can be seen. An auxiliary plane that is parallel to the major surface can be used to display an undistorted view.
Fits
The fit between two mating parts is the relationship which results from the clearance or interference obtained. There are three classes of fit, namely, clearance, transition and interference. These conditions are shown in the following Fig. 1-5.
(a)clearance fit(note that the shaft is always smaller than the hole)
(b)interference fit (note that the shaft is always larger than the hole)
(c)transition fit(note that the limits are such that the condition may be of clearance of interference fit)
Fig.1-5 classes of fit between a hole and a shaft

## Slide 7
【Text】
The following Fig. 1-6 is a typical example of the dimensioning of fit code in the assembly drawing.
Fig. 1-6 A typical example of the dimensioning of fit code in the assembly drawing
Interchangeability
An interchangeable part is one which can be substituted for a similar part manufactured to the same drawing①. The interchangeability of component parts is based upon these two functions.
(1) It is necessary for the relevant mating parts to be designed incorporating limits of size.
(2) The parts must be manufactured within the specified limits.
2. Limits of size
In deciding the limits necessary for a particular dimension, there are three consideration functional importance, interchangeability and economics.
The first necessitates a knowledge of what the component is required to do, the second its replacement in the event of failure, and the third the avoidance of unnecessary time and money being spent in production. The decision as to the degree of tolerance that can be utilized calls for discretion in the compromise between accuracy and economy. In order to assist the designer in his choice of limits and fits and to encourage uniformity throughout industry (home and abroad), a number of limit-and-fit systems have been published.

## Slide 8
【Words and phrases】

## Slide 9
【Course practice】
Complex Sentence Analysis
(1) The basic of all input AutoCAD is the Cartesian coordinate system, and the various input (absolute or relative) rely on this system.
The basic of … 在此的意思是“…的基础”，rely on的意思是“依赖，依靠”
译：笛卡尔坐标系是输入AutoCAD 的全部基础，各种输入方法（如绝对坐标、相对坐标）都依赖于这个系统。
(2) When a point is located, it is based on the origin point unless you are working in the three dimension, in which case you will have a third axis, called the z axis.
Unless 引导让步状语从句，in which case 引导的从句在此做定语修饰 dimension，called the z axis 在此作为 third axis的后置定语。
译：根据原点（0,0）标记其它任意一个点，但是在三维空间中绘图时，应该具有称为z轴的第三根轴。
(3) Sectional and auxiliary views are also commonly used to present part detail.
To present part detail 作目的状语。
译：剖面图和辅助视图同样经常被用来表示零件图。
(4) An interchangeable part is one which can be substituted for a similar part manufactured to the same drawing.
Interchangeable 在此为动词interchange的形容词形式，翻译为“可以互换的，可交换的”。
substitute for 在此意思是“代替，替换，取代”。
译：可互换性的零件是一种能由同一图纸加工出来的相似零件所代替的零件。
(5) In deciding the limits necessary for a particular dimension, there are three consideration functional importance, interchangeability and economics.
译：对一个具体尺寸给定公差带时，有三个需要考虑的方面：功能重要性、互换性和经济性。