## Slide 1: 机电工程专业英语
3.2 VEHICLE RADIATOR
汽车散热器

## Slide 2
【Text】
Introduction of typical car radiator
The vehicle radiator is an important heat dissipation device in vehicles such as cars and motorcycles, which is used to dissipate the heat generated by the engine and maintain the normal working temperature of the engine. With the continuous development of technology, new radiators such as assembled radiators, nitrogen shielded welding radiators and vacuum brazed radiators are gradually applied to the automobile and motorcycle manufacturing industry.
Vehicle radiator types and manufacturing companies
1. Assembled radiator
An assembled radiator is a radiator that is manufactured separately from the radiator and the water tank, and finally assembled. There are Shanghai Baosteel Group, Guangzhou Automobile Group, Beijing Automobile Group and so on. Foreign manufacturing companies have Germany Bosch, Delphi, Japan Denso and so on.
2. Nitrogen protected welding radiator
Nitrogen shielded welding radiator is a kind of radiator manufactured by nitrogen shielded welding technology. Domestic manufacturing companies are Shanghai Bao steel Group, Guangzhou Automobile Group, Beijing Automobile Group and so on. Foreign manufacturing companies have Germany Bosch, Delphi, Japan Denso and so on.
3. Vacuum brazing radiator
Vacuum brazing radiator is a kind of radiator made by vacuum brazing technology. Domestic manufacturing companies are Shanghai Bao steel Group, Guangzhou Automobile Group, Beijing Automobile Group and so on. Foreign manufacturing companies have Germany Bosch, Delphi, Japan Denso and so on.

## Slide 3
【Text】
The structure and working principle of the radiator
1. Assembled radiator
The assembled radiator consists of a heat sink and a water tank. The heat sink is usually made of aluminum alloy and has good thermal conductivity. The water tank is used to store the coolant. The working principle is that through the circulation of coolant, the heat generated by the engine is transferred to the heat sink, and then the amount is dissipated into the air through the blowing of the fan. The main application scenario is the engine cooling system of vehicles such as cars and motorcycles.
Fig. 1-1 Aluminum assembled water radiator

## Slide 4
【Text】
Fig.1-2 Profile of water radiator
2. Nitrogen protected welding radiator
Nitrogen shielded welding radiator is made of nitrogen shielded welding technology, which has the advantages of high welding strength and good corrosion resistance. Its structure and working principle are similar to the assembly radiator, and the main application scenario is also the engine cooling system of vehicles such as automobiles and motorcycles.
3. Vacuum brazing radiator
Vacuum brazing radiator is made of vacuum brazing technology, which has the advantages of high welding strength and good sealing. Its structure and working principle are similar to the assembly radiator, and the main application scenario is also the engine cooling system of vehicles such as automobiles and motorcycles. The structure of the aluminum brazing water radiator is shown in Figure 1-3.

## Slide 5
【Text】
Fig.1-3. Aluminum brazed water radiator
The significance of the development of radiator industry to China's automobile/motorcycle manufacturing industry
As new types of radiators, prefabricated radiators, nitrogen shielded welding radiators and vacuum brazed radiators are of great significance to automobile/motorcycle manufacturing industry in China.
First of all, these new radiators use advanced manufacturing technology with higher welding strength and tightness, which can improve the service life and reliability of the radiator, reduce the failure rate, and improve the overall performance of the car/motorcycle.
Secondly, the structure and working principle of these radiators are more advanced than traditional radiators, which can more effectively distribute the heat generated by the engine, improve the cooling effect of the engine, ensure the normal working temperature of the engine, and extend the service life of the engine.

## Slide 6
【Text】
Finally, the application of these new radiators has promoted the technological upgrading and industrial upgrading of China's automobile/motorcycle manufacturing industry, improved the competitiveness of China's automobile/motorcycle manufacturing industry, and promoted the development of the industry.
Fig. 1-4 Development stage of vehicle radiator
In summary, as a new type of radiator, assembled radiator, nitrogen shielded welding radiator and vacuum brazed radiator are produced by a number of manufacturing companies at home and abroad, and have important application scenarios and significance in the automobile/motorcycle manufacturing industry. The application of these radiators has promoted the technological progress and industrial upgrading of China's automobile/motorcycle manufacturing industry, improved the performance and reliability of the product, and promoted the development of the industry.

## Slide 7
【Words and phrases】
vehicle n .交通工具，车辆
radiator n. 暖气片，散热器；（暖气片型）燃油炉，电热器
dissipation n. 浪费；消散
motorcycle n. 摩托车
nitrogen n. [化学] 氮
shielded welding 保护焊
nitrogen shielded welding radiator 氮保护焊散热器
vacuum n. 真空，真空容器
brazed adj. 钎焊的；铜焊的;v.用铜焊接（braze 的过去式）
water tank 水箱
Vacuum brazing radiator 真空钎焊散热器
Domestic adj. （domestic）家庭的；国内的；家用的
heat sink 散热器/热沉
aluminum n. 铝
thermal conductivity 热导率
coolant n. 冷却剂
circulation n .发行量，销售量；血液循环；流传，流通
Nitrogen protected welding radiator 氮保护焊接散热器
corrosion n. 腐蚀，侵蚀；腐蚀产生的物质
scenario n. 设想，可能发生的情况 ；（电影、戏剧等的）剧情梗概；（艺术或文学作品中的）场景
the main application scenario 主要应用场景
sealing n. 猎捕海豹；封闭；密封v.系紧，封牢
prefabricated radiator 预制散热器

## Slide 8
【Course practice】
Complex Sentence Analysis
(1) then the amount of heat is dissipated into the air through the blowing of the fan.
…be dissipated into…消散为……
译：然后通过风扇的吹风将热量散发到空气中。
(2) The structure and working principle of these radiators are more advanced than traditional radiators
…more advanced than…比……先进
译：这些散热器的结构和工作原理比传统散热器更先进。