## Slide 1
1.6.2.2平衡轴
1.6.2防止发动机扭转振动和摇摆的措施
平衡轴用于平衡活塞和连杆惯性力产生的力矩。平衡轴有两个彼此错开1800布置的平衡重块。它由曲轴通过一个链条驱动，转动方向与曲轴相反。发动机力矩通过相反的转动方向和平衡重块来平衡。运行时不发生摇摆。

## Slide 2: 平衡轴驱动
拧入式张紧器
张紧轨
齿轮
没轨
齿链
齿轮传动
平衡轴
导轨
Notes: Balancing shafts drive at twice the engine speed.
Contra-rotation achieved at the gear drive stage.
2nd order mass inertia balanced.
2nd order moments of inertia balanced by height offset arrangement in crankcase
Advantages of bearings in crankcase:
Higher crankcase stiffness,
No oil foaming in the sump.

## Slide 3: 平衡轴在曲轴箱上的布置
机油回油
保护管 (侧视)
Contents
Notes: The protection pipe prevents adulteration of the return oil flow by the rotating balancing shaft.
The balancing shafts each have three bearings.
The bearing points are supplied with oil by the engine lubrication system.

## Slide 4
大众2.0T FSI发动机平衡轴
采用分体驱动链轮
●驱动齿轮与不平衡质量分离有利于提高平衡等级
●采用较宽齿轮的机油泵
●机油控制的机油压力调节阀位于平衡轴壳体上
● 强度优化的压铸壳体
● 轴承直接位于铝合金壳体上